## Slide 1: X-Ray Image-Based Navigation for Hip Osteotomy
Seminar Article Presentation
Teammate: |  | Jesse Hamilton
Mentors: |  | Dr. Mehran Armand, Dr. Yoshito Otake, Ryan Murphy
Course: |  | Computer Integrated Surgery II (EN.600.646)
Michael Van Maele
Group #3
24 April 2012

## Slide 2: Article Choice 3D/3D Registration
Notes: The article I chose is a recent journal publication treating the problem of 3D/3D registration, in other words, the problem of determining the optimal transformation between two sets of 3D points.

## Slide 3: Article Choice
Notes: The title of the article is [title], and the main author is Radu Horaud, whose group works in Montbonnot Saint-Martin, France at the INRIA Grenoble
Rhône-Alpes with contributions by Jian Zhang from the University of Hong Kong. Now, at least one component of this title should resonate with you, and that is the phrase ‘rigid registration.’

## Slide 4
Article Choice
Material covered in EN.600.646 (ICP).
Notes: As a reminder, rigid registration consists of determining the optimal rotation and translation aligning two sets of points. Here, the left hand side denotes the transformation of some 3D point X according to a set of parameters big theta, which are simply R and t for rigid registration. Recall that we studied the Iterative Closest Point algorithm in substantial detail. You won’t need to look at your Homework 5 code, but just recall that the ICP algorithm is generally deterministic, not probabilistic. So why did I just say probabilistic? It has to do with the second line in the title, Expectation Conditional Maximization.

## Slide 5
Article Choice
?
What is ECM?
Notes: Has anyone here ever heard of the ECM algorithm? Today, understanding just how the ECM algorithm can help to solve point registration problems will be our quest. But before we get into that, a little more on why I selected this article by Horaud et al.

## Slide 6: Article Choice
Relationship to X-ray navigation project.
  The 2D/3D registration algorithm implemented in our work * and the approach proffered by Horaud et al. exhibit the following interesting parallels:
    Uses maximum-likelihood estimation (MLE) framework.
    Solved via the ECM algorithm.
    Uses a Gaussian Mixture Model (GMM).
*Kang X, Taylor RH, Armand M, Otake Y, Yau WP, Cheung PYS, Hu Y. Correspondenceless 3D-2D registration based on expectation conditional maximization. Proc SPIE 2011 March 3, 2011;7964(1):79642Z.
Notes: Other than being very interesting work, I chose it based on the marked similarities it shares with the 2D/3D registration algorithm that our X-ray navigation system uses. That algorithm was developed by Ben Kang, you can learn more about it by looking up in our reading list. However, the main ideas shared between both Kang’s algorithm and Horaud et al.’s procedure are fourfold.
[Recite them.] Say GMM will be the most frightening topic of today’s discussion.
We will get into the nitty gritty of these similarities along the way because, honestly, to do so will essentially tell the whole story of the article I’m presenting.

## Slide 7: Technical Summary
Problem formulation.
  How does MLE work?
  MLE estimates the parameters of the presumed data distribution given a set of observed data, Y.
vs.
GAUSSIAN DISTRIBUTION
ESTIMATED PARAMETERS OF
GAUSSIAN DISTRIBUTION
MLE
Y
Notes: So we assume that the statistical distribution of the displacements of the elephants is Gaussian, or bell-shaped. Here, stands for elephant displacement, and stands for the probability of observing an elephant with that displacement. The peak of this curve is the most likely observed elephant displacement, or , the mean displacement. The variance is and it characterizes the degree to which the bell curve is peaked around that mean displacement. That is, a large variance would indicate that the elephants are scattered at widely variable distances around the watering hole, whereas a small variance would indicate that they are grouped mostly at a single, uniform, fixed distance from it.
What MLE does is estimate the optimal parameters of this Gaussian distribution of the true elephant displacements X, given the data that we observed, Y.
So we assume that the statistical distribution of the displacements of the elephants is Gaussian, or bell-shaped. Here, 𝑥 stands for elephant displacement, and 𝐹(𝑥) stands for the probability of observing an elephant with that displacement. The peak of this curve is the most likely observed elephant displacement, or 𝜇, the mean displacement. The variance is 𝜎^2, and it characterizes the degree to which the bell curve is peaked around that mean displacement. That is, a large variance would indicate that the elephants are scattered at widely variable distances around the watering hole, whereas a small variance would indicate that they are grouped mostly at a single, uniform, fixed distance from it.
What MLE does is estimate the optimal parameters of this Gaussian distribution of the true elephant displacements X, given the data that we observed, Y.

## Slide 8: Technical Summary
Problem formulation.
  How do we jump from average heights to point registration?
  Problem: We are missing the point correspondences between the two sets of points!
  Solution:
    Account for missing data by introducing categorical random variables.
    “observed point corresponds to model point .”
    is an inlier.
    is an outlier.

## Slide 9: Technical Summary
Problem formulation.
  How do we jump from average heights to point registration?
  Problem: We are missing the point correspondences between the two sets of points!
  Solution:
    Account for missing data by introducing categorical random variables.
    “observed point corresponds to model point .”
    is an inlier.
    is an outlier.
RANDOM VARIABLES

## Slide 10: Technical Summary
Gaussian Mixture Model (GMM).
model point
data point
“Coordinates of after it has been rotated by and translated by .”
Notes: We’re hoping that after we transform the model point X, it will land smack dab on the data point Y. Well…

## Slide 11: Technical Summary
Gaussian Mixture Model (GMM).
model point
data point
Notes: We’re hoping that after we transform the model point X, it will land smack dab on the data point Y. Well…

## Slide 12: Technical Summary
Gaussian Mixture Model (GMM).
data point
transformed model point
Wrong.
Notes: It looks like our initial guess wasn’t correct.

## Slide 13: Technical Summary
Gaussian Mixture Model (GMM).
data point
transformed model point
Notes: It looks like our initial guess wasn’t correct.

## Slide 14: Technical Summary
Gaussian Mixture Model (GMM).
data point
transformed model point
Mean: | 
Covariance: | 
Mean: | 
Covariance: | 
Notes: This is where Gaussian Mixture Models come to the rescue. We assume that the transformed model point is centered on the mean of a Gaussian distribution. This visualization is a little wrong because it’s actually a 3D distribution, not 1D, but it is easier to look at this diagram.
Next, we assumed that the observed data point is a random variable drawn from this distribution. The probability that this is actually the case is calculable.

## Slide 15: Technical Summary
Gaussian Mixture Model (GMM).
data point
transformed model point
Mean: | 
Covariance: | 
Mean: | 
Covariance: | 
ECM will use this probability to estimate the Gaussian density parameters which maximize the probability of seeing this data point.
Notes: This is where Gaussian Mixture Models come to the rescue. We assume that the transformed model point is centered on the mean of a Gaussian distribution. This visualization is a little wrong because it’s actually a 3D distribution, not 1D, but it is easier to look at this diagram.
Next, we assumed that the observed data point is a random variable drawn from this distribution. The probability that this is actually the case is calculable.

## Slide 16: Technical Summary
Gaussian Mixture Model (GMM).
  Assume each model point is associated with a Gaussian density, parameterized by its own mean and covariance .
  Assume each data point was generated by one of these Gaussian densities.
  Make data-to-model point matches by checking which Gaussian density was most likely to have emitted each data point: .
Notes: This is where Gaussian Mixture Models come to the rescue. We assume that the transformed model point is centered on the mean of a Gaussian distribution. This visualization is a little wrong because it’s actually a 3D distribution, not 1D, but it is easier to look at this diagram.
Next, we assumed that the observed data point is a random variable drawn from this distribution. The probability that this is actually the case is calculable.

## Slide 17: Technical Summary
Gaussian Mixture Model (GMM).
  That is, find the means and covariances for each Gaussian density which maximize the expected likelihood of seeing the observed data, !
Notes: This is where Gaussian Mixture Models come to the rescue. We assume that the transformed model point is centered on the mean of a Gaussian distribution. This visualization is a little wrong because it’s actually a 3D distribution, not 1D, but it is easier to look at this diagram.
Next, we assumed that the observed data point is a random variable drawn from this distribution. The probability that this is actually the case is calculable.

## Slide 18: Technical Summary
ECM Algorithm.
  There is a function which is maximized by the optimal parameters .
  is called the expected complete-data log-likelihood conditioned by the observed data.
expected complete-data log-likelihood
conditioned by the observed data
The parameters which lead to a local maximum of this function will also maximize the log-likelihood of our observed data!
Dempster AP, Laird NM, Rubin DB. Maximum-Likelihood Estimation from Incomplete Data via the EM Algorithm (with Discussion). J. Royal Statistical Soc., Series B, vol. 39, pp. 1-38, 1977.
Notes: Every problem arises from wanting something we can’t have. In this case, what we want are the rotation R and translation t which align one set of 3D points to another set of 3D points. But more than that, we want the optimal R and t. To get that, we can cast the problem into a probabilistic framework, and use a technique named Maximum Likelihood Estimation.
So what do our desired optimal parameters have to do with this method called MLE? What MLE does is assume that a function L, called the observed-data likelihood, which

## Slide 19: Technical Summary
  ECM Algorithm
    Initialize parameters:
    E-step: Compute posterior probabilities given the current values of , , and . Call these .
    CM-steps: Maximize with respect to:
      The registration parameters , conditional on the current covariance matrices.
      The covariance matrices , conditional on the new registration parameters.
    Check for convergence.
,
,
large.

## Slide 20: Technical Summary
  ECM Algorithm
    Initialize parameters:
    E-step: Compute posterior probabilities given the current values of , , and . Call these .
    CM-steps: Maximize with respect to:
      The registration parameters , conditional on the current covariance matrices.
      The covariance matrices , conditional on the new registration parameters.
    Check for convergence.
,
,
large.

## Slide 21: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
expected complete-data log-likelihood
conditioned by the observed data

## Slide 22: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
expected complete-data log-likelihood
conditioned by the observed data
How do we obtain ?

## Slide 23: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:

## Slide 24: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:

## Slide 25: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:
Probability that corresponds to given that was drawn from the Gaussian density centered at

## Slide 26: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:
Likelihood of observation ,
given its assignment to model point .
Probability that corresponds to given that was drawn from the Gaussian density centered at

## Slide 27: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:
Prior probability that observation
belongs to model point .
Likelihood of observation ,
given its assignment to model point .
Probability that corresponds to given that was drawn from the Gaussian density centered at

## Slide 28: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:
Marginal distribution of observation
Likelihood of observation ,
given its assignment to model point .
Prior probability that observation
belongs to model point .
Probability that corresponds to given that was drawn from the Gaussian density centered at

## Slide 29: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:

## Slide 30: Technical Summary
  ECM Algorithm: E-Step
  Compute posterior probabilities given the current values of , , and . Call these .
  Bayes’ Rule:
Mahalanobis distance (want small!).

## Slide 31: Technical Summary
  ECM Algorithm
    Initialize parameters:
    E-step: Compute posterior probabilities given the current values of , , and . Call these .
    CM-steps: Maximize with respect to:
      The registration parameters , conditional on the current covariance matrices.
      The covariance matrices , conditional on the new registration parameters.
    Check for convergence.
,
,
large.

## Slide 32: Technical Summary
  ECM Algorithm: CM-Step A
  Maximize ℰ(𝚿│𝒴,𝒵) with respect to the registration parameters 𝚯≔{𝐑,𝒕}, conditional on the current covariance matrices.
expected complete-data log-likelihood
conditioned by the observed data

## Slide 33: Technical Summary
  ECM Algorithm: CM-Step A
  Maximize ℰ(𝚿│𝒴,𝒵) with respect to the registration parameters 𝚯≔{𝐑,𝒕}, conditional on the current covariance matrices.
maximum-likelihood estimator

## Slide 34: Technical Summary
  ECM Algorithm: CM-Step A

## Slide 35: Technical Summary
  ECM Algorithm: CM-Step A
stands for current estimation,
stands for new estimation.

## Slide 36: Technical Summary
  ECM Algorithm: CM-Step A
stands for current estimation,
stands for new estimation.
“Return the which minimizes this expression.”

## Slide 37: Technical Summary
  ECM Algorithm: CM-Step A
stands for current estimation,
stands for new estimation.
“Return the which minimizes this expression.”
Constant term removed.

## Slide 38: Technical Summary
  ECM Algorithm: CM-Step A
“Simplification.”

## Slide 39: Technical Summary
  ECM Algorithm: CM-Step A

## Slide 40: Technical Summary
  ECM Algorithm: CM-Step A
Expansion of the transformation for the rigid case.

## Slide 41: Technical Summary
  ECM Algorithm: CM-Step A
Expansion of the transformation for the rigid case.

## Slide 42: Technical Summary
  ECM Algorithm: CM-Step A
Expansion of the transformation for the rigid case.

## Slide 43: Technical Summary
  ECM Algorithm: CM-Step A
MLE for updated parameters

## Slide 44: Technical Summary
  ECM Algorithm: CM-Step A
MLE for updated parameters

## Slide 45: Technical Summary
sub. into
  ECM Algorithm: CM-Step A
solve for
Too large for this slide.

## Slide 46: Technical Summary
  ECM Algorithm: CM-Step B
solve for

## Slide 47: Technical Summary
  ECM Algorithm: CM-Step B
solve for
Expand and simplify.
Mahalanobis distance.

## Slide 48: Technical Summary
  ECM Algorithm
    Initialize parameters:
    E-step: Compute posterior probabilities given the current values of , , and . Call these .
    CM-steps: Maximize with respect to:
      The registration parameters , conditional on the current covariance matrices.
      The covariance matrices , conditional on the new registration parameters.
    Check for convergence.
,
,
large.

## Slide 49: Technical Summary
  ECMPR-Rigid Algorithm
Initialization
Compute
,
Compute and
Estimate
Estimate
Estimate
Convergence?
Classification
Yes
No
Workflow
Assignment

## Slide 50: Technical Summary
  ECMPR-Articulated Algorithm
    Systematically calls ECMPR-Rigid to perform pose estimation on an open kinematic chain.
Palm
D1
D2
D3
3D HAND MODEL
DISPLACEMENT MATRIX

## Slide 51: Technical Summary
  ECMPR-Articulated Algorithm
    Systematically calls ECMPR-Rigid to perform pose estimation on an open kinematic chain.
Palm
D1
D2
D3
These parameters can be estimated by ECMPR-Rigid.
3D HAND MODEL
DISPLACEMENT MATRIX

## Slide 52: ECMPR-Rigid Experiment 1
Registration of Simulated Data
LEGEND
model point, x15
inlier, x15
outlier, x10
covariance, x15
ITERATION #2
Rotation,
model points, x15
Translation, Random
Noise, Gaussian
inlier points, x15
Uniform Distribution
outlier points, x10

## Slide 53: ECMPR-Rigid Experiment 1
Registration of Simulated Data
LEGEND
model point, x15
inlier, x15
outlier, x10
covariance, x15
ITERATION #6
Rotation,
model points, x15
Translation, Random
Noise, Gaussian
inlier points, x15
Uniform Distribution
outlier points, x10

## Slide 54: ECMPR-Rigid Experiment 1
Registration of Simulated Data
LEGEND
model point, x15
inlier, x15
outlier, x10
covariance, x15
ITERATION #35
Rotation,
model points, x15
Translation, Random
Noise, Gaussian
inlier points, x15
Uniform Distribution
outlier points, x10

## Slide 55: ECMPR-Rigid Experiment 1
Registration of Simulated Data
Algorithm | ECMPR-Rigid | TriICP
# of Iterations | 36 | 215
Error in Rotation (%) | 1.5 | 10.3
Error in Translation (%) | 5.6 | 6.5
Correct Matches (%) | 76 | 28
Process Time (ms) | 31.4 | 63.2

## Slide 56: ECMPR-Rigid Experiment 2
Registration of Real Data

## Slide 57: ECMPR-Rigid Experiment 2
Registration of Real Data
Algorithm | ECMPR-Rigid | TriICP (Best) | TriICP (Worst)
# of Iterations | 12 | 6 | 4
# of Inliers | 95 | 177 | 227
Error in Translation (%) | 12.5 | 34.6 | 22.4
Minimization Error (mm) | 4.6 | 6.0 | 4.9
3D Points
ECMPR-Rigid
TriICP

## Slide 58: ECMPR-Articulated Experiment 1
Ground Truth + Inliers + Outliers
Registration, Large Initial Covariances
Registration, Small Initial Covariances
Registration of Simulated Data

## Slide 59: ECMPR-Articulated Experiment 1
Registration of Simulated Data
Ground Truth
Large Initial Variance

## Slide 60: ECMPR-Articulated Experiment 1
Registration of Simulated Data
Ground Truth
Small Initial Variance

## Slide 61: ECMPR-Articulated Experiment 2
Registration of Real Data
LIVE ACTION

## Slide 62: ECMPR-Articulated Experiment 2
Registration of Real Data

## Slide 63: Conclusion Future Work & Applications

## Slide 64: Conclusion
Future Work:
  Improvement of the efficiency of the ECMPR algorithm through
    the study of Classification EM (CEM) methods and
    the implementation of a kD-tree data structure during E-Steps.

## Slide 65: Conclusion
Potential Applications:
  The authors list none.
  However, 3D/3D organ registration in medical images is important:
    surgical planning
    radiotherapy

## Slide 66: Analysis Strengths & Weaknesses

## Slide 67: Analysis
Strengths:
  The main conclusion is (for the most part) supported by the data.
  All the experiments (even those using real data) are rather repeatable.
  The concepts of rigid and articulated registration are easy to comprehend even on a first-pass reading.
  All of the performance measure plots are easy to interpret and provide information at a glance.

## Slide 68: Analysis
Weaknesses:
  The authors do not report results for the live action ECMPR-Articulated experiment.
  The ECMPR algorithm is compared only to (a) itself and (b) a leading alternative which is not exceptionally similar.
  The Introduction section of the article elaborated on irrelevant details.
  The equation manipulations tended to flow in an unintuitive fashion.
  Some citations are more general than they should be.

## Slide 69: Reading
Bishop C. Pattern Recognition and Machine Learning. Springer, 2006.
Chen Y and Gupta M. EM Demystified: An Expectation-Maximization Tutorial. Department of Electrical Engineering, University of Washington. February 2010. UWEETR-2010-0002.
Horaud R, Forbes F, Yguel M, Dewaele G, Zhang, JA. Rigid and Articulated Point Registration with Expectation Conditional Maximization. IEEE Transactions On Pattern Analysis And Machine Intelligence. March 2011. Volume 33, Issue 3. 10.1109/TPAMI.2010.94.
Kang X, Taylor RH, Armand M, Otake Y, Yau WP, Cheung PYS, Hu Y. Correspondenceless 3D-2D registration based on expectation conditional maximization. Proc SPIE 2011 March 3, 2011;7964(1):79642Z.