## Slide 1: Force Feedback of Dual Force-sensing Instrument for Retinal Microsurgery
Can Wang,Sally Hong,Will Yang (Gr. 8)
Mentors: Xingchi He, Dr. Iulian Iordachita, Dr. Russell Taylor

## Slide 2: Overview
Background
Objective
Technical Approach
Deliverables
Timeline
Management Plan
Dependencies
Reading List and Reference

## Slide 3: Background I Importance of Force Feedback
  Surgeons cannot "feel" the surgery itself
  Loss of depth perception, dexterity, sense of touch, straightforward hand-eye coordination
Desirable to have force feedback to assist with vision feedback
Force feedback: counter pressure / movement, or alarm system to the force applied by the surgeon
Limitations to current robotic surgery (including eye microsurgey)
image taken from http://www.eng.uwaterloo.ca/~fhaque/

## Slide 4: Background II Retinal Microsurgery
Delicate manipulation of retinal tissue
Very low interaction forces (below human perception threshold)
Need a force-sensing surgical instrument to measure forces of the tool tip
Challenges: interactions between the tool shaft and sclerotomy opening
Image of retinal surgical tool from (2)

## Slide 5: Background II Retinal Microsurgery

## Slide 6: Background III Force Feedback Methods
Auditory feedback: alarm surgeons if tool force extends beyond threshold
  Reduce chance of retinal damage
Haptic feedback: exert opposing force to surgeon's hand
  Increase safety of the operation
Images of the eye robot from(3) credits to ICRA

## Slide 7: Background IV Fiber Bragg Grating (Force Sensor)
Advantage:
  Relatively cheap
  Stable
  Accurate
  Sterilizable
  Small
  Unaffected by noise
Disadvantage
  Need 3 fibers for 2x2 DoF sensing
  Measures distal force
Image from http://www.fbgs.com/technology/fbg-principle/

## Slide 8: Background IV Fiber Bragg Grating (Force Sensor)
Images of FBG tool tip from(3) credits to ICRA

## Slide 9: Objective
To develop and assess different force feedback methods for a dual force sensing instrument for retinal microsurgery
Sites: sclera, retina
Forms: haptic, auditory
Goal: Assist the surgeon to provide maximal operation safety for the patient

## Slide 10: Technical Approach
Design and build phantoms to simulate forces on the sclera and retina for eye experiments
Get acquainted with the eye robot, program and auditory feedback tools
Develop force feedback methods
  Auditory: pitch, frequency, sound
  Vibrotactile feedback
  Haptic: increased resistance, opposing movements
Carry out assessment experiments to test the combinations of force feedback methods
Evaluate experiment results
Images of the eye robot and phantom from(3) credits to ICRA

## Slide 11: Deliverables
Minimum
Test & analyze the effectiveness of feedback methods
Optimal auditory and haptic feedback methods
At least five different experimentation data sets
Expected
IRB approval of use of outside volunteers for the study
Maximum
Vibrotactile substitution for auditory feedback
Design and prototype of a better phantom
Axial force simulation through a different phantom or depth measurement

## Slide 12: Timeline

## Slide 13: Milestones
02/19 Planning and proposal finalization
03/15 IRB submission for use of human subjects.
03/30 Testing haptic vs. auditory testing
04/15 IRB approval for use of human subjects.
04/26 Presentation/final analysis preparation

## Slide 14: Management Plans
Group meeting at 3PM every Tuesday and Thursday
Meeting with mentor (Xingchi He) at 4:30 every Tuesday
Weekly update of the wiki page
General Responsibilities
  Cathey: Vibrotactile Feedback Development
  Will: Axial Force Simulation,Communication
  Sally: Wiki Page Update, Subject Recruitment
  All: Algorithm Development, Testing, Data Analysis

## Slide 15: Dependencies
Access to lab (Resolved)
Eye phantoms (Available)
  stretched rubber bands - sclera model
  rubber eye ball (more geometrically similar)
Usage of Eye Robot and control software
  Training by Xingchi
Force sensing Fibers for the instrument
  Current: 2x1 DoF (one fiber broken) - to familiarize ourselves with the device
  Standard: 2x2 DoF - to develop methods and run experiments with
Vibration actuator(s) and (possibly) Arduino
  Propose design and budget to Dr. Taylor (~$100)
  Feedback from Dr. Gehlbach and Dr Handa

## Slide 16: Reading List & References
1. M. Balicki et al. Micro-force Sensing in Robot Assisted Membrane Peeling for Vitreoretinal Surgery. MICCAI 2010, Part III, LNCS 6363, pp. 303–310, 2010
2. I. Iordachita et al. A sub-millimetric, 0.25 mN resolution fully integrated fiber-optic force-sensing tool for retinal microsurgery. Int J CARS (2009) 4:383–390
3. X. He et al. A Novel Dual Force Sensing Instrument with Cooperative Robotic Assistant for Vitreoretinal Surgery
4. R. Kumar et al. Preliminary Experiments in Cooperative Human-Robot Force Control for Robot Assisted Microsurgical Manipulation. IEEE(2000) 610
5. M. Kitagawa et al. Effect of sensory substitution on suture-manipulation forces for robotic surgical systems. The Journal of Thoracic and Cardiovascular Surgery 129:1,151