## Slide 1
Tracheoesophageal Prosthesis Insufflator
K. Liu in collaboration with Dr. R. Taylor and Dr. J. Richmon
Goals
  -- To develop an insufflator that will drive air into a tracheoesophageal voice prosthesis (TEP) to circumvent blocking of stoma.
Significance
  -- Operating the TEP requires constant obstruction of stoma with a finger, which is inconvenient. Those with arthritis, poor coordination, or weak pulmonary reserves are at a disadvantage as well.
  -- The insufflator connects directly to the TEP via silicone tubing and drives air through the TEP at the user’s discretion, increasing convenience.
Results
  -- Using 16g CO2 cartridges, the insufflator is capable of delivering CO2 below 1 PSI through the TEP.
  -- Device is portable and swapping out CO2 cartridges takes less than a minute.
TEP device
CO2 source and regulator valve