## Slide 1: CIS II: Project No. 2 Synthetic Aperture Ultrasound Imaging with Robotic Tracking Technique
Team: Haichong “Kai” Zhang, Ezgi Ergun
Mentors: Dr. Emad M. Boctor, Xiaoyu Guo, Alexis Cheng

## Slide 2: Outline
Started Topic and Goal: Synthetic Aperture Ultrasound Imaging
Statement of Relevance/Importance
Technical Summary of Approach
List of “Deliverables”
Key Dates & Assigned Responsibilities
List of Dependencies & Plan for Resolving
Management Plan
Reading List

## Slide 3: Stated Topic and Goal: Ultrasound Imaging
Ultrasound imaging is used in general medical diagnosis and diagnosis of pregnancy.
Axial resolution is determined by frequency of ultrasound system.
Lateral resolution is restricted by aperture size of ultrasound transducer.
12 week fetus
http://www.qlife.jp/dictionary/item/i_030840000/
Lateral Resolution

## Slide 4: Stated Topic and Goal: Synthetic Aperture Ultrasound Imaging
Normal Ultrasound system
…
…
…
…
…
…
Transmission
Receive
Reconstructed
Ultrasound Image
Low resolution
High resolution
Synthetic Aperture Imaging system

## Slide 5
Synthetic Aperture Ultrasound Imaging (SAUI)
Transmission
Receive
Reconstructed
Ultrasound Image
SAI with Tracking Technique
Repeated
Aperture Size
Repeated
Higher resolution can be achieved by expanding the aperture size.
Transformation of Probe is tracked while moving
Stated Topic and Goal: SAUI with Tracking Technique

## Slide 6: Statement of Relevance/Importance
To see deep site of tissue, only low frequency around 2MHz is available, so that the image resolution is limited.
Goal of SAUI with tracking system is the improvement of ultrasound image resolution.
Visualizing precise structure of fetus in early stage helps early disease detection as well as correct diagnosis.

## Slide 7: Technical Summary of Approach
Invent a decent ultrasound calibration method
Primitive Investigation
Final Implementation

## Slide 8: Technical Summary of Approach: Invent a decent ultrasound calibration method
In order to move the probe for a designated position, or to know the location of the origin of ultrasound image, unknown rigid-body transformation on the transducer from sensor to image is needed to be calibrated.
Process to identify this unknown transformation is called ultrasound (US) calibration.
Universal
Robot
Unknown
Transformation

## Slide 9: Technical Summary of Approach: Invent a decent ultrasound calibration method
A major ultrasound calibration (hand-eye calibration) is based on segmentation method.
The problem is very difficult to find out a representative from a cloud.
Accuracy is limited (1.5 mm~) although compensation method is applied.
Figure:
AX=XB-phantom is used to reconstruct 3D information.
Rotation and transformation can be obtained through one image.
It is very difficult to identify the center of the point.

## Slide 10: Technical Summary of Approach: Invent a decent ultrasound calibration method
Goal: accuracy of 500 µm (wavelength of 2.5MHz transducer)
Idea to improve the accuracy:
US Calibration Using Moving Phantom
Moving the phantom toward x and y axis, from the coordinate of phantom.
Normalized cross correlation (NCC) is used to identify the displacement of phantom in image.
The goal of this project is to reconstruct X only using moving information.
0.3 µm accuracy is confirmed in simulation

## Slide 11: Technical Summary of Approach: Primitive investigation
Without US calibration, primitive confirmation of the potential of the technique is available using precise tracking system and accurate location indicator.
Active echo element is a strong candidate for the test due to its accurate sensitivity for ultrasound transducer center detection (50 um).
Learn SAUI algorithm and optimize it for this approach.
High quality closed-loop ultrasound imaging system
US 20140024928 A1

## Slide 12: Technical Summary of Approach: Primitive investigation
Rotate probe while keeping
the length of red line same
Scan a probe by keeping
the length of red line same
Rotate probe while keeping
the length of red line same
Figure: Three scenarios for the synthetic aperture test

## Slide 13: Technical Summary of Approach
Invent a decent ultrasound calibration method
Primitive Investigation
Final Implementation

## Slide 14: Deliverables
Minimum
Experimentally confirm the new calibration method is superior to segmentation based calibration.
Construct the design for SAUI w/ robotic tracking using active-echo system.
Expected
Confirm SAUI w/ robotic tracking using active-echo system.
Maximum
Implement SAUI w/ robotic tracking using calibrated transducer
Confirm the resolution improvement through phantom experiment

## Slide 15: List of Dependencies and Plan for Resolving
Ultrasound imaging system
  MUSiiC Lab
Low frequency ultrasound probe
  Got a 2.5MHz phased array transducer
  Need to make a connector to available US machine Discuss with Xiaoyu
  Need to make a attachment to robot Print in 3D or using silicon labber
Tracking system: Robot
  Universal Robot is available
  Need to figure out control system Learn from Rishabh and Fereshteh
Access to mentors
  Meeting with Dr. Boctor
  Take appointments to other mentors when needed

## Slide 16: Key Dates and Assigned Responsibilities
 | Feb |  |  |  | March |  |  |  | April |  |  | 
US calibration using moving phantom |  |  |  |  |  |  |  |  |  |  |  | 
Synthetic aperture ultrasound imaging |  |  |  |  |  |  |  |  |  |  |  | 
Primitive Investigation: Preparation |  |  |  |  |  |  |  |  |  |  |  | 
Primitive Investigation: Test using active-echo |  |  |  |  |  |  |  |  |  |  |  | 
SAUI implementation with tracking |  |  |  |  |  |  |  |  |  |  |  | 
Management plan
Kai: US calibration and robotic control system
Ezgi: Synthetic aperture imaging algorithm

## Slide 17: Reading List
Nock, L.P. , Trahey, G.E.
“Synthetic receive aperture imaging with phase correction for motion and for tissue inhomogeneities. I. Basic principles”, IEEE TUFFC, 1992
Trahey, G.E., Nock, L.P.
“Synthetic receive aperture imaging with phase correction for motion and for tissue inhomogeneities. II. Effects of and correction for motion”, IEEE TUFFC, 1992
Jørgen Arendt Jensen, Svetoslav Ivanov Nikolov, Kim Løkke Gammelmark, Morten Høgholm Pedersen
“Synthetic aperture ultrasound imaging”, Ultrasonics, 2006
Karaman, Mustafa,Pai-Chi Li, O'Donnell, M.
“Synthetic aperture imaging for small scale systems”, IEEE TUFFC, 1995

## Slide 18: Thank you for your attention.
Question?