## Slide 1
An Electrostatic Model for Assessment of Joint Space Morphology in Cone-Beam CT
Computer Integrated Surgery II – Project 11
Checkpoint Presentation
Student: Qian Cao
Mentor: Jeff Siewerdsen
CBCT Image
Segmentation
Threshold
Hole Filling
Shape Opening
ROI Boundary
Charged Plates
+Q Femur
-Q Tibia
Laplace Equation
Jacobi method
Iteration
3D Joint Space Map Visualization and Analysis
+
-
Interpolation
of Field Gradient
Distance along Field Lines
E
Rigid Registration
T
Notes: WHO declared yr 2000-2010 Bone and Joint decade as a recog… of substantial burden placed by MSK conditions all over the world….in this presentation…I am gonna talk .. ‘p Q imaging’ using a cbct scanner ..exclusively dedicated for MSK extremities…..

## Slide 2
CBCT Image
Segmentation
Threshold
Hole Filling
Shape Opening
ROI Boundary
Charged Plates
+Q Femur
-Q Tibia
Laplace Equation
Jacobi method
Iteration
Visualization of 3D Joint Space Map
+
-
Interpolation
of Field Gradient
Distance along Field Lines
E
Rigid Registration
T
Recap & Extended Goal
To develop an efficient method of mapping joint space width in CBCT volumes using electrostatics.
2. To apply the method to the analysis of osteoarthritic (OA) knees and non-OA knees under weight-bearing and non-weight-bearing conditions.  NEW
62 Scans Total: 31 knees in sitting and standing position, 18 OA, 13 non-OA.
Notes: WHO declared yr 2000-2010 Bone and Joint decade as a recog… of substantial burden placed by MSK conditions all over the world….in this presentation…I am gonna talk .. ‘p Q imaging’ using a cbct scanner ..exclusively dedicated for MSK extremities…..

## Slide 3
Revised Deliverables
Minimum Deliverable (Expected by 03/01/2014)
1. A set of prototyped MATLAB functions for joint space mapping using the capacitor model. ✓
2. A set of prototyped MATLAB functions for segmentation. ✓
3. Documentation of existing code. ✓
Expected Deliverable (Expected by 04/01/2014  PUSH BACK TO 05/03/2014)
1. A set of validated MATLAB functions for joint space mapping using the capacitor model. ✓
2. A refined MATLAB function for segmentation. ✓
3. Detailed analysis of algorithm performance (convergence characteristics, accuracy, speed etc). (50%)
4. MATLAB routines for visualization of the analysis results (volume rendering + GUI) in VTK. ✓
5. Provide relevant documentation. (50% complete)
6. Conduct a phantom study to compare the algorithm with existing closest-point method. NEW ✓
7. Apply the analysis pipeline to the analysis of OA and non-OA knee joints under load-bearing (standing) vs non-load-bearing (sitting) conditions (62 CT Volumes). (30% complete) NEW
Maximum Deliverable (Expected by 06/01/2014)
1. Submit abstract to the American Association of Physicists in Medicine (AAPM) annual meeting. NEW ✓
2. Submit a technical paper. NEW

## Slide 4
Revised Dependencies
Bi-weekly meeting with mentor (bi-weekly meeting scheduled with Prof. Siewerdsen).
CBCT knee volume test data (Two 61 datasets of OA knees and non-OA knees available for algorithm testing and validation).
Phantom study.
  Equipment + materials + access to shop (Traylor machine shop).
  Access to CBCT scanner (lab bench).
  Radiation safety training (radiation badge acquired).
Computing resources.
  Up-to-date MATLAB w/ image processing and parallel computing toolboxes (R2013b).
  CUDA-enabled graphics card (NVidia GTX470).
  C++ IDE and compiler (Visual Studio 2008).
  Visualization library (VTK).
Access to relevant literature (Lab database & JHU Library Website).

## Slide 5
Revised Timeline

## Slide 6
Results I - Phantom Study
Design & Goal
Vertically displace the cup via the caliper by a known amount. Try to recover the magnitude of displacement and the distance between the cup and the stationary wedge using the electrostatic modeling method.
Caliper
Cup
Wedge (30⁰ slope)
0.5 mm initial vertical displacement
Raise cup in increments of 0.4 mm for 10 increments
…
0.9 mm
1.3 mm
1.7 mm
4.5 mm

## Slide 7
A sampling of field lines at 4.5 mm vertical displacement:

## Slide 8
Vertical Displacement from Wedge: 0.5 mm
1.3 mm
2.1 mm
2.9 mm
3.7 mm
4.5 mm

## Slide 9
3.9 mm
1.8 mm
Though the electrostatic model results in larger measurements of absolute distance than the conventional closest-point scheme for this geometry, it could measure incremental displacement accurately using the minimum line.
(Figs.) Field lines with minimum length at 2 different vertical displacements.
Histogram of field line lengths with respect to displacement.
0.5 mm
4.5 mm
Slope: 0.9947
Intercept: 0.3068
R2: 0.99967

## Slide 10
Results II - Patient Study
Data
Standing and sitting CT scans of 13 asymptomatic knees and 18 symptomatic knees for osteoarthritis (OA).
Goal
To distinguish OA vs non-OA, load-bearing vs non-load-bearing via the electrostatic method.
CBCT Image
Segmentation
Threshold
Hole Filling
Shape Opening
ROI Boundary
Charged Plates
+Q Femur
-Q Tibia
Laplace Equation
Jacobi method
Iteration
Visualization of 3D Joint Space Map
+
-
Interpolation
of Field Gradient
Distance along Field Lines
E
Rigid Registration
T

## Slide 11
Case A072 Non-OA: Load-bearing vs. non-load-bearing
Sitting
Standing
Sitting  Standing
Lateral
Medial
Anterior
Posterior

## Slide 12
Case A036 OA: Load-bearing vs. non-load-bearing
Sitting
Standing
Sitting  Standing
Lateral
Medial
Anterior
Posterior

## Slide 13
Thanks!