## Slide 1: 3D Triangle Mesh-Based Edge Detection and Segmentation Project #2 Seminar Presentation En.600.446 Spring 2015
Joshua You
Mentors: Dr. Armand, Dr. Gordon, Captain Grant, Dr. Ryan Murphy

## Slide 2: Project Overview
Project Goal: Integration of 3D scanning solutions for defect identification and reconstruction in cranioplasty procedures.

## Slide 3: Structure Sensor
$350 iPad accessory
USB interface
Open Source code
Comes with SDK
Supported by Occipital

## Slide 4: Today’s Papers
(1) Y. Sun, D. L. Page, J. K. Paik, A. Koschan, M. A. Abidi. Triangle Mesh-Based Edge Detection and Its Application to Surface Segmentation and Adaptive Surface Smoothing. Imaging, Robotics, and Intelligent Systems Laboratory. IEEE ICIP: 2002.
(2) M. Kolomenkin, I. Shimshoni, A. Tal. On Edge Detection on Surfaces. Computer Vision and Pattern Recognition. IEEE Conference: 2767-2774, 2009.
(3) V. Vidal, F. Dupont. Robust Feature Line Extraction on CAD Triangular Meshes. International Conference on Computer Graphics Theory and Applications. GRAPP: 2011.

## Slide 5: Motivation
Need to be able to accurately process the mesh model
Depth segmentation especially needs to be precise

## Slide 6: Paper 1: Introduction
Proposed in 2002
Proposes an edge detection algorithm for triangle meshes
Uses edge strength to segment surfaces

## Slide 7: Paper 1: Math Terminology
Eigen analysis - “Method of simplifying coordinates”
Geodesic - A curve whose tangent vectors remain parallel if they are transported along it
Normal (Tensor) Voting - A way of estimating the orientation information and curvature of a surface at a given point

## Slide 8: Paper 1: The Formula
For all vertex q in the mesh:
  The neighboring triangles, T_i, “cast votes”:
    Where μ is the weight of the vote
    and n' is the voted normal by T_i’s normal n

## Slide 9: Paper 1: The Formula
The collection of tensor votes at q is:
  Where M is the number of triangles inside a geodesic window of q
  μ_i exponentially decreases, based on geodesic distance between p (barycenter of T_i) and q

## Slide 10: Paper 1: The Formula
And, to find n_i', the voted normal:
It is not clear what the ⋀ operator is
  Pretty sure it’s just a tensor product: ⊗

## Slide 11: Paper 1: The Formula
Finally, to calculate edge strength:
  Where v_1 ≥ v_2 ≥ v_3 are eigenvalues of T
  e_1 is the eigenvector corresponding to v_1
  And

## Slide 12: Paper 1: The Formula

## Slide 13: Paper 1: The Results

## Slide 14: Paper 2: Brief Overview
Triangle Mesh = “smooth manifold (base)” + “local height function (relief)”
Relief edges are then just the zero crossings of the normal curvature defined by the local height function.

## Slide 15: Paper 2: Results
Very complicated, though extremely accurate
“Too much” for what we need

## Slide 16: Paper 3: Potential Addition
Seems like a similar idea to what is proposed in paper 1
Talks about making system more robust by machine learning
  Support Vector Machines

## Slide 17: Questions?