## Slide 1: Surgical Instruments for Robotic Microsurgery Computer Integrated Surgery II - Spring 2015
Zaid Ashai
Pranav Lakshminarayanan

## Slide 2: Team Members and Mentors
Zaid Ashai
Pranav Lakshminarayanan
Dr. R. Taylor Kevin Olds
Dr. J. Richmon Allen Feng

## Slide 3: Background and Motivation
Endolaryngeal microsurgery is the treatment of choice for a variety of disorders including
phonotraumatic nodules
polyps and cysts
vocal cord dysplasia and cancer
benign laryngeal neoplasms such as papilloma

## Slide 4: Background and Motivation
Robotic ENT Microsurgery System (REMS)
General purpose “steady-hand” robot
5 DOF:
3 translational at delta stage
1 roll at arm
1 tilt at tool holder
A 6 DOF force/torque sensor

## Slide 5: Background and Motivation
Feasibility Testing:
Subjects = 3 surgeons (surgeon, fellow, novice)
Testing phantom = aluminum plate with clusters of holes
Hole diameters = 1.6mm, 1.1mm, and 0.8mm
“Operation”-like procedure:
Touch plate → bad buzzer → failure
Avoid plate → good buzzer → success
Results: 28% success manually, 91% robotically

## Slide 6: Background and Motivation
Olds, Kevin, et al. “Preliminary Evaluation of a New Microsurgical Robotic System for Head and Neck Surgery”. 2004.

## Slide 7: Goal
Develop novel surgical instruments for robot assisted vein suturing

## Slide 8: Relevance
Two categories of existing robots:
Broad proficiency (ie. Da Vinci machine)
Special-purpose (sub branch of head and neck)
New system (REMS) needed for greater proficiency at head and neck level
Admittance-style, not master-slave

## Slide 9: Areas for Improvement
Tool changing is tedious
Error from tip deflection (1.167mm overall)
Integrated needle holder is flimsy
Inner components are not efficient
Movement algorithm
Ineffective needle holder tips, easily worn down

## Slide 10: Criteria
Specifications
Quick-release tool holder
Tweezer-like suture needle holder
Minimal obstruction of surgeon’s hand

## Slide 11: Design Approach
Brainstorming
CAD Models
Implement with REMS
Testing
Refine/Redesign
Prototyping

## Slide 12: Design of Instruments
Eye Robot Tool
Kalt Eye Needle Holder

## Slide 13: Design of Instruments
Possible design by Allen Feng

## Slide 14: Deliverables
Computer-aided design of:
suture needle holder
tool attachment unit
Pilot study with simple tool
Final report analyzing viability of designs
Minimum

## Slide 15: Deliverables
Building of designed suture needle holder and tool attachment unit
Needle holder tips with improved precision and durability
Implementation of tools with REMS robot
Surgical testing in mock OR by Dr. Richmon
Expected

## Slide 16: Deliverables
Conduct clinical study on viability of new tools with medical students, under the supervision of Allen Feng and Dr. Richmon
Re-designing and optimizing the REMS movement algorithm and/or mechanisms
Maximum

## Slide 17: Projected Timeline

## Slide 18: Dependencies
Dependency | Resolution
Machine shop certification | Register by end of February
Access to steady-hand robot | Schedule time to work with robot
Materials to design prototypes | Check availability of materials in machine shop Purchase remaining materials
Funding for materials and prefabricated components | Request funding from Dr. Taylor Estimated to $200
Scheduling of mock operations and study | Schedule with Dr. Richmon and Allen Feng

## Slide 19: Management Plan
Zaid | Pranav
Brainstorming and design of needle holder and locking mechanism | 
CAD models | Calibration algorithm
Prototyping of needle holder and locking mechanism | 
Implementation of tools with REMS and phantom testing | 
Weekly meetings with mentor (Kevin)
Bi-weekly updates to Dr. Richmon and Allen