## Slide 1: 3D Forward and Back-Projection for X-Ray CT Using Separable Footprints
04/21/16
Group 5: Seung Wook Lee
Mentor: Dr. Jeff Siewerdsen
Dr. Matthew Jacobson, Dr. Tharindu da Silva, Dr. Joseph Goerres
Notes: Name: Wook
Paper I am presenting today is ~

## Slide 2: Project Overview
“Fluoro-hunting”:
Process to find an optimal fluoroscopic view
Time-consuming, more radiation exposure to both patients and physicians, physically cumbersome, safety issues.
Solution: Digitally Reconstructed Radiograph (DRR):
Generate forward-projection image of preoperative CT data
Use DRR to find the most optimal view
Advantages
Less time consuming
Less radiation exposure
Less user variability
Goal: Surgeon-friendly User Interface (UI) to simulate fluoroscopic view of mobile C-arm
Notes: To briefly restate our project, aim of our project is to develop a surgeon-friendly user interface to simulate fluoroscopic view of mobile C-arm. Often during orthopedic surgeries or in other procedures involving C-arm, surgeons often suffer finding a view they want to see. This process is time consuming and more exposes patient and surgeons to radiation.
So we propose a method to use digitally reconstructed radiograph simulate the fluoroscopic view corresponding to a C-arm position. Users can

## Slide 3: Paper Selection
Long, Yong, Jeffrey A. Fessler, and James M. Balter. "3D Forward and Back-Projection for X-Ray CT Using Separable Footprints." IEEE Transactions on Medical Imaging IEEE Trans. Med. Imaging 29.11 (2010): 1839-850. Web.
Paper:
Proposes two new approaches for 3D forward and back projections by approximating a voxel footprint function as a 2D separable function.  Reduce computational burden by simplifying integration of the footprint functions
Our project: Generate DRR  forward projection
  Possible implementation for more accurate DRR generation (as a future work)
*Footprint Function: projection of a basis function (i.e. cubic voxel, etc)

## Slide 4: Background
Iterative statistical methods for 3D CT reconstruction  Better image quality/ reduce dose than conventional
Computationally heavy: bottleneck in iteration of forward/back projections
  Forward/backprojection per iteration
  Many studies with compromise b/t complexity and accuracy
  Evaluating integrals of footprint fn. over detector cell / Exact calculation of footprint function  expensive
Notes: Little background for motivation of this research.
Conventionally, Iterative reconstruction provides better quality images with lower noises as it iteratively reconstruct images. However, as each iteration requires one forward and backprojection, the process is computationally expensive. One of the factor contributing to complexity of this method lies in complexity of integrating footprint function over a detector cells, and exact calculation of the footprint function – these processes will be briefly discussed in later slides.

## Slide 5: Background: Cone-Beam Geometry
Cone-Beam (CB) system with flat detector
β: source position angle from y axis
(s, t): detector coordinate
p0, p1: source / projection point
: Direction vector
Ds0 : Source-rotation center distance
D0d : Rotation center-detector distance
: Azimuthal angle of a ray
: Polar angle of a ray
y
z
p1
p0
x
z
y
p1
p0
Notes: Here is a litte background for Cone-Beam geometry. This paper focus on flat-detector axial-CB geometry. Here are figures of the geometry, and parameters that are used to described geometry. I am not going to explain this part with too much detail. (read out)

## Slide 6: Background: Cone beam projection
Discretized object described by basis function superimposed on N1xN2xN3 Cartesian Grid:
Projection y of a 3D discretized object f(n) on detector (sk,tl): sum of blurred footprint * value
Blurred footprint F: 2D convolution of q/h
  q: footprint function of nth basis on (s,t) with angle β
  h: shift-invariant 2D blur function
CB projection footprint function of nth basis on (s,t) with proj. angle β: forward projection
  - Computationally expensive
Basis function
Notes: With the geometry in mind, I will briefly talk about cone-beam projection and footprint function.
Formula on the top describes a discretized object, represented by common basis function superimposed on a Cartesian grid. (In practice of iterative image reconstruction, this model rather than continuous object f(x) is used)
What’s below is projection y on detector coordinate s,t descried as a sum of multiples of blurred footprint fn alpha of nth object on detector coordinate s,t and value of the nth object. This blurred footprint function is described as 2D convolution of shift-invariant blur function h and q, the cone beam footprint function of beta. And solving for q exactly, and solving for this double integral around the footprint function is one of main computational complexity in iterative reconstruction approach.

## Slide 7: Alternative approach: approximate footprint
Simulated flat-detector CB geometry
“Exact” Footprint functions computed for voxels centered at 3 different places
  Origin (left)
  (100, 150, 15), β = 0 ° (mid) θ=2.1°
  (93, 93, 93), β = 0°(right) θ=11.5°  high axial angle
Profile in t/s: look like 2D separable functions
Profile in s: Trapezoidal function
Profile in t: Rectangular/trapezoidal fn.
Notes: As exact computation of the footprint function is computationally heavy, the paper proposes an alternative. In process of the search of alternative, they generate exact footprint function for voxels centered at three different places solving formula written last slide. And they found profile of footprint function in s and t direction seems separable. Profile in s looks like a trapezoid and profile in t looks like rectangular, for voxel with not much axial angle and trapezoidal for voxel with high axial angle.

## Slide 8: Separable Footprint
Models footprint function as a multiple of amplitude function and 2D separable function.
2D Separable function:
Approximation of footprint function:
  No need of line integral
  Much faster to compute blurred footprint (in assumption h(s,t) also separable)
2D separable footprint fn.
Amplitude
Notes: Inspired by these observation, the paper proposes a model of separable footprint. It approximates the footprint function as a multiple of amplitude L and 2D separable function qsf. Qsf is separable to two components, one in terms of s and the other in terms of t. In other words, the footprint function is separated into multiple of s and t profiles with an appropriate amplitude. This approach poses a number of advantages over exact calculation. As it is faster~

## Slide 9: Separable Footprint
As observed previously, increase in axial angle of a ray changes shape of profile in t of a footprint function
Two methods:
  Trapezoid/Rectangular (SF-TR)
    s profile: trapezoid (transaxial)
    t profile: rectangular (axial)
  Trapezoid/Trapezoid (SF-TT)
    s/t profile: trapezoid (both)
    More accurate approximation for bigger axial angles
Footprint fn.
Profile in t
θ
source
Detector
Notes: So as previously mentioned, difference in profile for voxels with high and low axial angles. So they developed two approximation method, one to use trapezoid function in transaxial direction and to use rectangular of axial direction. This approach is named SF TR. The other uses trapezoid function to approximate both directions.

## Slide 10: Separable Footprint
Amplitude Approximation:
Determined by azimuthal/polar angles of rays
A3: voxel-dependent amplitude
  Based on angles of rays passing every voxel center
A2: voxel-ray dependent amplitude
  Polar amp: Based on polar angle of ray connecting source/detector center
A3: ray-dependent amplitude
  Based on azimuthal/polar angle of ray connecting source/detector center
Notes: The amplitude approimatino is done in 3 ways. The amplitude fn depend on azimuthal and polar angle of the rays. Three different methods to calculatethe amplitude, A3 a2 and a1. A3 is voxel dependent so it computes amplitude based on angles of ray connecting source and voxel centers. A2 method uses rays connecting detector center and the source to calculate l_theta, while using same voxel based approach to compute l pi. A1 uses rays connecting detector centers and the source to compute both terms.

## Slide 11: Experiments:
Compared with distance-driven (DD) projector method for evaluation
  DD method: approximates voxel footprints using rectangle.
Experiment 1: Forward projection of 1mm3 voxel
  Computed maximum errors of forward projections
Experiment 2: Speed of forward/back projection
  Measured computation time
Experiment 3: Iterative Reconstruction
  Compared image generated by iterative reconstruction of digital phantom
Notes: CoTo test perforamcne of their approach, the study set an experiment to compare performance of Separable footprints with distance-driven method. This method approximates voxel footprints just using rectangles.
First experiment is forward project .
2nd is to test speed of forward back projection
And 3rd is to check quality of reconstructed images with iterative reconstruction
mpared with distance-driven projector method

## Slide 12: Results: Experiment 1
Forward projection of basis function
  Voxel size 1x1x1 mm
  Centered at (0,0,0) and (100, 150, -100)
Combination of different SF and amplitude methods examined (TR-A1~A3, TT-A1,A2)
Ground truth: linearly averaging 1000 x 1000 analytical line integrals of rays sampled over each detector cell
SF method: lower maximum error than DD method
Case 1: center at (0,0,0)
  TR/TT showed same result – similar profile
  A1 vs. A2, A3 Slightly higher error for A1 by 3.4x10-4 at β = 45°
  DD errors: at β = 45° x652 larger than SF-A1 methods x2.6 × 103 larger than SF with A2/A3 methods
Notes: Forward proj. of a voxel at 000 and 100 150 -100 was performed. Figure on right here shows result from voxel centered at origin. Combination of two different footprint approximations and 3 different amplification methods were used. They established ground truth as~.
And figure on the right shows SF method overall has lower maximal error than DD.
In this particular case,

## Slide 13: Results: Experiment 1
Case 2: Voxel centered at (100, 150, -100) mm
TT method showed higher accuracy
  TT: More accurate approximation when high axial angle.
Overlap of different TT and TR methods
  With larger cone angles, three amplitude method have similar accuracies
Notes: In this case, voxel centered at ~ examined. TT method showed higher accuarcy

## Slide 14: Result: Experiment 2
Use (512x512x128) volume with spacing 0.5 mm in all directions
Average of 5 projector runs
SF-TR A1/A2 method: as fast as DD method (or faster)
A3 method: takes 50% more time than A1/A2
SF-TT: takes x2 more time than SF-TR method or DD method

## Slide 15: Result: Experiment 3
Compared DD/SF-TR-A1 and A2 methods within iterative image reconstruction
  A1/A2 returned visually the same result
3.1. Whole field of view comparison
3D Shepp-Logan digital phantom
FOV: 250x250x40 mm3 Sampled: 256x256x64 Resolution: 0.98 × 0.98 × 0.63 mm3 (coarse)
Maximum/RMS errors similar for two images
DD method: artifact around top/bottom
  CB artifact due to poor sampling @ off-axis slices
Notes: 300 ITERATIONS of conjugate gradient algorithm,. Initialized by reconstruction by Fdk method
Fineer sampling of ROI appearently introduced

## Slide 16: Result: Experiment 3
3.2 ROI Comparison
ROI: at rotation center of FOV (50 x 50 x 20)
Higher sampling: 256x256x65
Resolution: 0.24×0.24×0.31 mm3
Maximum errors: - SF-TR: 20 Hounsfield units (HU) - DD: 105 HU
RMS errors: - SF-TR: 1.6 HU - DD: 2.8 HU
More artifacts in DD method – rectangular app.
Finer sampling of FOV: aliasing removed in DD
SF-TR vs. SF-TT: Artifacts from poor sampling @ off-axis slices dominates No difference with voxel with high axial angle
Notes: Rectangle approximation of DD: blurs corner of voxels
With finer sampling of FOV, aliasing was removed. This tells finer sampling reduces differences between trapezoidal and rectangular approximation.

## Slide 17: Assessments
Pros
  Well organized
  Well written, extensive amount of background info.
  Experimental methods well described with speculation of systems.
    Types of processor used, FOV/ROI dimensions, spec. of digital phantom used, etc.
    Establishment of ground truth
  Future works addressed
Cons
  Use of low-resolution digital phantom.

## Slide 18: Conclusion
Separate Footprint method: good accuracy in forward projection
  Many possible implementation – different basis function, etc
  Well-resolves complexity associated with exact computation of footprint fn.
  Better accuracy in approximation of footprint functions.
Time too slow for our application
  Implementation on GPU?
  Report from another paper: forward projection took 20.9s for a single-turn (360°) with 984 views for 3D object of size 512 x 512 x 640 [2]
May provide additional option for a surgeon to observe a particular fluoroscopic view with a higher accuracy, in sacrifice of computation time

## Slide 19: References
[1] Long, Yong, Jeffrey A. Fessler, and James M. Balter. "3D Forward and Back-Projection for X-Ray CT Using Separable Footprints." IEEE Transactions on Medical Imaging IEEE Trans. Med. Imaging 29.11 (2010): 1839-850. Web.
[2] M. Wu and J. A. Fessler. “GPU acceleration of 3D forward and backward projection using separable footprints for X-ray CT image reconstruction”. Proc. Intl. Mtg. on Fully 3D Image Recon. in Rad. and Nuc. Med, pages 56–9, 2011

## Slide 20: Questions?