## Slide 1: Head Mounted Display Integration for Orthopedic Surgery
Group 17, Zhuokai Zhao
Mentors: Long Qian, Alexander Barthel, Sing Chun Lee, Javad Fotouhi, Dr. Bernhard Fuerst, Dr. Nassir Navab
Computer Aided Medical Procedures

## Slide 2: Background
Motivation: Orthopedic Surgery
  Placements of screws and wires into bones for fracture reduction
  Image-guided systems provide 2D view
  Complex task to do 3D alignment with 2D images  Requires frequent re-positioning of X-ray machine
  Can augmented reality help?
Image Source: Lee, S. C., Fuerst, B., Fotouhi, J., Fischer, M., Osgood, G., & Navab, N. (2016).
Calibration of RGBD camera and cone-beam CT for 3D intra-operative mixed reality visualization.
International Journal of Computer Assisted Radiology and Surgery, 11(6), 967-975. doi:10.1007/s11548-016-1396-1

## Slide 3: Goal
Deploying HMDs with simple 2D X-ray views to orthopedic surgery
Use augmented reality to visualize the occluded part of the needle
  Build a needle model in Unity which could be later deployed to HoloLens
  Display (Optical See-through) the part of the needle that is inside the patient’s body with HoloLens
Comparison of user’s perception of AR visualizations
  Use ARToolKit to track the wire for evaluation purposes
  The virtual needle should align with the physical needle
  The virtual needle should move with the physical needle
  Which AR visualization is the best?

## Slide 4: System Setup
Surgical site observed by both RGBD camera and the head mounted display device

## Slide 5: Technical Summary
Calibrate RGBD camera (Intel SR300) and HMD device (HoloLens)
  A marker is placed in surgical site observed by both RGBD camera and the head mounted display device
  Use ARToolKit to track and get the transformation of marker between RGBD Camera and head mounted display device
Patient’s body model detection and recognition
  Approach by developing basic algorithms with thresholding on point clouds
Display the under-skin virtual needle in HoloLens
  Optical See-through problem, virtual needle needs to align with the physical needle
  Unity needle model in 3D, build and deploy in Visual Studio
  Locations depend on result from above

## Slide 6: Deliverables
Minimum
  Roll out HMDs to the hospital operating room
  Camera calibration algorithm for RGBD camera and the head mounted display device
  Marker tracking algorithm used to track needle movements
  Skin model detection algorithm with basic thresholding on point clouds
Expected
  Needle location and orientation estimation in 3D space
  Algorithms that determine which part of the needle is within the patient’s body
  Display the part of the needle that is within the patient’s body via HoloLens
Maximum
  Implementation of different perceptual cues
  Evaluation and comparison of different visualizations

## Slide 7: Dependencies Hardware
Microsoft HoloLens ✓
  Mentor Supplies
Intel RealSense SR300 ✓
  Mentor Supplies
Windows Laptop/Desktop ✓
ARToolKit ✓
Visual Studio 2015 Update 3 ✓
HoloLens Emulator ✓
Intel RealSense SDK ✓
Checkerboard used for calibration ✓
Software & Others

## Slide 8: Management
Weekly CAMP Meetings
  Wednesday 9 – 10 am
  Discuss the progress with Dr. Fuerst and Dr. Navab
Weekly Meeting with Mentors
  Tuesday 3pm
  C-arm related resources/questions: Javad and Sing Chun
  Head Mounted Display related resources/questions: Alex and Long

## Slide 9: Time Table

## Slide 10: Milestone Dates

## Slide 11: Supplemental Readings
Brand, J., & Mason, J. (n.d.). A comparative assessment of three approaches to pixel-level human skin-detection. Proceedings 15th International Conference on Pattern Recognition. ICPR-2000. doi:10.1109/icpr.2000.905653
Tan, W. R., Chan, C. S., Yogarajah, P., & Condell, J. (2012). A fusion approach for efficient human skin detection. IEEE Transactions on Industrial Informatics, 8(1), 138–147. doi:10.1109/tii.2011.2172451
Pauly, O., Diotte, B., Fallavollita, P., Weidert, S., Euler, E., & Navab, N. (2015). Machine learning-based augmented reality for improved surgical scene understanding. Computerized Medical Imaging and Graphics, 41, 55–60. doi:10.1016/j.compmedimag.2014.06.007
Zhang, Z. (2000). A flexible new technique for camera calibration. IEEE Transactions on Pattern Analysis and Machine Intelligence, 22(11), 1330–1334. doi:10.1109/34.888718

## Slide 12: Supplemental Readings Continue
Yogarajah, P., Condell, J., Curran, K., McKevitt, P., & Cheddad, A. (2012). A dynamic threshold approach for skin tone detection in colour images. International Journal of Biometrics, 4(1), 38. doi:10.1504/ijbm.2012.044291
Robert Discover (2016, April 20). Augmented reality (ARToolkit + unity3D) Retrieved from https://youtu.be/T8O-XKQ2Avo