## Slide 1
Robot-Assisted Transcranial Magnetic Stimulation (RA-TMS)
A system to systematically map the effects of TMS at the cerebral cortex
Mentors:
VOR lab: Dr. Amir Kherdamand (akherad@jhu.edu), Dr. David S. Zee
BIGSS lab: Farshid Alambeigi (falambe1@jhu.edu), Dr. Mehran Armand

## Slide 2
TMS as a tool to study brain function:
TMS can excite or inhibit a target area within the brain, allowing functional mapping
of cortical regions by creating transient functional changes in the brain

## Slide 3
Steps involved in applying RA-TMS:
Interactive navigational guide that co-registers subject’s head with the 3D MRI-based reconstruction of the head and the brain (A)
Real-time tracking of the trajectory of TMS coil for placement over a target cortical location (B)
Find the best orientation of the TMS coil over the scalp to keep it tangent with respect to the underlying cortical target
Maintain and adjust precise orientation and distance of the coil from the cortex while applying TMS (B)
Move the TMS coil reliably between a number of different cortical locations
Notes: In this slide let’s talk about the TMS

## Slide 4
The robotic arm can move in between trajectories while maintaining proper orientation of the TMS coil relative to the target cortical location (represented by the red cone). The purple mark within the blue grid shows where the coil is being moved in real time by the robotic arm to match the marked trajectory on the MRI image.
Conceptual illustration of the Robot-Assisted TMS (RA-TMS):
Notes: In this slide let’s talk about the TMS

## Slide 5
What Students Will Do:
Collaborating with the VOR Lab and BIGSS Lab to
  Make a setup simulating the RA-TMS procedure
  Calibrate the robot and TMS coil, Register the head, and create the coil target points
  Program UR5 to safely perform the RA-TMS both in simulation and on setup considering the mentioned requirements
Deliverables:
A robotic-system (both software and hardware) to safely perform the RA-TMS procedure
Size group(s): 2-3
Skills:
Team work, Commitment, C++ Programming, Fundamentals of Robotics and Robot-Assisted Surgery (CIS I + Intro. to Robotics courses are recommended)
Mentors: Refer to the first page