## Slide 1: Thermal Imaging Checkpoint
Student: Changfan Chen
Mentor: Dr.Emad Boctor Younsu Kim
04/09/2019

## Slide 2
Review
  HIFU(High Intensity Focused Ultrasound) monitoring
Audigier C, Kim Y, Ellens N, et al. Physics-based simulation to enable ultrasound monitoring of hifu ablation: An mri validation[C]//International Conference on Medical Image Computing and Computer-Assisted Intervention. Springer, Cham, 2018: 89-97
Method:
Using HIFU to ablate the target tissue
Challenge:
Temperature monitoring
Ablate malignant tissue only
MRI too expensive and not portable
Notes: Just a little bit review about my project. This is HIFU system which use high intensity focused ultrasound to ablate the tissue. The challenage of this system is to monitor the temperature because we want to ablate malignant tissue only while protect healthy ones. Current, MRI is widely used to monitor the temperature however, MRI is very expensive and not portable. Thus, we develop a novel method which uses ultrasound signals to monitor the temperature.

## Slide 3
Data collecting
Notes: This is our experiment setup to collect channel data. It alternates ablation phase and monitoring phase. In ablation phase, all 256 HIFU elements send ultrasound with high intensity. In the monitoring phase, HIFU elements send low intensity ultrasound one by one. All signals are received by MRI compatible probe.

## Slide 4
Data
  Channel data
System alternates ablation phase and monitoring phase
Collect data from monitoring phase
Design neural network to predict temperature image from channel data
Temperature image
Coronal image
Axial image
2 pins are lost in 3rd phase
Notes: This is the data we collected. There are five heating phases and six monitoring phases. In the third monitoring phase, we lost two pins so we use the rest five phases to train the network. Then we design a network to predict temperature form such channel data.

## Slide 5
Network
  Networks
4096 samples
256 HIFU elements
128 receiving elements
ConvLSTM Cell
ConvLSTM Cell
Initial Channel data
Current Channel data
Dense layer
Batch normalization
Reshape
1600 units
Kernel size:(16,16)
Stride:(16,16)
Filters:32
Relu activation
Learning rate:0.0001
Loss:MAE/MSE
Optimizer:Adam
Notes: This is what my network looks like. The input data is a two phases. Each phase is a image whose size is 4096 times 256. Each data set has 128 inputs which corresponding to 128 receiving elements in the probe.

## Slide 6
Network
Problem:
Due to the large size of input, GPU RAM will be out of memory
Solution:
Use first 2048 samples instead of all 4096 samples since important properties like TOF can be extract from first 2048 samples
Use simple network
Enlarge the kernel size and stride of convolution to decrease image size and maintain important information
Data split
Sample 100 probe elements for training set, 10 probe elements for validation set and 18 probe elements for test set
Training set: 100*3*5
Validation set:10*3*5
Test set:18*3*5
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 7
Ultrasound thermometry
MR
thermometry
Difference
10
20
0
10
20
0
20
40
20
0
20
40
20
0
20
40
20
0
20
40
20
0
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
10
20
0
10
20
Phase 1
Phase 2
Phase 3
Phase 4
Phase 5
Coronal Image

## Slide 8
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
Ultrasound thermometry
MR
thermometry
Phase 1
Phase 2
Phase 3
Phase 4
Phase 5
Axial Image
Difference
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40
20
40
0
20
40

## Slide 9
Result
mean error
max error
Coronal image
Axial image
Larger error in axial due to more non zero pixels to predice and irregular shape
Large range shows the difficulty of predicting all images. Many outliers.
The higher the temperature is, the larger the error is.
If use MAE, the mean error is very small but extremely high max error.
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 10
Image to image
Since coronal image is easier to predict than axial image. Is it possible to use the predicted coronal image to generate axial image->Image reconstruction
Previous
network
(20,20,32)
(10,10,64)
(20,20,32)
Use more MRI images to train indenpendentlys
Convolution
Kernel:(5,5,32)
Stride:(2,2)
Transpose
Convolution
Kernel:(5,5.32)
Stride:(2,2)
Convolution
Kernel:(5,5,64)
Stride:(2,2)
Transpose
Convolution
Kernel:(5,5,1)
Stride:(2,2)
Mean error and max error are larger than the network without coronal image
Analysis: Axial images are much more irregular than coronal images. More information is needed to predict.
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 11
Pattern injection
If the diamension of data set is changed, it becomes pattern injection approach where only one element send signal and received by 128 probe elements
42 HIFU elements are available. 30 for train set. 12 for validation set. 12 for test set.
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 12
Network trial 1
  Networks
s
4096 samples
256 HIFU elements
128 42 receiving elements
ConvLSTM Cell
ConvLSTM Cell
Initial Channel data
Current Channel data
Dense layer
Batch normalization
Reshape
1600 units
Kernel size:(16,16)
Stride:(16,16)
Filters:32
Relu activation
Learning rate:0.0001
Loss:MSE
Optimizer:Adam
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 13
Network trial 1--Result
mean error
max error
Coronal image
Axial image
The data capacity is too small
Axial images are still harder to predict.
Result is worse than HIFU approach due to small data capacity.
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 14
Problem
Problem:
The distance of elements in the probe are very small.
Thus, the receiving signals are similar.
There are correlation between train set and test set.
Solution:
Randomly pick 128 HIFU elements from 256 elements each time
The distance of HIFU elements are big and the signals are different.
This can increase the data size and include 3rd phase.
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 15
Random Pick
128 HIFU elements
ConvLSTM
Cell
Initial Channel data
Current Channel data
Position
vectors
+
Reshape
Flatten
Dense
Drop=0.3
Dense
(128,3)
(128,16,32)
(64,16,4)
(40,40)
1600
1600
(40,40,32)
(20,20,64)
(40,40,64)
(40,40,32)
51200
400
Dense
Flatten
Reshape
(20,20)
4480
ConvLSTM
Cell
Input
ConvLSTM
Convolution
FLC
Convolution
FLC
Output
128 receiving elements
2048 signal samples
Relative position between HIFU element and probe element
Learning rate:0.00015
Loss:MSE
Optimizer:Adam
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 16
Axial Image

## Slide 17
Coronal Image

## Slide 18
Coronal image
Axial image
The axial image has larger error than coronal image
The result of randomization approach has larger error than previous approach but more convincible

## Slide 19
Next step
Ultrasound transducer
Tissue
to ablate
Ultrasound
element
Guo, X., Kang, H. J., Etienne-Cummings, R., & Boctor, E. M. (2014). “Active ultrasound pattern injection system (AUSPIS) for interventional tool guidance”. PloS one, 9(10), e104262.
Pattern injection
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 20
Next step
Simulation + deep learning
-
Learn from matlab example and Conduct simulation based on Matlab K-wave simulation tool
Simulate the pattern injection image before ablation and after ablation
Deduct the pattern injection image by the one before ablation
Use ConvLSTM network to train
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 21
Possible network
…
Pattern 1
Pattern 2
Pattern 3
Pattern 4
Pattern 5
Pattern n
ConvLSTM
Cell
ConvLSTM
Cell
ConvLSTM
Cell
ConvLSTM
Cell
ConvLSTM
Cell
ConvLSTM
Cell
CNN
CNN
CNN
CNN
CNN
CNN
+
+
+
+
+
+
Position information
Position information
Advantage
Robust to different tissues
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 22
Previous Dependencies
Dependency | Solution | Alternative | Status
GPU | Thin6 | MARCC | Solved
Machine Learning and data processing packages and Matlab | Open source Acquire Matlab with Hopkins ID | Open source Acquire Matlab with Hopkins ID | Solved
HIFU | Make appoint with hospital to use Sonalleve HIFU | Borrow HIFU from Dr. Boctor | Solved
MRI Room | Make appoint with hospital and ask Xiaoyang to conduct | Use the one in NIH | Solved
Degaser | Borrow from hospital | Borrow from hospital | Solved
US Probe Verasonics | Borrow from Dr.Boctor |  | Solved
Phantom | Ask Younsu for help | Contact Dr. Boctor to buy one | Due Mar 14th
3D Printer | Use the one in Wyman Park | Buy one online | Due Mar 14th
Animals | Ask Dr. Boctor for in vivo pig | ex vivo tissue | Due May 7th
Hospital not available. People in NIH will be back around mid May

## Slide 23
Deliverable update
 | Deliverable | More activity | More deliverable
Min | code written in Python which generate temperature image from channel data Save code and documentation & report on how different parameters and 4 different structures affect performance | Pattern injection approach Writing paper Randomizaiton stradegy | 8 pages Paper for IUS
Expected | Process and test 7 experiments dataset from the HIFU experiment Written report of difference between performance of TOF and channel data | K-wave simulation on matlab for channel data | Report on simulation Code and documentation on simulation
Max | Written report on vivo experiments | Pattern deduction and deep learning Writing paper on pattern deduction approach | Report on patten deduction approach Code and documentation on deep learning
Notes: The solution is HIFU monitoring. Since we use HIFU to ablate, why don’t we use it to monitor at the same time. This is what our setup looks like. There are two phases, first we generate ultrasound focused on the target to ablate it. Then, with function generators and amplifiers, we generate ultrasound signals and received by MRI-compatible PVDF receiver. These signals can help us generate the temperature image. These two phases are conducted one after another. Since ultrasound is a kind of wave, it is able to be received in anywhere else. Thus, we set a receiver on the top to receive these signals, where all signals sent from HIFU can be received. With these raw data, we are able to generate a temperature image and tell doctors whether the tissue has been ablated.

## Slide 24
Previous timeline
Notes: The solution is HIFU monitoring. Since we use HIFU to ablate, why don’t we use it to monitor at the same time. This is what our setup looks like. There are two phases, first we generate ultrasound focused on the target to ablate it. Then, with function generators and amplifiers, we generate ultrasound signals and received by MRI-compatible PVDF receiver. These signals can help us generate the temperature image. These two phases are conducted one after another. Since ultrasound is a kind of wave, it is able to be received in anywhere else. Thus, we set a receiver on the top to receive these signals, where all signals sent from HIFU can be received. With these raw data, we are able to generate a temperature image and tell doctors whether the tissue has been ablated.

## Slide 25
New timeline
I am here
Notes: The solution is HIFU monitoring. Since we use HIFU to ablate, why don’t we use it to monitor at the same time. This is what our setup looks like. There are two phases, first we generate ultrasound focused on the target to ablate it. Then, with function generators and amplifiers, we generate ultrasound signals and received by MRI-compatible PVDF receiver. These signals can help us generate the temperature image. These two phases are conducted one after another. Since ultrasound is a kind of wave, it is able to be received in anywhere else. Thus, we set a receiver on the top to receive these signals, where all signals sent from HIFU can be received. With these raw data, we are able to generate a temperature image and tell doctors whether the tissue has been ablated.

## Slide 26: Question