## Slide 1: Thermal Imaging
Student: Changfan Chen
Mentor: Dr.Emad Boctor Younsu Kim
02/12/2019

## Slide 2
Background
What is one of the most dangerous illness in the world?
Cancer!!
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 3
Background
What do doctors usually do with cancer?
https://www.evanhospital.com/services/surgery/surgery
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 4
Background
New Technology: HIFU(High Intensity Focused Ultrasound)
Video courtesy of Zeal Zone Productions | HIFU Presentation
Notes: Here we have a new technology called HIFU which is high intensity focused ultrasound. The machine is placed at the bottom of a patient and it send ultrasound focused on the tissue to increase the temperature. With the doctors’ operation, the machine ablate different small areas in the tissue and finally ablate all of them.

## Slide 5
Background
  Challenges: Monitoring the ablation
https://www.verywellhealth.com/mri-tips-multiple-sclerosis-2440713
Accurate temperature monitoring
Expensive
MRI is not portable
Patients have contraindication
Advantage
Disadvantage
30 – 45 °C
45 – 60 °C
60 – 75 °C
75 – 88 °C
Before Ablation
During Ablation
Notes: But the challenge is how to know whether the tissue has been ablated or not. We do not want healthy tissues ablated while leave tumour alive. Current solution is using MRI. They put patient into MRI machine. They use HIFU system to ablate the tumour and use MRI to monitor the temperature. The top right picture shows what the tissue looks like before ablation and the bottom right one shows the temperature during ablation. It is obvious that the temperature rises in a certain area.
The advantage of MRI is that it monitor the temperature accurately. It is a mature solution and widely used today.
However, MRI is extremely expensive and it is not portable. MRI is heavy and you need to build a room for this. Also, some patients have contraindiction with MRI. They are afraid of staying there. It makes them uncomfortable.

## Slide 6
Goal
  Design a temperature monitoring tool
Goal
Low-cost
Portable
Easy to use
Notes: So, our goal is to design a machine which is portable, low-cost so that every hospital can afford that. Easy to use so that doctors put more attention on ablating the tissue instead of operating the machine. Also, the image should be high quality and accurate.

## Slide 7
Setup
  Solution: HIFU monitoring
Audigier C, Kim Y, Ellens N, et al. Physics-based simulation to enable ultrasound monitoring of hifu ablation: An mri validation[C]//International Conference on Medical Image Computing and Computer-Assisted Intervention. Springer, Cham, 2018: 89-97
Notes: The solution is HIFU monitoring. Since we use HIFU to ablate, why don’t we use it to monitor at the same time. This is what our setup looks like. There are two phases, first we generate ultrasound focused on the target to ablate it. Then, with function generators and amplifiers, we generate ultrasound signals and received by MRI-compatible PVDF receiver. These signals can help us generate the temperature image. These two phases are conducted one after another. Since ultrasound is a kind of wave, it is able to be received in anywhere else. Thus, we set a receiver on the top to receive these signals, where all signals sent from HIFU can be received. With these raw data, we are able to generate a temperature image and tell doctors whether the tissue has been ablated.

## Slide 8
Setup
US probe, fixed with holder 128 elements
HIFU
256 transmitter
Verasonics
Phantom
Notes: Here is how our experimental setup looks like. We have a HIFU at the bottom which conduct two different phases. Specifically, the first one is to send high intensity ultrasound to ablate the tissue. The second one is to send signals which is received by US probe in order to monitor the temperature in the phantom. The phantom in the middle is made by Younsu and I will learn how to make it before I conduct experiment indenpendently. The top one is US probe which has 128 elements which means we can receive signals from 128 places to get more information.

## Slide 9
Principle
Zhigang Sun and Hao Ying. “A multi-gate time-of-flight technique for estimation of temperature distribution in heated tissue: theory and computer simulation”. Ultrasonics, 37(2):107{122, 1999.
Speed of sound and attenuation depends on temperature
U Techavipoo, T Varghese, Q Chen, TA Stiles, JA Zagzebski, and GR Frank. “Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reected pulses”. The Journal of the Acoustical Society of America, 115(6):2859{2865, 2004.
Notes: The principle of this machine is that speed of sound and attenuation changes with temperature. As is shown in the picture, as the temperature increases, the speed of sound will also increase while decreasing the time of flight. Thus, signals sent with different temperature have different time to reach the receiver. Also, as the temperature increases, the attenuation coefficient will first decrease then increase. So the signal will have different intensity when reaching the receiver.

## Slide 10
Approach
  Machine Learning
Signal
Temperature Image
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 11
Approach
  Networks
Input
CNN
Output
Dense layers
Input
CNN
LSTM
Dense layers
Output
Input
CNN
CNN
LSTM
LSTM
Axial image
Coronal image
1.
2.
3.
4.
Coronal image
Input
CNN
Axial
Dense layers
Coronal
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 12
Approach
  More detail
Loss function: MAE or MSE
CNN: image encoder and decoder
Stride: larger stride to decrease input but too large will loss information
Generalize: Without enough data, add some noise or mistake in the data to increase generalization
Notes: With all signals reached probe, we record it and change it into temperature image with the help of machine learning.

## Slide 13
Dependencies
Dependency | Solution | Alternative | Status
GPU | Thin6 | MARCC | Solved
Machine Learning and data processing packages and Matlab | Open source Acquire Matlab with Hopkins ID | Open source Acquire Matlab with Hopkins ID | Solved
HIFU | Make appoint with hospital to use Sonalleve HIFU | Borrow HIFU from Dr. Boctor | Solved
MRI Room | Make appoint with hospital and ask Xiaoyang to conduct | Make appoint with hospital and ask Xiaoyang to conduct | Solved
Degaser | Borrow from hospital | Borrow from hospital | Solved
US Probe Verasonics | Borrow from Dr.Boctor |  | Solved
Phantom | Ask Younsu for help | Contact Dr. Boctor to buy one | Due Mar 14th
3D Printer | Use the one in Wyman Park | Buy one online | Due Mar 14th
Animals | Ask Dr. Boctor for in vivo pig | ex vivo tissue | Due May 7th

## Slide 14
Timeline and workflow

## Slide 15
Deliverables
Minimum:
Video of comparison between prediction and ground truth
design neural networks for our dataset
Save code and documentation & report on how different parameters and 4 different structures affect performance
Expected:
Process and test 7 experiments dataset from the HIFU experiment
Written report of difference between performance of TOF and channel data
Maximum:
Run the system using ex vivo tissue or in vivo pig
Written report on vivo experiments

## Slide 16
Deliverables and Milestone
Conduct 4 more experiments to collect more data
March 26th
Conduct animal experiment
May 13th
Design network with TOF and finish report of difference
April 26th
March 11th
Design network with help of coronal and axial image and do documentation
Final report written
and video taken
May 13th

## Slide 17
Management
Meeting
Lab meeting: Once a week with Dr. Boctor’lab on Monday or Wednesday
Personal meeting: Meet with Younsu when needed and follow schedule
Data and code
JH Box
MRI help
Xiaoyang Liu, Parag Karmarkar

## Slide 18
Reading List
[1] Kim Y, Audigier C, Ziegle J, et al. Ultrasound thermal monitoring with an external ultrasound source for customized bipolar RF ablation shapes[J]. International journal of computer assisted radiology and surgery, 2018, 13(6): 815-826.
[2] Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
[3] Audigier C, Kim Y, Ellens N, et al. Physics-based simulation to enable ultrasound monitoring of hifu ablation: An mri validation[C]//International Conference on Medical Image Computing and Computer-Assisted Intervention. Springer, Cham, 2018: 89-97.
[4] Audigier C, Kim Y, Boctor E. A Novel Ultrasound Imaging Method for 2D Temperature Monitoring of Thermal Ablation[M]//Imaging for Patient-Customized Simulations and Systems for Point-of-Care Ultrasound. Springer, Cham, 2017: 154-162.
[5] Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
[6] Gers F A, Schmidhuber J, Cummins F. Learning to forget: Continual prediction with LSTM[J]. 1999.
[7] Eilertsen G, Kronander J, Denes G, et al. HDR image reconstruction from a single exposure using deep CNNs[J]. ACM Transactions on Graphics (TOG), 2017, 36(6): 178.