## Slide 1: Seminar Presentation Thermal Imaging
Student: Changfan Chen
Mentor: Dr.Emad Boctor Younsu Kim
03/07/2019

## Slide 2
Background Review
  HIFU monitoring
Audigier C, Kim Y, Ellens N, et al. Physics-based simulation to enable ultrasound monitoring of hifu ablation: An mri validation[C]//International Conference on Medical Image Computing and Computer-Assisted Intervention. Springer, Cham, 2018: 89-97
Notes: The solution is HIFU monitoring. Since we use HIFU to ablate, why don’t we use it to monitor at the same time. This is what our setup looks like. There are two phases, first we generate ultrasound focused on the target to ablate it. Then, with function generators and amplifiers, we generate ultrasound signals and received by MRI-compatible PVDF receiver. These signals can help us generate the temperature image. These two phases are conducted one after another. Since ultrasound is a kind of wave, it is able to be received in anywhere else. Thus, we set a receiver on the top to receive these signals, where all signals sent from HIFU can be received. With these raw data, we are able to generate a temperature image and tell doctors whether the tissue has been ablated.

## Slide 3
Papers
[1]Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865.
[2] Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
[3] Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
This article describes the way to do thermal imaging with HIFU(High Intensity Focused Ultrasound)
This article describes how we can do thermal imaging with deep learning
This article describes how to collect data of speed of sound and attenuation ratio change and inspires us to do thermal imaging with this property
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 4
Why important to project
The ultrasound thermal monitoring is possible using ultrasound physics : SOS(Speed of Sound) and attenuation changes with temperature
It provides more accurate way to plot SoS versus temperature, which can be helpful to conduct experiments
It shows attenuation coefficient works only in some specific cases. Thus, we should rely more on SoS.
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 5
Problem & Goal
Problem
Previous SoS(Speed of Sound) change and Attenuation coefficient measurements are in little change on temperature 20-50 celsius degree
Measurement of SoS and Attenuation coefficient are not conducted simultaneously
Tissues are used repetitively which result the cumulative degradation of the tissue structure
Goal
Measure data in wide and high temperature range
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 6
Technical Approach
Pulse echo transducer
Tissue are heated in the heating bath and test in measurement bath
Signal was transmitted through a tissue sample positioned within a tissue holder and received by a second transducer.
Ultrasound echoses from interfaces were detected by pulse echo transducer
Time of transmitting and receiving are collected as well as amplitude
Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 7
Conclusion & Results
SoS
Plots of mean propagation speed were measured at different temperatures compared to the previous result.
Note that error bars are plus and minus one standard error across different samples
Attenuation Coefficient
Attenuation coefficients were measured at different temperatures for frequency of 4,5 and 6 MHz
Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 8
Conclusion & Results
SoS
Bar plots comparing the SoSin canine liver tissue measured at 37 °C before and after the tissue samples were heated to the elevated target temperatures.
Attenuation Coefficient
Bar plots comparing the attenuation coefficients in tissue measured at 37 °C before and after the tissue samples were heated to the elevated
target temperatures.
Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 9
Conclusion & Results
More conditions are considered and the measurement is more accurate
SoS does not change much after heating and cooling process while attenuation attenuation coefficient changes much. Thus, SoS is better than attenuation coefficient as the parameter to measure temperature
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 10
Good & Bad
Bad
The article does not clarify the challenage of measurement in large and high temperature range as well as the specific solution
The picture is not complete and the article does not clarify the function of Attenuator
No ground truth is provided
Good
The paper consider the property of tissue may change the SoS and attenuation coefficient
The paper made a comparison with graph to show SoS is a better parameter which is clear and convincing
The bar plots are clear to show all information and relationship between experiments
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 11
Inspiration
We can make full use of change of SoS to design the network and monitor the temperature change in HIFU experiment
The initial status before ablation is important information to measure the temperature thus the network should include the initial status
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 12
Papers
[1]Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865.
[2] Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
[3] Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
This article describes the way to do thermal imaging with HIFU(High Intensity Focused Ultrasound)
This article describes how we can do thermal imaging with deep learning
This article describes how to collect data of speed of sound and attenuation ratio change and inspires us to do thermal imaging with this property
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 13
Problem & Goal
Problem
Using MRI to monitor temperature is expensive and not portable
Some people feel uncomfortable in MRI room
Goal
Design a novel method for HIFU monitoring with ultrasound signal
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 14
Why important to project
It provides a novel method and experiment to generate temperature image from ultrasound signals.
It provides the derivation of generating temperature from collected time of flight, where the network can learn from.
It provides SoS versus temperature which can be reference.
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 15
Technical Approach
128 US elements transmitting US pulses in heating phases and monitoring phases
The pulses going through ablation zone and propagating to the opposite where TOF(Time of Flight) is collected.
Using TOF and position of elements to derive the temperature
Setup
Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 16
-- p Position of the receiver
-- Position of the ith HIFU element
-- The speed of sound in room temperature
-- Time of Flight of ith HIFU element
How to know the length
Technical Approach
Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 17
Technological Approach
How to know the SOS of one voxel
Subject to
--S The intersection lengths of traversing paths through each voxel in the ROI(Reagion of Interest)
--x Inverse of the local SOS in each voxel
shows the TOF of inner layer is smaller of TOF of outer layer
shows the TOF of same layer is equivalent
shows the range of SoS
Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 18
Intuition
SoS is measured by conducting experiment. Two elements are put on two sides of phantom to transmit and receive signal. Thus, TOF and length are acquired. We can derive the SoS through TOF and length.
Technical Approach
Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 19
Technical Approach
Three identical HIFU ablations were performed sequentially at the same location. Each one has 10s heating phases and 24 seconds monitoring.
The first ablation was performed under MR monitoring, the second one with a set of 64 elements used for monitoring, the third one with another set of 64 elements.Wait long enough to cool down so that three data set are acquired simultaneously.
Time of trigerring and receiving is recorded to know TOF.
Data with low SNR(signal noise ratio) is removed.
24 Images(one per second) from simulation as well as MRI images are averaged
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 20
Conclusion & Results
Coronal and axial images at three increasing ablation times are generated.
The temperature in ROI in coronal plane was 1.1,1.3 and 1.3 Celsius degrees on average with a maximum difference of 3.0,4.1 and 3.8 Celsius degrees.
Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 21
Conclusion & Results
The monitoring phase is too long and averaging them provides less accurate information.
The location of ultrasound elements affects the monitoring accuracy. The result could be further improved by adjusting the location of the elements. The number of elements could be increased.
The method is novel and proved to be feasibility.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 22
Good & Bad
Bad
The paper only shows the result of one experiments. More experiments results and analysis are preferred.
The notation of how to reconstruct SOS image is not clear. is not clarified.
Good
Discussion part is very inspiring and proposed a lot of method to improve the result and experiments.
The paper clearly shows how the SOS image is generated mathmatically.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 23
Inspiration
Number of elements can be increased to provide more useful information.
Position of elements can be changed to be generalized.
The initial status is provided to network to learn position of elements and SoS of background.
The temperature image can not only be determined on current information since SoS will first increase then decrease as temperature increases.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 24
New in my project
Deep learning are used to generate temperature image instead of modeling method.
The speed of triggering the elements is improved which provides more information before the phantom cooling down. The predicting result would be improved.
All the information is collected instead of TOF only.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 25
Papers
[1]Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865.
[2] Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
[3] Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
This article describes the way to do thermal imaging with HIFU(High Intensity Focused Ultrasound)
This article describes how we can do thermal imaging with deep learning
This article describes how to collect data of speed of sound and attenuation ratio change and inspires us to do thermal imaging with this property
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 26
Why important to project
It provides idea of collecting data by simulation, which will significantly improve data size.
It provides reasonable structure of deep learning like image reconstruction.
It provides some experience and skills to design the network.
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 27
Problem & Goal
Problem
Due to few element number, the collected TOF is sparse
Temperature image accuracy depends highly on element location
Goal
Design a CNN(Convolutional Neural Network) with data from simulation
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?

## Slide 28
Technical Approach
The input for the network is a concatenated vector of the ToF acquired before ablation and the ToF shifts during HIFU procedure.
TOF shift is amplified since it is too small compared with TOF.
Ground truth is the MRI image.
Several fully connected layers expands the input to match the output size.
Convolutional layer and transposed convolutional layer is to extract features and reconstruct image.
Learning rate is 10e-4
Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 29
Conclusion & Results
mean errors and maximum errors between the reconstructed images and the ground truth images.
The worst case was a reconstructed image showing a maximum difference of 3.22 C.
Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 30
Conclusion & Results
Deep learning method and CSRM method are compared. Four different locations of external element and their performace are recorded as P1,P2,P3,P4
Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 31
Good & Bad
Bad
The paper does not clarify the reason why the TOF shift is included in the paper and the two phases of shift.
The paper does not clarify what parameters are included in simulation.
Good
Illustrate the structure of network and the function of each layer.
The result of deep learning network and previous method is compared within different location of ultrasound element which helps to generalization.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 32
Inspiration
Image reconstruction can be used in the design of deep learning network to extract features and generate image.
Due to limition of data, the network is highly possible to overfit. The network should prevent it.
More data can be acquired in simulation. However, simulation data is not robust to noise.
Part of input can be amplified if they are too small.
In this approach, it uses time of flight only. If we use the entire channel data, then we may reconstruct more accurately with real data.
Notes: What do doctors usually do with cancer?
They perform a surgery on patients. They cut into body and excise the tumour. However, such a surgery will leave a permanent scar and great pain on patient.

## Slide 33
My Project
  Channel data
Amplitude
samples
sample
HIFU element number
256 signals all together
Signal of one element
Some cluster because of reflection inside the probe or ringing effect
Different amplitude is due to different distance and attenuation coefficient
Amplitude
Notes: The solution is HIFU monitoring. Since we use HIFU to ablate, why don’t we use it to monitor at the same time. This is what our setup looks like. There are two phases, first we generate ultrasound focused on the target to ablate it. Then, with function generators and amplifiers, we generate ultrasound signals and received by MRI-compatible PVDF receiver. These signals can help us generate the temperature image. These two phases are conducted one after another. Since ultrasound is a kind of wave, it is able to be received in anywhere else. Thus, we set a receiver on the top to receive these signals, where all signals sent from HIFU can be received. With these raw data, we are able to generate a temperature image and tell doctors whether the tissue has been ablated.

## Slide 34
Reference
[1]Techavipoo U, Varghese T, Chen Q, et al. Temperature dependence of ultrasonic propagation speed and attenuation in excised canine liver tissue measured using transmitted and reflected pulses[J]. The Journal of the Acoustical Society of America, 2004, 115(6): 2859-2865.
[2] Kim Y, Audigier C, Ellens N, et al. A novel 3D ultrasound thermometry method for HIFU ablation using an ultrasound element[C]//2017 IEEE international ultrasonics symposium (IUS). IEEE, 2017: 1-4.
[3] Kim Y, Audigier C, Ellens N, et al. Low-Cost Ultrasound Thermometry for HIFU Therapy Using CNN[C]//2018 IEEE International Ultrasonics Symposium (IUS). IEEE, 2018: 1-9.
Notes: Let me ask you a question. What is one of the most dangerous illness in the world?
Cancer is one of them, right?