## Slide 1: Material Decomposition using Dual-Energy X-ray of the nView System
Team Member: Cong Gao (cgao11@jhu.edu)
Mentors: Mathias Unberath, Mehran Armand, Russ Taylor
Group 17

## Slide 2
Motivation
Standard X-ray imaging brings difficulty for surgeons to identify ROI features from anatomical clutter.
Dual-energy X-ray enables anatomical clutter reduction via material decomposition
Fig 1. Illustration of material decomposition[1].
[1] Slide: Dual energy imaging and digital tomosynthesis: Innovative X-ray based imaging technologies, University of Toronto

## Slide 3
Motivation -- Femoroplasty
Decompose femur and cement during femoroplasty. (Femoroplasy: femur operation for reducing fracture risk in patients with severe osteoporosis.)
Decomposed frames can be used to improve 3D reconstruction of the injected cement, to better understand the cement distribution during injection
[2] Otake, Yoshito, et al. "An image-guided femoroplasty system: development and initial cadaver studies." Medical Imaging 2010: Visualization, Image-Guided Procedures, and Modeling. Vol. 7625. International Society for Optics and Photonics, 2010.

## Slide 4
Physics Background
: Measurement of X-ray detector at 2D coordinate
: Spectrum probability of photon energy at energy
: Delta function to identify material at 3D coordinate
: Material and energy dependent linear attenuation coefficient
: Material density
: X-ray casting length
Notes: This formula is the physics model of X-ray detector. m(u) is the measurement of detector

## Slide 5
Physics Background
In the case of 2 materials
: low energy; high energy
: Material 1; Material 2
: unknowns
Notes: We can then try to compose the items to a simple expression.
This integral is basically the thickness of material corresponding to each 2D pixel. We name it T(u)
The other part is the coefficient depending on spectrum and attenuation parameters.
Then we have this linear equation, where L and H mark the energy, number 1 and 2 mark the material type. T(u) is our unknown.

## Slide 6
Coefficient Calculation
Tungsten anode
3mm Aluminum filtration
+ 0.5mm copper filtration
60kV and 75kV

## Slide 7
Coefficient Calculation
https://www.nde-ed.org/EducationResources/CommunityCollege/Radiography/Physics/attenuationCoef.htm
Notes: The attenuation coefficient is measured and published by an online resource center.

## Slide 8
Coefficient Calculation
: 1d linear interpolation between spectrum and attenuation.
spectrum
attenuation

## Slide 9
Least Square Solution
Least Square solution for each :
Notes: Here, I want to introduce physics behind dual-energy solution. N0 is the number of photons emitting from the source, and N is how many photons the detector receives, and they are related to the attenuation u and material thickness T. In ideal case, we don’t include noise, and we do log measurement, we will get a linear system for 2 materials, which means analytical solution exists if only including 2 materials.

## Slide 10
Data Acquisition
Femoroplasty experiment with the nView system
Set high energy: 75kV, low energy: 60kV
125 X-ray frames/shot, with 3D reconstruction

## Slide 11
Data Acquisition
nView X-ray image (low energy)
Dual Energy Histogram

## Slide 12
Least Square Output
Negative problem,
Violates physical constraints

## Slide 13
Constrained Least Square Solution
Least Square solution for each :
constrained to

## Slide 14
Constrained Least Square Output
Signal appears, but sparse

## Slide 15
Problem of Least Square Solution
Model is simple, noise is not included
Solution is pixel-wise, no spatial information
Improved Optimization model:
Non-negative constraint
Regularization term
(noise & spatial information)

## Slide 16
Simulation Study
DeepDRR Framework: Simulate X-ray images from CT data
Fig. DeepDRR Framework[3]
[3] Unberath, Mathias, et al. "Deepdrr–a catalyst for machine learning in fluoroscopy-guided procedures." International Conference on Medical Image Computing and Computer-Assisted Intervention. Springer, Cham, 2018.
Femur CT Image
Notes: DeepDRR, a network framework that could segment materials in 3D from CT scans, and combining scatter and noise, which lead to high-quality simulations to the real X-ray images.

## Slide 17
Simulation Study
Cement model
Femur CT
DRR Projection
+ Poisson Noise[4]
[4] Zhang, H., Ouyang, L., Ma, J., Huang, J., Chen, W., Wang, J.: Noise correlation in cbct projection data and its application for noise reduction in low-dose cbct. Medical physics 41(3) (2014)
Simulation DRR Effect
Notes: DeepDRR, a network framework that could segment materials in 3D from CT scans, and combining scatter and noise, which lead to high-quality simulations to the real X-ray images.

## Slide 18
Our Original proposal
Build end-to-end prediction framework
Dual-energy
Acquisitions
❗️
Deep Network
Decomposition
Result
End-to-end prediction will likely overfit to training data
Exclude physical constraints at optimization stage
Problem:

## Slide 19
Modified Approach
Training Phase:
Discriminator
Decomposition
Groundtruth
Generator
Generator
Result
Loss
Model the probability of
Dual-energy
Acquisitions
Constrained Least
Square Solution
Least Square
Result
Initialization
Least Square
Result
Cycle Consistency Loss

## Slide 20
Modified Approach
Dual-energy
Acquisitions
Constrained Least
Square Solution
Least Square
Result
Least Square
Result
Inference Phase:
Discriminator
Freeze the weights
Improved optimization model:
Everything is differentiable, enabling gradient descent search for T
Loss
Model the probability of
Initialization

## Slide 21
Deliverables
Minimum
Expected
Maximum
X-ray simulation software using DeepDRR framework from femur CT data
simulation
algorithm
Deep Network software
Validation
Processed data & Validation result from real bone injection experiment
Documentation
Final Report of algorithm description, simulation & validation results
simulation
algorithm
Validation
Documentation
X-ray simulation software with cement/metal simulation
Deep Network software with workable architecture
Processed data & Validation result of cement injection dataset
Final Report of algorithm description, simulation & validation results
simulation
algorithm
Validation
Documentation
X-ray simulation software with cement/metal simulation, improvement of noise, scattering modeling, well fit nView system effect
Deep Network software with well-performed architecture and generalization ability
Real time cement monitoring using the nView system
Final Report of algorithm description, simulation & validation results
In Progress
In Progress
In Progress

## Slide 22
Dependencies
 | Dependency | Solution | Alternative | Status
1 | Deep DRR software | Contact Dr. Unberath | X | Solved
2 | Real Femur CT Data before & after injection | Contact Amir. Farvardin | Contact BIGSS/CAMP lab | Solved
3 | Access to the nView system | Contact Dr. Armand | X | Solved
4 | nView system useage training | Contact Singchun Lee, watch the nView training video | Contact the nView team | Solved
5 | Femur injection experiment | Schedule with Dr. Armand | X | Solved
6 | Computation Resource | Desktop from BIGSS lab | MARCC | Solved
7 | Feedback from instructors | Attend group/personal meeting | X | Solved
8 | More separate nView energy data | Contact nView people Modify the configuration file | X | In Progress

## Slide 23
Milestones
Project Proposal & kick-off
nView system bone injection experiment
Finish simulation software and simulation dataset
Finish network design for 2 materials, get simulation result
Finish network design for multiple materials, get simulation result
Test on real dataset, get validation result
✅
✅
❗️
❗️
Mid March
End March
Mid April
End April
End February
✅
In Progress