## Slide 1: Evaluation of Various Sensing Modalities for Accurate Measurement of Neck Flexion Angle during Thyroid and Ear Surgery
Team Member : Zhen Hu, Hanqing Duan
Mentor: Dr. Russell Taylor, Dr. Deepa Galaiya
CIS II Project

## Slide 2: Project Review
Last week:
Finish processing the calibration data
Finish processing the Mock OR data

## Slide 3: Calibration Data
The measurement result from EM tracker | The measurement result from IMU 1A | The measurement result from IMU A6
3.8810 | 4.1524 | 3.8791
15.5105 | 15.8083 | 15.3880
26.6346 | 27.6527 | 27.6778
32.6116 | 33.3907 | 33.4102
37.8730 | 38.5087 | 38.4184
42.1996 | 42.6490 | 42.52
45.7238 | 46.0262 | 45.8209
48.4941 | 48.6611 | 48.4686
50.2905 | 50.4428 | 50.2339
52.8936 | 53.3970 | 53.1683

## Slide 4: Calibration Result: A6
Linear Regression

## Slide 5: Calibration Result: 1A
Linear Regression

## Slide 6: Mock OR data analysis
Method:
For standard case:
Average quaternion from two IMUs separately when surgeon stands.
For every other cases:
1. Calculate the angle between the quaternion from IMU-A6 and the quaternion in standard case;
2. Calculate the angle between the quaternion from IMU-1A and the quaternion in standard case;
3. Use the linear regression function to do the calibration;
4. Calculate the difference angle between two calibrated angles from IMU-A6 and IMU-1A.

## Slide 7: Traditional Case
Most angles are in the the range: (5,13) degree

## Slide 8: Endoscopic Case
Most angles are in the the range: (-10,10) degree

## Slide 9: When Head turn left
Question: This kind of movement will also influence our pitch angle result. How could we minimize this influence?

## Slide 10: When Head Up and Down

## Slide 11: When Head Rotate to Left