## Slide 1: Detection and Guidance of K-Wire Placement in Pelvic Trauma Surgery
Team: Kinjal Shah and Irina Bataeva
Mentor: Dr. Ali Uneri
CIS2 Project
May 5, 2020

## Slide 2
Motivation: K-wires in Pelvic Trauma Surgery
Motivation: Improve accuracy of K-wire detection to reduce injury while limiting radiation exposure
Objective: Use deep learning methods to:
(1) Detect K-wires in 2D radiographs of the pelvis
(2) Localize their 3D pose to provide surgical navigation
J. Goerres, et al."Deformable 3D-2D registration for guiding K-wire placement in pelvic trauma surgery", Proc. SPIE 10135, Medical Imaging 2017: Image-Guided Procedures, Robotic Interventions, and Modeling, 101350A (3 March 2017);

## Slide 3
Approach
Simulated Dataset Generation
Training of Neural Network
Images
Weights
Perform Prediction on Test Dataset
Manually annotated labels
Output
Prediction Results
[1]
[1] Ronneberger, Olaf, et al. “U-Net: Convolutional Networks for Biomedical Image Segmentation.” Lecture Notes in Computer Science Medical Image Computing and Computer-Assisted Intervention – MICCAI 2015, 2015, pp. 234–241., doi:10.1007/978-3-319-24574-4_28.
Analysis of workflow performance

## Slide 4: Dataset Generation: Transfer Learning
uint16
976 × 976
×25 Data Augmentation
Rotation
Translation
Scaling
Noise
uint16
960x960
Per Image
×1 K-wire
Simulation
uint16
960x960
CLAHE
Radiograph
Label Map
uint8
960x960
8-bit
Conversion
Training Data Set
Pelvis Radiographs
=80
Label Map
Radiograph
uint16
960x960
Crop
Down-
Sample
uint8
224x224
Access to quality, annotated training datasets remains a pain point for deep learning based medical image analysis
We propose a transfer learning approach based on fully simulated training data

## Slide 5: Dataset Generation: Transfer Learning
uint16
976 × 976
×25 Data Augmentation
Rotation
Translation
Scaling
Noise
uint16
960x960
Per Image
×1 K-wire
Simulation
uint16
960x960
CLAHE
Radiograph
Label Map
uint8
960x960
8-bit
Conversion
Training Data Set
Pelvis Radiographs
=80
Label Map
Radiograph
uint16
960x960
Crop
Down-
Sample
uint8
224x224
Access to quality, annotated training datasets remains a pain point for deep learning based medical image analysis
We propose a transfer learning approach based on fully simulated training data
Augmentation of Real Cadaver Radiographs
1

## Slide 6: Dataset Generation: Transfer Learning
uint16
976 × 976
×25 Data Augmentation
Rotation
Translation
Scaling
Noise
uint16
960x960
Per Image
×1 K-wire
Simulation
uint16
960x960
CLAHE
Radiograph
Label Map
uint8
960x960
8-bit
Conversion
Training Data Set
Pelvis Radiographs
=80
Label Map
Radiograph
uint16
960x960
Crop
Down-
Sample
uint8
224x224
Access to quality, annotated training datasets remains a pain point for deep learning based medical image analysis
We propose a transfer learning approach based on fully simulated training data
K-wire Simulation
2

## Slide 7: Dataset Generation: Transfer Learning
uint16
976 × 976
×25 Data Augmentation
Rotation
Translation
Scaling
Noise
uint16
960x960
Per Image
×1 K-wire
Simulation
uint16
960x960
CLAHE
Radiograph
Label Map
uint8
960x960
8-bit
Conversion
Training Data Set
Pelvis Radiographs
=80
Label Map
Radiograph
uint16
960x960
Crop
Down-
Sample
uint8
224x224
Access to quality, annotated training datasets remains a pain point for deep learning based medical image analysis
We propose a transfer learning approach based on fully simulated training data
Post-Processing
3

## Slide 8
Training Dataset Generation: Examples
AP-like views
Single K-wire
Image sizes:
960x960
480x480
224x224
Dataset sizes:
250
500
1000
2000
4000
K-wire projection:
Deformed
Rigid

## Slide 9
Test Dataset
7 Single
Raw Test Dataset:
Image Size: 976x976
7 Single K-wire Images
13 Multiple K-wire images
Test Dataset:
Image Size: 960x960
33 Single K-wire Images
IRB Approved Dataset
Acquired using Cios Spin (Siemens, Erlangen Germany)
AP-like views, single K-wire
Split based on Mask
13 Multiple
26 Single

## Slide 10: Figures of Merit: Standard CNN Prediction Metrics
Area under the Curve
Precision
Recall
F1 Score (Sørensen–Dice coefficient)
 |  | Ground Truth | 
 |  | P | N
Prediction | P | TP | FP
 | N | FN | TN

## Slide 11: Figures of Merit: Standard CNN Prediction Metrics
Area under the Curve
Precision
Recall
F1 Score (Sørensen–Dice coefficient)
 |  | Ground Truth | 
 |  | P | N
Prediction | P | TP | FP
 | N | FN | TN

## Slide 12: Figures of Merit: K-Wire Detection Task Specific
Binarize (>0.1) and Dilate
Connected-component labeling
Threshold by area
(>4px)
Skeletonize
Identify K-wire component based on Hausdorff distance
(<7mm)
Prediction
Weighted Hausdorff distance based on the object’s area
Ground Truth
Skeletonize
Percentage of length of the centerline detected
Centerlines
Predicted K-wire Centerline
Input Image
K-wire Centerline

## Slide 13: Training Time
Training Dataset Size: 2000
Batch Size: 10
Epoch: 80
Image Size: 224x224
Binary Cross-Entropy Loss Function

## Slide 14: Training Dataset Size
General improvement as training dataset size increases
Training Dataset Size: 250–4000
Batch Size: 10
Epoch: 80
Image Size: 224x224

## Slide 15: Training Dataset Size
Recall improvement is of particular interest
Hope to see false negatives decrease
Training Dataset Size: 250–4000
Batch Size: 10
Epoch: 80
Image Size: 224x224

## Slide 16: Training Dataset Size: Centerline Metrics

## Slide 17
Prediction Examples

## Slide 18
Prediction Examples

## Slide 19: Image Resolution
Marginal improvement in performance
*need larger test set and statistical analysis to assess
Training Dataset Size: 2000
Batch Size: 4
Epoch: 80
Image Size: 224 vs. 480 px

## Slide 20
Performance is essentially equivalent
Training Dataset
Simulated K-Wire Shape
Training Dataset Size: 2000
Batch Size: 10
Epoch: 80
Image Size: 224x224

## Slide 21
Increased diversity in background images prior to augmentation yields better results
Training Dataset:
Diversity of Background Image Selection
Training Dataset Size: 2000
Batch Size: 10
Epoch: 80
Image Size: 224x224

## Slide 22
Displayed comparison
UNet to UNet++
UNet++: more complex network
~2x the inference time / image
Similar performance
CNN Architectures
Training Dataset Size: 250–4000
Batch Size: 4
Epoch: 80
Image Size: 224x224

## Slide 23: Summary
Generated simulated dataset
Trained and evaluated application of UNet for K-Wire detection
Achieved predictions on real pelvic images from real patient experiments
Minimum Deliverable
Expected Deliverable
Irina Bataeva | Kinjal Shah
Training Set Generation: K-wire simulation Test Set Segmentation Model Evaluation: Task Specific Metrics | Training Set Generation: Dataset augmentation Model Implementation Model Evaluation: Standard CNN Metrics
Responsibility Ownership

## Slide 24: Next Steps
Improve Transfer Learning
Refine dataset generation process
Assess alternate model architectures
Multiple K-Wires
Multi-class segmentation, object detection
3D Localization
Multi-class segmentation
Maximum Deliverable

## Slide 25: Questions
Thank you!

## Slide 26: Appendix: Prediction Example
Ideal Case
Failure Case
Input Image
Prediction
Ground Truth
Input Image
Prediction
Ground Truth

## Slide 27: Appendix: Prediction Example (4000 image training dataset) – Image crop issue

## Slide 28: Appendix: Prediction Example (4000 image training dataset) – Failure