## Slide 1: Robot System Control for Automating Mosquito Microdissection
Team Member: Zhuohong (Zooey) He zhe17@jhu.edu
Mentors: Dr. Simon Leonard sleonard@jhu.edu
Dr. Russell Taylor rht@jhu.edu
Industry Partners: Dr. Kim Lee Sim Sanaria Inc.
Sumana Chakravarty Sanaria Inc.
Date: March 3rd, 2021
**The information in this presentation is strictly confidential
Group 03: Paper Review

## Slide 2: Reviewing the CIS II Project
**The information in this presentation is strictly confidential
Robot Control for Mosquito Dissection

## Slide 3: Project Summary
Problem: Sanaria needs to increase the production rate of Plasmodium falciparum sporozoites (PfSPZ) from infected mosquito glands to help produce a promising malaria vaccine.
Overall Goal: Automate the gland dissection process using a robot system. Our goal is to dissect 600 mosquitoes per hour (mph).
CIS Project Goal: To develop a robot system control algorithm that introduces parallel processes, error checking, and error recovery.
**The information in this presentation is strictly confidential
Robot Control for Mosquito Dissection

## Slide 4: Robot System Concept
Main Concept: Nodes surrounding a turntable
Components:
Turntable Node – convey mosquitoes from node to node.
Robot & Decapitate Node – drag mosquito between blades and decapitate.
Extraction Node – squeeze mosquito to extrude salivary glands, extract glands.
Cleaning Node – clean of mosquito body.
**The information in this presentation is strictly confidential

## Slide 5: Paper Summary
** All media used in this section are from the paper **
**The information in this presentation is strictly confidential
Robot Control for Mosquito Dissection

## Slide 6: Paper Selection Motivation
Previous iteration of our current system.
Discussed the design of a serial robot system for mosquito dissection which can analyze to inform the design of our parallel system.
Discussed a simulator which would be useful for testing.
There are few papers in this area of research, this paper is the most relevant.
Li, W., He, Z., Vora, P., Wang, Y., Vagvolgyi, B., Leonard, S., Goodridge, A., Iordachita, I., Hoffman, S., Chakravarty, S., & Taylor, R. (in press). Automated Mosquito Salivary Gland Extractor for PfSPZ-based Malaria Vaccine Production. 2021 IEEE International Conference on Robotics and Automation (ICRA).
**The information in this presentation is strictly confidential

## Slide 7: Introduction & Background
Key Concepts:
Malaria is significant
  228 million cases; 405,000 deaths in 2018
  Vaccines are a long term solution to curb spread
  Sporozoite lies in salivary glands.
Sanaria is working on increasing production
  Manual gland extraction is a labor intensive step (290 mph)
  Semi-autonomous system (sAMMS) increases extraction speed (450 mph)
Figure 1. Malaria Life Cycle
**The information in this presentation is strictly confidential

## Slide 8: System Overview
Automation Procedure:
Mosquito placed in loading area
Turntable introduces a mosquito in front of robot
Robot places mosquito on the linear stage
Decapitate the mosquito
Move stage to squeezing station
Squeeze the mosquito body to extrude saliva gland.
Figure 2. Actual System
Figure 3. System Diagram
**The information in this presentation is strictly confidential

## Slide 9: System Overview (Video)
Automation Procedure (Video)
**The information in this presentation is strictly confidential

## Slide 10: Software Design Specifics
The controller is designed using Robot Operating System (ROS).
Communication occurs on topics.
ROS ActionLib client-service paradigm allow for robust communication and connection to simulation.
Figure 4. Action Client/Service
Figure 5. Serial Controller Diagram
**The information in this presentation is strictly confidential

## Slide 11: Simulation
Simulation of each component is visualized using the Robot Visualization tool (RViz)
Each simulation node acts as another server which listens to controller client commands.
GUI built using RQt.
Trajectory Generator nodes simulate the real robot physics
Figure 6. (a) Simulation ROS Architecture, (b) Simulation GUI, (c) RViz 3D Visualization

## Slide 12: Results
Experiments were conducted on 100 real mosquitoes to determine the success rate of each step in dissection.
Table 1. Quantitative Evaluation Results

## Slide 13: Discussion
The system produced an overall success rate of 81% demonstrating the potential for automated mosquito dissection.
Decapitate had strong performance (100%)
Pick-and-Place (93%) and Gland Extraction (87.1%) are the weakest which could be improved by redesigning, improving CV, or adding error recovery.
Stiff mosquitoes caused many failures. Need improved method to keep mosquitoes fresh and nimble.
Still need gland storage and automated cleaning stations.

## Slide 14: Discussion
Removing Linear Stage Time (47s):
Adding parallelization and error recovery, could result in even faster speeds.
Figure 7. Experiment Timing Analysis (** this figure is not included in paper)
**The information in this presentation is strictly confidential

## Slide 15: Key Lessons
The stations are all effective, but can be improved from both the hardware and controller aspects.
System centered around turntable could improve times by removing the time of the linear stage.
Error recovery is most needed on the pick-n-place and extraction stations.
Parallelization of stations could further improve the throughput rate.
ActionLib Client-Server architecture is effective for our controller.
The RViz simulation is a great resource for debugging and development.
Figure 8. Improvements to system after work in paper

## Slide 16: References
[1] Li, W., He, Z., Vora, P., Wang, Y., Vagvolgyi, B., Leonard, S., Goodridge, A., Iordachita, I., Hoffman, S., Chakravarty, S., & Taylor, R. (in press). Automated Mosquito Salivary Gland Extractor for PfSPZ-based Malaria Vaccine Production. 2021 IEEE International Conference on Robotics and Automation (ICRA).
[2] M. Schrum, A. Canezin, S. Chakravarty, M. Laskowski, S. Comert, Y. Sevimli, G. S. Chirikjian, S. L. Hoffman, and R. H. Taylor, “An efficient production process for extracting salivary glands from mosquitoes,” 2019, arXiv:1903.02532 [q-bio.QM]. [Online]. Available: https://arxiv.org/abs/1903.02532
**The information in this presentation is strictly confidential
Robot Control for Mosquito Dissection

## Slide 17: Thank You
Any Questions?
Robot Control for Mosquito Dissection