## Slide 1: Group 10: Cross Modality Medical Image Synthesis and Registration through Machine Learning
Team member: Ping-Cheng Ku (pku1@jh.edu)
Mentors: Mehran Armand, Alejandro Martin Gomez
Paper Presentation

## Slide 2: Project recap - Background
Core Decompression for Osteonecrosis
  Drilling several holes into the femoral head to relieve pressure in the bone and create channels for new blood vessels to nourish the affected areas of the hip
  X-rays provides images of dense structures (like bones) and intraoperative x-ray shots are taken to monitor the surgical procedure.
Image source (Left and right image): [1] orthoinfo - aaos. Retrieved February 16, 2021

## Slide 3: Project recap - Project Goal
Motivation
  Surgeons also rely on preoperative MR scans for tool trajectory planning for core decompression surgery, but there is no easy way for them to visualize the planned paths in the intra-operative X-ray shots
Project Goal
  We would like to convert the annotations of segmentation of the necrotic tissues and the drill insertion paths from preoperative MR images to intraoperative x-rays would be helpful for surgeons.
Image source (Left and right image): [1] orthoinfo - aaos. (n.d.). Retrieved February 16, 2021

## Slide 4: Paper Overview
Introduction of gradient consistency loss to CycleGAN loss functions to improve the boundaries in synthesized images
Accuracy of synthesized images was investigated by adjusting the number of training data and the implementation of gradient consistency loss
Cross-modality image synthesis from unpaired data using CycleGAN: Effects of gradient consistency loss and training data size
Yuta Hiasa, Yoshito Otake, Masaki Takao, Takumi Matsuoka, Kazuma Takashima, Jerry L. Prince, Nobuhiko Sugano, Yoshinobu Sato

## Slide 5: Paper: Background
CT is commonly used in orthopedic procedures, while MRI is used along with CT to identify muscle structures and diagnose osteonecrosis due to its superior soft tissue contrast [1].
Image synthesis has been performed through patch-based learning [2] as well as deep learning, including convolutional neural networks (CNN) and generative adversarial networks (GAN).
Previous CycleGAN approaches focus on more consistent field-of-view (FOV), while the entire hip region has larger variation in the anatomy and the pose.

## Slide 6: Paper: Dataset
302 unlabeled MR volumes
  T1-weighted
  matrix size: 256×256
  field of view: 320×320 mm
  slice thickness: 2 mm
613 unlabeled + 20 labeled CT volumes
  matrix size: 512×512
  field of view: 360×360 mm
  slice thickness: 2mm
MR
dataset
CT
dataset
Image reference: [2] Y. Hiasa
Image reference: [1] Y. Hiasa

## Slide 7: Paper: CycleGAN Workflow
Generator networks
  : translates MR to CT
  : translates CT to MR
Discriminator networks
  : distinguish real and fake MR
  : distinguish real and fake CT
Loss functions
  , : adversarial losses
  : cycle consistency loss
  : gradient correlation loss
Image reference: [2] Y. Hiasa

## Slide 8: Paper: CycleGAN loss
Adversarial losses
  Generators create synthesized images, while the discriminators attempt to distinguish between the real and synthesized images by maximizing the adversarial losses
Cycle consistency loss
  Compare the real image and the reconstructed images from synthesized images
  Prevent convergence where generators creates same set of images
: Input CT
: Input MR
: Input CT
: Input MR

## Slide 9: Paper: Gradient consistency loss
Gradient correlation (GC) is a similarity metric in medical image registration. The value is defined to be the normalized cross correlation (NCC) between two images.
Gradient consistency loss is formulated as:
Overall loss function:

## Slide 10: Paper: Evaluation method
Variable: Training dataset size
  20 MR volumes + 20 CT volumes
  302 MR volumes + 613 CT volumes
Variable: Implementation of gradient consistency (GC) loss
  with GC loss implemented
  without GC loss implemented
Evaluation methods:
  Data with ground truth (paired CT and MR images):
    mean absolute error (MAE)
    peak-signal-to-noise ratio (PSNR) [dB] (increases when mean squared error decreases)
  Data without ground truth:
    Mutual Information (MI)
  Quantitative evaluation on segmentation

## Slide 11
Paper: Results
MAE and PSNR:
  Average MAE decreases and PSNR increases when there are more training volumes and when GC is implemented
Mutual information (MI):
  Increased training data and implementation of GC both yield improvements
Image reference: [2] Y. Hiasa

## Slide 12: Paper: Results
With gradient consistency loss implemented, the shape of the femoral head and the adductor muscles would be more likely preserved.
Image reference: [2] Y. Hiasa

## Slide 13: Paper: Results
Quantitative evaluation on segmentation
Image reference: [2] Y. Hiasa

## Slide 14: Paper: Conclusions
Main contributions:
  introduction of gradient consistency loss in CycleGAN
  quantitative and qualitative evaluation of the dependency of both image synthesis accuracy and segmentation accuracy on a large number of training data
Future work:
  patients with implants are excluded in the dataset for the cycleGAN training
  development of a method that effectively incorporates information in unlabeled CT and MR volumes to improve segmentation accuracy

## Slide 15: Paper: Critiques
Good:
  Clearly explained model and clear math for all the loss functions involved
  Made full use of available data (paired/unpaired volumes and few labeled volumes) to provide quantitative and qualitative evaluation of the results
Bad:
  Effect of implementation of GC loss is not significant. The balancing weights for GC loss was set to a constant throughout the paper.
  No publicly available code implementations, which may be difficult for researchers to reproduce the results

## Slide 16: Paper: Relevance to project
Understanding the loss functions involved in CycleGAN
Provides insights to modification of network losses
Understanding the evaluation and testing methods

## Slide 17: Reference
Osteonecrosis of the Hip - OrthoInfo - AAOS.url:https://orthoinfo.aaos.org/en/diseases--conditions/osteonecrosis-of-the-hip
Hiasa, Y., Otake, Y., Takao, M., Matsuoka, T., Takashima, K., Carass, A., . . . Sato, Y. (2018). Cross-Modality image synthesis From UNPAIRED data Using CycleGAN. Simulation and Synthesis in Medical Imaging, 31-41. doi:10.1007/978-3-030-00536-8_4