## Slide 1: VR Guided Surgery SDF based guidance and safety
Team: Hisashi Ishida, Juan Barragan Antonio
Mentors: Max Li, Adnan Munawar, Prof. Misha Kazhdan, Prof. Russ Taylor
Project16

## Slide 2: Background
Mastoidectomy Procedures
  Remove hollow bone behind the ear by drilling the temporal bone
  Require high precision
  It is critical to preserve important structures, e.g., semicircular canals, sigmoid sinus,and facial nerves.
Mastoid surgery animation (https://www.youtube.com/watch?v=ZRxG_AmDaLI)

## Slide 3: Project Overview
Volumetric Drill Simulation [1]
Signed Distance Field [2]
[1] Munawar, A., Li, Z., Kunjam, P., Nagururu, N., Ding, A.S., Kazanzides, P., Looi, T., Creighton, F.X., Taylor, R.H. and Unberath, M., 2021. Virtual reality for synergistic surgical training and data generation.
[2] T. Saito and J.-I. Toriwaki, “New algorithms for euclidean distance transformation of an n-dimensional digitized picture with applications,” Pattern Recognition, vol. 27, no. 11, pp. 1551–1565, Nov. 1994, doi: 10.1016/0031-3203(94)90133-3.
Goal: Evaluate the effectiveness of feedback modalities based on SDFs to improve the user’s awareness of critical anatomies.
Notes: (Our target procedure, Mastoidectomy, requires high precision and preserving the important structures.)
Previously developed virtual simulator, AMBF, which is presented on your left was reported effective for virtual drilling simulation since it allows users to practice surgical procedures while also generating relative data for surgical computer vision algorithms.
However, this simulation environment does not provide any assistance for safety related to the distance between the drill and critical anatomies. Currently there is no haptic feedback or visual situational awareness to secure the patient safety.
Therefore, our project aims to develop and evaluate the effective feedback modalities based on SDFs to improve situational awareness on virtual drilling
SDF is a function that assigns each point in space the closest distance between an object or the boundaries and that specific point.
Simulator environment for Mastoidectomy. , requires high precision and preserving the important structures.)
The simulator is good for training but lacks some key safety features.
Goal of the project was to develop feedback modalities.
SDF. Mathematical function that allows you to calculated easily the distance between

## Slide 4: Methodology(1): SDF calculation and loading
Notes: We calculated the SDF and modified the simulation plug-in.
Using the segmented CT images, SDF grids for 16 anatomies are calculated once at the initialization phase based on the assumptions that critical anatomies will not change.
*

## Slide 5: Methodology(2) Feedback modalities
1. Visual Feedback
Closest structure
name
color
distance
3. Haptic Feedback
Avoid collision
2. Audio Feedback
Beep sound
Notes: We proposed 3 types of feedback based on SDF.
First, visual overlay of the text for the closest structural name, color and distance between the drill to the structure will be projected on the HMD.
When you get close to the structure and violate the certain threshold , first audio feedback will be provided and let you know you are approaching to the structure.
Lastly, force feedback will be actived trying to avoid the structure.
Every parameters including the magnitude and the threshold were determined after the pilot study with the medical docor

## Slide 6: Preliminary experiment and result
Experiment setup
Subject: 1 resident
After sufficient time of practice, subject were asked to expose the incus under (1) without any assistance (2) with proposed feedback modalities.
Result
Reduced the number of collision
Reduced the workload
modality preference
  Audio > Haptic > Visual feedback
Values closer to the center indicate better results.
Notes: Simple user study was performed with 1 resident to evaluate the effectiveness of our proposed method. After sufficient time of practice, the subject was asked to expose the incus under 2 condition: (1) without any assistance, (2) with proposed feedback modalities.
This study represent a proof of concept that our method has the potential to improve safety and reduce workload in drilling.

## Slide 7: Future work
User study with larger sample size.
Evaluating feedback modalities’ effectiveness to improve safety in the procedure.
Identify surgeons' preferences, i.e., identifying most effective modality.
Real-time calculation of signed distance fields.

## Slide 8: References
[1] A. Munawar et al., “Virtual reality for synergistic surgical training and data generation,” Computer Methods in Biomechanics and Biomedical Engineering: Imaging & Visualization, vol. 0, no. 0, pp. 1–9, Nov. 2021, doi: 10.1080/21681163.2021.1999331.
[2] T. Saito and J.-I. Toriwaki, “New algorithms for euclidean distance transformation of an n-dimensional digitized picture with applications,” Pattern Recognition, vol. 27, no. 11, pp. 1551–1565, Nov. 1994, doi: 10.1016/0031-3203(94)90133-3.
[3] S. A. Bowyer, B. L. Davies and F. Rodriguez y Baena, "Active Constraints/Virtual Fixtures: A Survey," in IEEE Transactions on Robotics, vol. 30, no. 1, pp. 138-157, Feb. 2014, doi: 10.1109/TRO.2013.2283410.
[4] Li, Z., Gordon, A., Looi, T., Drake, J., Forrest, C., & Taylor, R. H. (2020, October). Anatomical mesh-based virtual fixtures for surgical robots. In 2020 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS) (pp. 3267-3273). IEEE.
Link to our repo
Link to our repo

## Slide 9
Appendix

## Slide 10
Technical overview: Offline calculation of SDF
Anatomy representation
SDF maps for each anatomical structure.
SDF module
SDF look up table
Design parameters
16 different anatomical structures
SDF Resolution 171/256/512
Size SDF cube: 49.664 mm^3
Zero-padding: 0
Notes: 1.5 min

## Slide 11
Technical overview: Using SDF at runtime.
(Tx, Ty , Tz) --> (Ix, Iy, Iz)
(Tx, Ty, Tz)
Outside the SDF grid
Inside the SDF grid
No distance information when drill tooltip is outside of SDF grid.
When inside the grid a conversion between tooltip coordinates and voxel grid index is needed to access the distance data.
Notes: 0.5 min

## Slide 12
OLD

## Slide 13
Project Goals and deliverables
Goal: Evaluate the effectiveness of feedback modalities based on SDFs to improve situational awareness on virtual drilling simulations.
 | Deliverable
Minimum | Creating an AMBF plugin to calculate SDFs for static objects in the volumetric drilling simulation.
Expected | Develop SDF based feedback modalities to improve situational awareness. Developing haptic based feedback modalities. Developing visual based feedback modalities. Document all the flow
Maximum 1 | Internal user study and/or conference paper.
Maximum 2 | Optimizing algorithms to calculate SDFs of objects changing overtime in real-time, e.g., the drilling volume.
Notes: In order to achieve our goal, we set these following deliverables.

## Slide 14: Project phases
SDF for static volumes (Offline SDF calculation)
  Familiarize with methods to calculate the signed distance fields. (https://github.com/mkazhdan/EDT)
  Integrate SDF functions with AMBF using plugins.
Use SDF to improve situational awareness of the user.
  Provide Visual feedback.
  Haptic Feedback.
  Perform a user study (optional).
SDF for changing volumes (Online SDF calculation)
  Optimizing algorithms to calculate SDF for volumes that change over time
~Apr. 27
~Mar. 1412
~May. 17
Notes: 30 sec

## Slide 15: Updated Dependencies
Dependency | Status | Fallback/Prevention | Needed by | Effect
Access to a Linux workstation | Obtained | N/A | 02/18/2022 | Delay in all milestones.
Access to haptic device | In progress Obtained | Focus only on visual feedback mechanisms. | 03/23/2022 | Delay in haptic feedback development.
IRB approval | In progress | N/A | 03/31/2022 | Delay in internal user study.
VR device | Obtained | Using 2D screen | 03/31/2022 | Delay in internal user study.
Notes: 30sec

## Slide 16: Project phases
SDF for static volumes (Offline SDF calculation)
  Familiarize with methods to calculate the Euclidean Distance Transform. (https://github.com/mkazhdan/EDT)
  Integrate SDF functions with AMBF using plugins.
Use SDF to improve situational awareness of the user.
  Provide Visual feedback.
  Haptic Feedback.
  Perform a user study (optional).
SDF for changing volumes (Online SDF calculation)
  Optimizing algorithms to calculate SDF for volumes that change over time
~Apr. 27
~Mar. 14
~May. 17
Notes: Juan

## Slide 17: Technical overview
Phase 1: SDF calculation for static objects & software integration architecture.
SDF look-up table
SDF calculation
Load volume
User interaction
Feedback
Drill position
Initialization
Run time
SDF calculation for volumes represented by a voxel grid based on [Saito and Toriwaki, 1994][2].
SDF functions will be loaded as a shared library to AMBF.
Notes: Answer how we are going to integrate EDT into AMBF?
Method to calculate EDT
Slide pitch:
- Talk about the goal. What are static objects? This are are the critical anatomies that the surgeon needs to avoid during the surgery.
- Requirements for our SDF algorithms --> they need to work for volumnes represented with a voxel grid. (2) compiled a c++ shared library for easy integration with AMBF.
- Describe flow diagram:
1 segmented cT is loaded to simulation and used to calculated SDF for each anatomy.
2 SDF are stored in a look up table.
3 During the simulation user interacts with the environment. AFter each user command the distance between the drill and the different critical anatomies will be calculated and used to provided feedback to the user.

## Slide 18: Technical overview
Phase 1: SDF calculation for static objects & software integration architecture.
SDF calculation
Load volume
User interaction
Feedback
Drill position
Initialization
Run time
SDF look up table
Notes: Answer how we are going to integrate EDT into AMBF?
Method to calculate EDT
Slide pitch:
- Talk about the goal. What are static objects? This are are the critical anatomies that the surgeon needs to avoid during the surgery.
- Requirements for our SDF algorithms --> they need to work for volumnes represented with a voxel grid. (2) compiled a c++ shared library for easy integration with AMBF.
- Describe flow diagram:
1 segmented cT is loaded to simulation and used to calculated SDF for each anatomy.
2 SDF are stored in a look up table.
3 During the simulation user interacts with the environment. AFter each user command the distance between the drill and the different critical anatomies will be calculated and used to provided feedback to the user.

## Slide 19
Technical overview: Offline calculation of SDF
Design parameters
SDF Resolution 171/256/512
Size SDF cube: 49.664 mm
Zero-padding: 0
V0
49.664 mm
171/256/512 pixels
Notes: 0.5min

## Slide 20: Current Progress
Provide distance between Tool tip and the critical structure(blue)
  SDF resolution: 171
  Controlled using keyboard
Notes: This is the video for our current progress.
First, we provide the distance between Tool tip and the critical structure(blue) which is buried in the bone.

## Slide 21: Current problems
Limited SDF workspace
  Expand the size of volume(zero-padding)
  Find the appropriate SDF resolution
Effective visual feedback
  Toggle the opacity of the bone and highlight the closest critical structure
Important parameters for Online SDF calculation(Phase3)
Notes: These design parameters are highly important for Phase 3 when we need to calculate the SDF in real time.
We would like to discuss about this parameters more with our mentors.
Furthermore, we only provide single distance between the the tooltip and the important structure.
However, there are multiple critical structures, and current visual information is not enough. One of our plans is to implement the functionality to toggle the opacity of the bone and highlight the closest critical structure.
I believe this will improve the situational awareness drastically.

## Slide 22
30%
0%
0%
0%
0%
0%
2022
Today
Feb
Mar
Apr
May
Phase1: Offline SDF calculation
Feb 14
Phase2: Situational awareness interface
Mar 1612
Phase3: Online SDF calculation
Apr 18
Project Close
May 5
Feb 14 - Mar 3
14 days
SDF implementation
Mar 1612 - Mar 29
14 days
Feedback Modalities
7 days
User study setup
Apr 18 – Apr 30
12 days
Online SDF implementation
Mar 3 - Mar 1612
14 days
AMBF integration
Data collection
Apr 4 - Apr 18
14 days
May 1 - May 5
5 days
Data collection
Mar 29 - Apr 4
Updated Gantt chart
IRB
7 days
Notes: I would like to go through the Gantt chart.
We have three phases. each of them corresponds to the our minimum, expected, and maximum deliverables.

## Slide 23: Background
Mastoidectomy Procedures
  Remove hollow bone behind the ear by drilling the temporal bone
  Require high precision
  Preserve important structures e.g.) semicircular canals, sigmoid sinus, facial nerves etc.
Mastoid surgery animation (https://www.youtube.com/watch?v=ZRxG_AmDaLI)
http://entsurgeonkemptonpark.co.za/tympanoplasty-cortical-mastoidectomy-2/
Notes: Our target procedure is mastoidectomy.
Mastoidectomy is a common procedure to treat an infection in mastoid air cells. The surgeon will make a cut behind the ear remove hollow bone by drilling the temporal bone.
This procedure can be highly challenging due to the fact that the it requires high precision and preserving the important structures. such as …which are illustrated in the figure on the lower right corner.

## Slide 24: Volumetric drilling virtual simulator
Asynchronous Multibody Framework (AMBF+)[1]
[1] Munawar, A., Li, Z., Kunjam, P., Nagururu, N., Ding, A.S., Kazanzides, P., Looi, T., Creighton, F.X., Taylor, R.H. and Unberath, M., 2021. Virtual reality for synergistic surgical training and data generation.
Allows users to practice surgical procedures Generates relevant data in real-time for training of CV assistive system
Notes: Previous work from Hopkins have developed virtual simulator for volumetric drilling.
It uses segmented CT images to create the drilling simulator environment. This simulator can be interacted with both haptic feedback and stereoscopic display.
This simulator is particularly powerful because it allows users to practice surgical procedure but also generates relevant data in real time.
Generated data includes RGBD image, segmented masks and all the pose and status of the voxels and it can be used to train the CV assistive system.

## Slide 25: Problem statement
Warning comes out only after it actual collide with the important anatomy No haptic feedback or virtual fixture to secure important anatomy
Notes: This is a video using the volumetric simulator.
It is very realistic and accurately simulate the environment, and also the drill moves smoothly without any interference.
However, this simulator has some room of improvement.
First. it has situational awareness for some extent but not enough.
Warning comes out only after the drill actual collides with the important anatomy, and this is most of the time too late.
Second, there is no haptics feedback to secure the important anatomy.
We believe that improving these two aspects and provide better situation awareness will not only improve safety but also increasing the learning effectiveness of the simulator by reduce workload and time it takes for this procedure.

## Slide 26: Method Overview
Context situational awareness method using SDF Get SDF for each type of volume
  Visual feedback (“Warnings” when close to the important tissue)
  Haptic feedback (Virtual fixture or haptic guidance)
Volumetric Drill Simulation [2]
[2] Munawar, A., Li, Z., Kunjam, P., Nagururu, N., Ding, A.S., Kazanzides, P., Looi, T., Creighton, F.X., Taylor, R.H. and Unberath, M., 2021. Virtual reality for synergistic surgical training and data generation. (https://www.youtube.com/watch?v=jnonLwxW2Cg)
Signed Distance Field [1]
Notes: Mastoidectomy requires drilling of the temporal bone without damaging critical anatomies of the skull
Explain what it is a SDF.
Pitch for the slides
- To achieve the goals of our project.
SDF is a function that assigns to each point in space the closest distance between an object and that specific point.
- Example image of the right.
- Once calculated the SDF allow us to know the distance between the drill tip and all the other anatomies in the simulator.
- This information can used to provided feedback to the user of how close he is to particular anatomy and even prevent the user from drilling that anatomy.
- This results in improved safety and situational awereness.

## Slide 27: Project phases
SDF for static volumes (Offline SDF calculation)
  Familiarize with methods to calculate the Euclidean Distance Transform. (https://github.com/mkazhdan/EDT)
  Integrate SDF functions with AMBF using plugins.
Use SDF to improve situational awareness of the user.
  Provide Visual feedback.
  Haptic Feedback.
  Perform a user study (optional).
SDF for changing volumes (Online SDF calculation)
  Optimizing algorithms to calculate SDF for volumes that change over time
~Apr. 27
~Mar. 14
~May. 17
Notes: Juan

## Slide 28: Technical approach
Development of Feedback modalities
  Visual Feedback
  Haptic Feedback
S. A. Bowyer, B. L. Davies and F. Rodriguez y Baena, "Active Constraints/Virtual Fixtures: A Survey," in IEEE Transactions on Robotics, vol. 30, no. 1, pp. 138-157, Feb. 2014, doi: 10.1109/TRO.2013.2283410.
Overlay warning message
Provide warning when the drill gets closer to anatomy than the threshold
Forbidden virtual fixture Avoid collision with the anatomy Use the gradient field of the SDF
Notes: I would like to talk technical approach for Phase 2: development of feedback modalities.
There are two types of feedback using SDF: the visual and haptic.
For visual feedback, we are thinking of the overlaying the warning message.
Different from we currently have, we are using SDF and specific threshold to provide warning before the drill actually damages the important tissue.
For haptic feedback we are adopting the virtual fixture method specifically the forbidden regional VF to avoid collision with the anatomy using the gradient field of the SDF

## Slide 29
30%
0%
0%
0%
0%
0%
2022
Today
Feb
Mar
Apr
May
Phase1: Offline SDF calculation
Feb 14
Phase2: Situational awareness interface
Mar 16
Phase3: Online SDF calculation
Apr 18
Project Close
May 5
Feb 14 - Mar 3
14 days
SDF implementation
Mar 16 - Mar 29
14 days
Feedback Modalities
7 days
User study setup
Apr 18 – Apr 30
12 days
Online SDF implementation
Mar 3 - Mar 16
14 days
AMBF integration
Data collection
Apr 4 - Apr 18
14 days
May 1 - May 5
5 days
Data collection
Mar 29 - Apr 4
Gantt chart
IRB
Notes: I would like to go through the Gantt chart.
We have three phases. each of them corresponds to the our minimum, expected, and maximum deliverables.

## Slide 30: Management plan
Weekly meeting with mentors:
  Max Li
  Adnan Munawar
Weekly lab meeting
Weekly team meeting
Technical advisory meeting(on demand)
  Prof. Kazhdan
  Prof. Taylor
Communication through Slack
Code management with Github
Additional file management with OneDrive

## Slide 31: References
[1] A. Munawar et al., “Virtual reality for synergistic surgical training and data generation,” Computer Methods in Biomechanics and Biomedical Engineering: Imaging & Visualization, vol. 0, no. 0, pp. 1–9, Nov. 2021, doi: 10.1080/21681163.2021.1999331.
[2] T. Saito and J.-I. Toriwaki, “New algorithms for euclidean distance transformation of an n-dimensional digitized picture with applications,” Pattern Recognition, vol. 27, no. 11, pp. 1551–1565, Nov. 1994, doi: 10.1016/0031-3203(94)90133-3.
[3] S. A. Bowyer, B. L. Davies and F. Rodriguez y Baena, "Active Constraints/Virtual Fixtures: A Survey," in IEEE Transactions on Robotics, vol. 30, no. 1, pp. 138-157, Feb. 2014, doi: 10.1109/TRO.2013.2283410.
[4] https://shaderfun.com/2018/03/25/signed-distance-fields-part-2-solid-geometry/
[5] https://www.youtube.com/watch?v=ZRxG_AmDaLI
[6] http://entsurgeonkemptonpark.co.za/tympanoplasty-cortical-mastoidectomy-2/

## Slide 32
30%
0%
0%
0%
0%
0%
2022
Today
Feb
Mar
Apr
May
Phase1: Offline SDF calculation
Feb 14
Phase2: Situational awareness interface
Mar 23
Phase3: Online SDF calculation
Apr 27
Project Close
May 17
Feb 14 - Mar 3
14 days
SDF implementation
Mar 23 - Apr 5
10 days
Feedback Modalities
Apr 11 - Apr 15
5 days
User study setup
Apr 27 - May 12
12 days
Online SDF implementation
Mar 3 - Mar 22
14 days
AMBF integration
Data collection
Apr 16 - Apr 26
7 days
May 12 - May 17
5 days
Data collection
Old Gantt chart
IRB
Notes: I would like to go through the Gantt chart.
We have three phases. each of them corresponds to the our minimum, expected, and maximum deliverables.

## Slide 33
V0
V1
V15
V16