## Slide 1: Mixed Reality Surgical Team Training: Checkpoint Presentation
Team member: Haochen Wei
Mentors: Peter Kazanzides; Dayeon Kim
Mar 29th 2022

## Slide 2: Project Review
We want to create a mixed reality surgical training system.
We want to create a more general mixed reality environment for different kinds of endoscopic surgical process training.
No limitation on tool numbers
No limitation on tool shapes (A little bit hard for the current stage)
Can be combined with Da Vinci Robot

## Slide 3: Project Review: Concept image
Simulator
Point clouds of hand-held (and robotic) instruments from sensorized phantom
3D endoscope video (simulated patient, real instruments)
HMD optional (could deliver training info)
Anatomy is simulated, instruments are real.
Realistic physical interaction with system (except for direct interaction with anatomy)
2D video
Endoscope video (of instruments)
Sensorized phantom
Sensorized phantom provides 3D point clouds of inserted instruments
Unmodified da Vinci data
Simulator video output
Sensorized phantom output

## Slide 4: Deliverable
Simulator
Point clouds of hand-held (and robotic) instruments from sensorized phantom
2D endoscope video (Point Cloud)
Endoscope video (of instruments)
Sensorized phantom
Unmodified da Vinci data
Simulator video output
Sensorized phantom output
Minimum: (To be finished at 4/8)
Point clouds of hand-held (and robotic) instruments from sensorized phantom
2D video from the perspective of the endoscope output to the standalone monitor.
Expected: (To be finished at 4/28)
Overlay the patient’s 3D model with the obtained point cloud. (Proof of concept)
Check for collisions between instruments and anatomy
Notes: PK: Hopefully, you will be able to do more than this, since this result would look worse than just showing the real endoscope video

## Slide 5: Milestone and project phase
Date | Object | Explain
3/11 | Obtain, mount and calibrate all the cameras. | Freezing the hardware.
3/25 | Finishing improving the point cloud data. | The project is aiming to achieve real-time rendering. The algorism of collecting real-time point cloud and filtering out noise should be given by now.
4/8 | Finish minimal object | The real-time rendering object should be achieved.
4/28 | Finish the expected object | Collision detection achieved
Notes: PK: This seems overly optimistic

## Slide 6: First milestone:
Finish comparison, Obtain, and Calibrate all the cameras. Finished at 3/11
Selected Camera:
Camera Type: Traditional Stereo Camera
Model: ZED mini stereo camera system
Reason to give up ToF and Quad cameras solution:
1. Current solution won’t take advantages of the quad camera system.(Will explain detail in next phase)
2. Don’t have enough time to try ToF solution
Problem:
1. The mounting bracket can be improved in the future

## Slide 7: Second milestone:
Finishing improving the point cloud data. Finished at 3/27
Feature detection algorithm:
Taking the advantage that most endoscopic tools are slender tube shapes. Take the feature point from the centerline of tools.
Binary the image to make the tools be black.
Find the centerline of black block (This step will contain many noises not belongs to the tool)
Find the straight-line using Hough from raw feature point (Improving this step will expand the available tools range)
Filter and Classify the point near the find a straight line, only keep those points that are closed to the finding straight line. Classified them as well for future reconstruction.
Reason:
Bypass the poor performance of regular feature detection algorithms such as SIFT/SUFT/ORB on slender tools. Ensure the accuracy and density of the point cloud.
Problem:
Only Works on straight slender tools now. Can improve on the detection of the end-point tool.

## Slide 8: Second milestone: example shown
Feature detection algorithm shown:
1. 2.
3. 4.

## Slide 9: Third and Fourth milestone:
Achieve Real time rendering (minimal deliverable). In progress
Improve on speed:
Current running speed: 0.02-0.05 seconds per frame. The current solution can generate the point cloud at an average of about 30 fps. Marginally OK.
Rendering tool selection:
Currently decided using unity as rendering engine.
Collision detection. Not started
Considering Rendering the 3d mesh model directly. Based on current data, it is possible to directly obtained the 3d line equation to solve the occlusion problem.
Documentation.
Will start writing doc after achieve minimal deliverable

## Slide 10: Technical Problem and Possible Approach
Sync between endoscope frame and point cloud frame.
Due to the fact, the point cloud data speed is not constant, time sync between endoscope position and point cloud data need to be addressed. The current idea is a timestamp from the system.
The connection between unity engine and obtained point cloud.
The currently available point cloud pack for unity is not very great for real-time rendering. Directly rendering a 3D model might solve the issue, and might incidentally solve the inherent point cloud problem of multiple tools crossing
Only Works on straight slender tools now. Algorithm need to revised to support irregular shape tools.
So far don’t have an idea about this problem.
Notes: PK: If endoscope attached to robot, why do you need AR tag? And, where do you plan to attach this tag, on the inside of the phantom? With the robot, you just need to do a one-time registration between the robot and the phantom. For a hand-held endoscope, this is more difficult and one possible solution is to attach a tag, as you mention.

## Slide 11: Updated Timeline
Green: Finished Yellow: In progress Red: Not started
Chart: Project timeline
| Designing mount bracket and installision | Point clouds using Cameras and decide | Rendering the point cloud asynchronous | Improving the point cloud quality | Researching on Real-time rendering | Locolization of endoscope | Achieve real time rendering | Overlay 3d model to rendered graph | Point collision function | Wrap-up the research | Buffer,Doc and Final report
Start date | 44617 | 44631 | 44631 | 44638 | 44638 | 44645 | 44645 | 44659 | 44666 | 44673 | 44680
Range | 14 | 7 | 16 | 9 | 9 | 14 | 14 | 14 | 14 | 7 | 7
Notes: PK: This seems overly optimistic

## Slide 12: Updated Dependency
Items | Sources | Need Date | Status | Priority, Possible effect and Substitution
2 x RGB Cameras and MCU | Lab | 3 /11 | Obtained | 1. Cannot perform research without it.
ToF RGBD Cameras | SMART Lab | 3 /11 | Abandoned | 2.Still can perform experiment without it but will not be able to perform comparison
Other RGB/ToF RGBD camera(s) | Purchase | 3 /25 | Abandoned | 2. Still can perform experiment without it but will significantly loss the accuracy
Mounting Bracket for Cameras | Fabrication on machine shop | 3 /11 | Obtained (Subject to change) | 2. Have alternative method but will significantly influence accuracy of cameras.
DVRK | LCSR Lab | 3/18 | Available | 2. Can perform the experiment without it. Only be able to use AR-tag to localization the endoscope.
Abdominal Phantom | LCSR Lab | 3 /11 | Available | 3. Can perform the experiment without it. Easily find alternatives e.g cardboard box.
Computer | Myself | Now | Available | 1. Cannot perform research without it.
Endoscopic tools | LCSR Lab | 3 /11 | Available | 3. Can perform the experiment without it. Easily find alternatives e.g pen
Unity Engine | Online | 3 /11 | Available | 1. Cannot perform research without it.

## Slide 13: Documentation and management
Code, report, paper and CAD design uploaded on google drive to share between mentor and team.
Meetings with Professor Peter Kazanzides and Dayeon Kim every Friday

## Slide 14: Reference
Qian L., Zhang X., Deguet A., Kazanzides P. (2019) ARAMIS: Augmented Reality Assistance for Minimally Invasive Surgery Using a Head-Mounted Display. In: Shen D. et al. (eds) Medical Image Computing and Computer Assisted Intervention – MICCAI 2019.
Azimi, Ehsan et al. “An Interactive Mixed Reality Platform for Bedside Surgical Procedures.” MICCAI (2020).
Zollhöfer, Michael & Stotko, Patrick & Görlitz, Andreas & Theobalt, Christian & Nießner, Matthias & Klein, Reinhard & Kolb, Andreas. (2018). State of the Art on 3D Reconstruction with RGB‐D Cameras. Computer Graphics Forum. 37. 625-652. 10.1111/cgf.13386.
Han, X., Laga, H. Bennamoun, M. Image-Based 3D Object Reconstruction: State-of-the-Art and Trends in the Deep Learning Era. IEEE Transactions On Pattern Analysis And Machine Intelligence. 1578-1604 (2021,5), http://dx.doi.org/10.1109/TPAMI.2019.2954885

## Slide 15: Thank you Questions?