## Slide 1: Check Point Presentation Photoacoustic Image Based Intraoperative Surgical Guidance System in da Vinci Robot System
Team Members: Zijian Wu, Shuojue Yang
Mentors: Hyunwoo Song, Dr. Hamid Moradi, Dr. Emad M. Boctor
03.31.2022

## Slide 2
Objective
Introperative Guidance System
  Nerve sparing radical prostatectomy
  Surgical tool & target tracking
  Registration between camera and transducer
Introduction

## Slide 3: Progress Overview
Conventional registration algorithm using virtual markers
  Simulation analysis (key component: PA position search)
  Implementation and integration
  Verification of the algorithm in the da Vinci platform
Novel registration algorithm using virtual markers
  Simulation analysis
  Marker tracking module
  Implementation and integration
Intraoperateive Guidance System Integration using a GUI interface
  Overall design and developemnt of GUI
  Implementation of laser excitation control
Introduction

## Slide 4
Host 1
(ROS)
Micro-controller (Arduino)
da Vinci
Flag
Laser pulser
(Function Generator)
Trigger
FL image
Trigger
US DAQ
Calculate spot position in FL image
GUI ( rqt, ROS)
Registration
  - Conventional
  - Novel
Host2
(Windows)
Actuator
TRUS transducer
attached
Pulsed laser diode
Tool tip
FL ECM
attached
User ctrl
Rotate the actuator
Acquire PA image
Calculate spot position in PA image
Searching algorithm
Introduction
TCP/IP
black - completed
red - uncompleted
PA image & Spot position

## Slide 5
Goal: determine the imaging plane position where the PA marker located
Algorithm: coarse-to-fine search
- Coarse search: narrow the search range
- Fine search: accurately find the position
Progress
FOV
sensitive range
TRUS
Here we assume:
Field of view (FOV): -45°~45°
Sensitive range: -4.5°~4.5°
Simulation analysis for PA position search algorithm

## Slide 6: Coarse Search
4.5
threshold
Progress
The intensity function of distance (degree) between the imaging plane and the PA position
9°
-45°
45°
0°
Initial position
The diagram of coarse search
PA spot

## Slide 7: Fine Search
Progress
Ternary search

## Slide 8: Results in Simulation Data - Ternary Search
Progress
Partial results of ternary search

## Slide 9: Failure Analysis
In 2000 times tests, success rate is 99.10%
The function is not strictly unimodal because of noises
Current algorithm will be trapped in local minimum in some cases
Progress

## Slide 10: Fine Search
Progress
Sample-Based Algorithm
- Sample at equal intervals (add first and end positions)
- Fit to a smooth function by using Gaussian
- Directly find peak in this soomth function using library function

## Slide 11: Results - in experimantal and simulation data
In simulation data, test 100 times
Average error: 0.10175°
Average iteration times in coarse search (max 10): 5.47
Iteration times in fine search (fixed): 10
Success rate: 100%
In experimantal data, test 100 times
Average error: 0.2871°
Average iteration times in coarse search (max 10): 5.78
iteration times in fine search (fixed): 10
success rate: 100%
Progress

## Slide 12: Next step for conventional registration
Implementation of the search algorithm
Acquision of photoacustic image
Computation of spot coordinates in PA image
Progress

## Slide 13
System Integration with GUI
Registration Control
Laser control
Point detection in FL image
Sample management
Point-pair registration1
TODO
Aquisition of PA image & spot

## Slide 14
Minimum - completed
Design and implementation of the GUI.
Simulation analysis for the conventional registration pipeline.
Expected
Implementation and validation of the conventional registration algorithm.
Maximum
Implementation of necessary modelus of novel registration algorithm.
Simulation analysis for novel registration algorithm.
Deliverables

## Slide 15
 |  | Feb |  | Mar | Apr | May
GUI & System Integration |  |  |  |  |  | 
- Overall design and development of GUI |  | 2/21 2/28 |  |  |  | 
- Implementation of laser excitation control |  | 3/1 3/14 |  |  |  | 
Conventional Registration Algorithm |  |  |  |  |  | 
- Simulation analysis |  | 2/21 4/7 |  |  |  | 
- Implementation and integration |  | 3/28 4/22 |  |  |  | 
- Verification in the da Vinci platform |  | 4/22 4/29 |  |  |  | 
Novel Registration Algorithm |  |  |  |  |  | 
- Simulation analysis |  | 4/7 4/22 |  |  |  | 
- Marker tracking module |  | 4/22 5/5 |  |  |  | 
- Implementation and Integration |  | 5/5 5/16 |  |  |  | 
Milestone

## Slide 16: Thank you!