## Slide 1: Photoacoustic Image Based Intraoperative Surgical Guidance System
Team Members: Zijian Wu, Shuojue Yang
Mentors: Hyunwoo Song, Dr. Emad M. Boctor, Dr. Hamid Moradi
02.24.2022

## Slide 2
Background
Clinical Scenario
  Nerve sparing radical prostatectomy
  Post-operative complication (e.g., erectile dysfunction,urinary incontinence)
  Intraoperative guidance system is required
Introduction

## Slide 3
Background
Ultrasound imaging modality
  Monitoring morphological structures
Photoacoustic effect in Photoacoustic (PA) image
  Laser spot has a substantial impact in US image
  Non-physical markers for registration and location
  Avoid EM field distortion, line-of-sight restrictions, complexity of surgical setting...
Introduction
Cheng, 2017

## Slide 4: System Overview
Intraoperateive Guidance System Integration using a GUI interface
Registration algorithm using virtual markers
Photoacoustic Visual-servoing
Introduction

## Slide 5: Overview & Motivation
Photoacoustic Image based Intraoperateive Guidance System
  Locate lesions or ROI
  Laser spots serving as virtual markers
  Registration of stereoscopic endoscopes and US transducers
Photoacoustic Visual-servoing
  Better imaging quality
  Surgical tool track with little time delay
Introduction

## Slide 6: Motivation
Elevation, y
Axial, z
TRUS
Laser spot
FL
Lateral, x
x
z
y
da Vinci base
x
z
y
US/PA image
FL image
scanline
Introduction
Photoacoustic virtual marker Registration
Visible spot in endoscope camera
Obtain point pairs in FL/PA images
High laser power
Complex procedure

## Slide 7
Elevation, y
Axial, z
TRUS
Laser spot
FL
Lateral, x
x
z
y
da Vinci base
x
z
y
US/PA image
scanline
Novel Registration Algorithm
Invisible spot in camera view
Less laser power
Simple process
Introduction
FL image
System Overview & Motivation

## Slide 8: Goal
High-level Clinical Goal:
Minimize the intraoperative trauma and post-operative complication in the nerve sparing radical prostatectomy.
Engineering Goals:
1. Integration of the intraoperative guidance system with a GUI interface
2. Registration of US transducer and camera without visible spots in camera view
3. Photoacoustic visual-servoing module improving the tool track
Introduction

## Slide 9
Host 1
(ROS)
Micro-controller (Arduino)
da Vinci
Flag
Laser pulser
(Function Generator)
Trigger
FL image
Trigger
US DAQ
Spot (virtual marker) position calculation
Registration
  - Conventional
  - Novel
Feed actuator
Host2
(Windows)
Actuator
TRUS transducer
PA image
attached
Pulsed laser diode
Tool tip
FL ECM
attached
User ctrl
Servoing
Angle
GUI (PyQt, ROS)
Laser Control
Registration Control
Visualization
Rotate the actuator
Technical approach - System Integration
TCP/IP
black - completed
red - uncompleted

## Slide 10
attach markers on the diode
obtain the marker’s position
calibrate the marker w.r.t. the diode
Technical approach - Novel Registration
Mathematical Form:
Conventional Approach:
detect photoacoustic virtual marker in the FL image
Novel Approach:
detect diode pose from the endoscopic camera
Implementation:
MATLAB code for simulation analysis is completed
Integrat this algorithm to the system using Python / C++

## Slide 11
Technical approach - Visual Servoing
General Definition:
where - the image coordinates of interest points
- a vector of k visual features
- contains desired values of the k features
IBVS System Diagram:
Image Based
Controller
TRUS Transducer Actuator
Feature Extraction
US Image

## Slide 12
Minimum
System integration with a GUI enabling surgeons to control the laser excitation and registration of TRUS frame with respect to camera frame.
Expected
Implementation and validation of the novel registration algorithm based on the da Vinci robot platform.
Maximum
System optimization by introducing photoacoustic servoing function.
Deliverables

## Slide 13
Dependency | Status
Da Vinci Surgical System | completed
Laser Implementation | completed
Actuator / TRUS / US DAQ | completed
Phantom or ex vivo tissue | completed
Dependencies

## Slide 14
 |  | Feb |  | Mar | Apr | May
GUI & System Integration |  |  |  |  |  | 
- GUI overall design and develop simplified version |  | 2/21 2/28 |  |  |  | 
- Implement laser excitation control function |  | 3/1 3/20 |  |  |  | 
- Registration control |  |  |  |  | 4/7 4/14 | 
Novel Registration Algorithm |  |  |  |  |  | 
- Program for marker location recognition |  | 2/21 3/14 |  |  |  | 
- Implement algorithm with Python / C++ |  | 3/8 3/31 |  |  |  | 
- Integrate registration algorithm to the GUI |  | 4/1 4/7 |  |  |  | 
- Verify the algorithm in the da Vinci platform |  | 4/8 4/22 |  |  |  | 
Photoacoustic visual-servoing |  |  |  |  |  | 
- Simulate classic IBVS algorithm |  | 4/15 5/1 |  |  |  | 
- Implement classic IBVS algorithm in the system |  | 5/2 5/15 |  |  |  | 
- Verify the servoing algorithm and optimize it |  | 5/16 |  |  |  | 
Milestone

## Slide 15
Group meeting: Tuesday 4:00pm - 5:30pm
Meeting with mentors : Monday 1:30pm - 2:00pm
Code management: GitHub
Daily communication: Slack
Management Plan

## Slide 16: Thank you!