## Slide 1: Transparency Optimization of the Galen Surgical System with a Frequency Domain Admittance Controller Design
Students: Brevin Banks
Mentors: Ugur Tumerdem, Manish Sahu, Adnan Munawar, Mohammad Salehizadeh, Russell Taylor

## Slide 2: Project Introduction
The outcome of this project is a new functional frequency domain-based admittance controller that optimizes the transparency of the current Galen robot system in the mock OR while maintaining system stability.
This will be accomplished by reimagining the current control system entirely with basic linear models and then introducing an admittance controller with loop-shaping to better compensate for stability issues that are presently experienced when forces are applied to the robot by the environment.
Furthermore, the controller will be designed and optimized with hand over hand transparency in mind and allow for the application of virtual fixtures.
https://www.galenrobotics.com/about-galen-robotics/

## Slide 3: Background
The current Galen campus robot controller faces performance and stability issues when forces are applied.
In addition to controller stability improvement, we want to optimize the transparency with a new controller.
Stability innately affects the transparency of the control system and cannot be easily adjusted by simply tuning gains. There is much work to be done in the field of transparency optimization.

## Slide 4: Significance
Natural and Steady Movements in the Operating Room
Easy application of Virtual fixtures
Could be Adapted to Make Quicker and More Accurate Procedures

## Slide 5: Deliverables
Minimum:
A stable frequency domain admittance controller in MATLAB code for the Galen surgical robot in the AMBF simulation environment
A simulated control system package with optimized transparency containing code files that can be used in AMBF and MATLAB and is transferable to hardware
Expected:
An applied control system package to the low-level Galen controller that is stable and optimized for transparency including virtual fixtures
A validated objective improvement in transparency according to specified metrics
Maximum:
A completed user study to investigate subjective transparency preference with different controllers on the Galen robot

## Slide 6: Technical Approach
Start with a basic linear system for the robot in simulation to develop controller architecture (Either Velocity or Position Control)
Include environment and human impedance factors
Apply Admittance Controller and Frequency based filters to tune the controller performance
Identify robot dynamics for plant with LTI approach or similar method

## Slide 7: Technical Approach
Bound the human impedance and environment impedance with estimated values
Aim for High Admittance a high impedance while maintaining stability and watching the effects of damping

## Slide 8: Technical Approach Continued

## Slide 9: Project Dependencies
Dependency | Need | Contingency Plan | Planned Deadline | Hard Deadline | Status
Access to Computer | Need a computer with a Linux platform | Use a lab computer | 8-Feb | 13-Feb | Completed
Access to Galen AMBF Model | File access and editing permissions | Create a basic 3D model and crude dynamics | 14-Feb | 20-Feb | Awaiting Files
Software Installation MATLAB SIMULINK | License | Use Lab Computer with preinstalled software | 8-Feb | 13-Feb | Completed
Software Blender and AMBF Addon | Installation Instructions | Use Lab Computer with preinstalled software | 8-Feb | 13-Feb | Completed
Galen Robot and Controller Access | Anton and Adnan complete controller pipeline for Galen task space and joint space control | Go without Galen hardware implementation. Implement on similar robot or move on without implementation | 15-Mar | 15-Apr | waiting
IRB for user study | IRB Approval | Go without the User Study | (Submission 20-Feb) 3-Apr | (Submission 24-Feb) 17-Apr | Waiting

## Slide 10: Project Timeline
Task 1.1
Task 1.2
Task 2.1
Task 2.2
Task 2.3
Task 2.4
Task 2.5
Task 3.1
Task 3.2
Task 4.1
Task 4.2
Task 4.3
Task 4.4

## Slide 11: Key Milestones

## Slide 12: Testing Plan
Nyquist plot or Root Locus to assess stability across both extreme bounds for human impedance and environment.
Observe stability in bode plot phase and gain margin. (Key for loop-shaping)
Produce Stability Map
Organize and carry out user study with ENT surgeons to collect qualitative performance data on the transparency of the controller compared to the current controller
https://doi.org/10.48550/arXiv.2007.14503

## Slide 13: Team
Student:
  Brevin
  Roles: Admittance Controller Design, Simulation, Hardware Integration
Mentors:
  Ugur Tumerdem, Ph.D.: Primary Lead, Controls Lead
  Manish Sahu, Ph.D.: Coding Consultant
  Adnan Munawar, Ph.D.: AMBF and Galen Lead
  Mohammad Salehizadeh, Ph.D. Galen Consultant
  Russell Taylor Ph.D.: General Consultant

## Slide 14: Meetings and Data Management
Regularly scheduled weekly meetings with mentor: 4pm Thursdays
Weekly correspondence with the current week’s deliverables and updates delivered before the weekend by email to mentor
Attend Weekly meetings for Galen Robot Controller team: TBD
All code files and deliverables are to uploaded to GitHub and the project wiki. This includes MATLAB, C++, Word, Excel, PowerPoint, and PDF files
Code files are regularly pushed and updated to GitHub repository

## Slide 15: Readings
Alonso, V., & de la Puente, P. (2018). System transparency in shared autonomy: A mini review. Frontiers in Neurorobotics, 12. https://doi.org/10.3389/fnbot.2018.00083
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Feng, A. L., Razavi, C. R., Lakshminarayanan, P., Ashai, Z., Olds, K., Balicki, M., Gooi, Z., Day, A. T., Taylor, R. H., & Richmon, J. D. (2017). The Robotic Ent Microsurgery System: A novel robotic platform for Microvascular Surgery. The Laryngoscope, 127(11), 2495–2500. https://doi.org/10.1002/lary.26667
Huang, S. H. (2019). Optimizing for Robot Transparency. UC Berkeley. ProQuest ID: Huang_berkeley_0028E_19188. Merritt ID: ark:/13030/m5mq08z2. Retrieved from https://escholarship.org/uc/item/5q20h9cs
J. Fong, V. Crocher, Y. Tan, D. Oetomo and I. Mareels, "EMU: A transparent 3D robotic manipulandum for upper-limb rehabilitation," 2017 International Conference on Rehabilitation Robotics (ICORR), London, UK, 2017, pp. 771-776, doi: 10.1109/ICORR.2017.8009341.
Keemink AQ, van der Kooij H, Stienen AH. Admittance control for physical human–robot interaction. The International Journal of Robotics Research. 2018;37(11):1421-1444. doi:10.1177/0278364918768950

## Slide 16: References
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Democratizing Robotic Surgery and Microsurgery. Galen Robotics. (2022, November 15). Retrieved February 13, 2023, from https://www.galenrobotics.com/
Simple gantt chart. Microsoft 365 Templates. (2022, August 13). Retrieved February 13, 2023, from https://templates.office.com/en-us/simple-gantt-chart-tm16400962
Munawar, A., Wang, Y., Gondokaryono, R., & Fischer, G. S. (2019). A real-time dynamic simulator and an associated front-end representation format for simulating complex robots and environments. 2019 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). https://doi.org/10.1109/iros40897.2019.8968568
Munawar, A., Wu, J. Y., Fischer, G. S., Taylor, R. H., & Kazanzides, P. (2022). Open simulation environment for learning and practice of robot-assisted surgical suturing. IEEE Robotics and Automation Letters, 7(2), 3843–3850. https://doi.org/10.1109/lra.2022.3146900
Varier, V. M., Rajamani, D. K., Tavakkolmoghaddam, F., Munawar, A., & Fischer, G. S. (2022). AMBF-RL: A real-time simulation based Reinforcement Learning Toolkit for Medical Robotics. 2022 International Symposium on Medical Robotics (ISMR). https://doi.org/10.1109/ismr48347.2022.9807609