## Slide 1: Towards Collaborative Drilling with a Cobot Using Admittance Controller
Students: Group 1: Brevin Banks
Mentors: Ugur Tumerdem, Manish Sahu, Adnan Munawar, Mohammad Salehizadeh, Russell Taylor
Yusuf Aydin, Doganay Sirintuna, and Cagatay Basdogan (2020)
Literature Review:

## Slide 2: Project Review: Admittance Controller Design
Problem: Current Galen robot controller not well optimized for transparency, and sometimes unstable
Project Goal:
Improve the transparency and stability of the Galen robot with a new controller with verified measurable and quantifiable performance metrics using an Admittance based design
Project Deliverables:
A fully developed, stable, and tested controller that optimizes Galen robot transparency in Simulation
A fully developed, stable, and tested controller that optimizes Galen robot transparency on Hardware
Controller performance maps in stability and transparency
A completed user study for qualitative feedback of controller performance

## Slide 3: Literature Selection: Towards Collaborative Drilling with a Cobot Using Admittance Controller
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Justification:
The project features the design of an admittance controller for robot human interaction
Uses stability and cost impedance maps to predict the desired performance of the robot
Utilizes system dynamics type Identification of the robot in a similar way to our project

## Slide 4: Key Terms for Comprehension
Cobot –
Robot that is intended to interact with humans or in close human proximity
Admittance –
Allowance of external force (removal of robot impedance or resistance felt by the human user)
Stability –
A bounded input (force, velocity, etc.) results in a bounded output (velocity, position) that is controllable and safe
Transparency –
A metric to represent the lack of impedance or resistance felt by the human user due to the robot

## Slide 5: Summary:
Towards Collaborative Drilling with a Cobot Using Admittance Controller
Developed admittance controller scheme that allows for selecting the optimal values of admittance for increasing the transparency of a given system.
Their goal was to drill a hole in a board with a cobot.
Showed how stability maps can be coupled with cost impedance maps to quantify transparency
Results:
A single cartesian directional transparency optimized cobot

## Slide 6: Significance
Showed how admittance controllers can be applied to many nonlinear cobot systems while keeping them stable.
Defined easy to follow, robust, quantifiable metrics for transparency
The control scheme outlined in this paper provides the backbone of our project approach

## Slide 7: Controller Design
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Transfer Function
Total Impedance felt by human
(cut at Zdisp(s))

## Slide 8: Controller Design
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Used system identification with a frequency analysis to capture G(s)
G(s) contains both the plant and controller
Introduce an admittance controller Y(s).
m - is the desired mass felt by the user
b - is the desired damping felt by the user
Low pass filter H(s) combats force noise
Impedances Ze(s) and Zh(s) added by test case

## Slide 9: Equivalent Impedance
Impedance from the human or environment (e.g. board or table) are hard to measure directly since they vary
Bound the values of human and environment impedance for best case and worst-case scenarios
Zeq(s) = Zh(s)+Ze(s)
Buerger SP and Hogan N (2007) Complementary stability and loop shaping for improved human–robot interaction. IEEE Transactions
on Robotics 23(2): 232–244. DOI:10.1109/TRO.2007.892229.
Case | Human mass mh | Human damping bh | Human stiffness kh | Environment stiffness ke
Best | 0 kg | 0 Ns/m | 401 N/m | 0 N/m
Worst | 5 kg | 41 Ns/m | 401 N/m | 16499 N/m

## Slide 10: Stability and Transparency
Stability:
Check for positive closed loop poles
In some cases, evaluate the sign of the phase margin
Transparency:
Evaluate the impedance felt by human between 0.01Hz and 20Hz
Find weighted sum of impedance magnitudes
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643

## Slide 11: Experiment
Test different selection of m and b values for Y(s) that are in the stable region on robot while drilling a piece of wood
Observe
Human input force
Resultant velocity
Accuracy of the hole depth
12 trials performed
4 repetitions for each of the 3 controllers
AR interface displayed the current drill depth relative
to the desired drill depth
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643

## Slide 12: Results
The effects of damping strains the user greater than the effects of mass
Larger masses result in greater amplitudes of oscillation
A fine balance of damping to mass in the stable region will produce a higher accuracy permitting controller
Lower m and b resultant in more transparency or human effort
Force exerted by human
Output robot velocity
Resultant effort of the human
No contact
During contact
Error from desired hole depth
Amplitude of Oscillation
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643

## Slide 13: Reflection
Next Steps
Apply to more than one cartesian dimension
  The constraints of one dimension allow a linear control scheme to function quite well, but how would that performance look in 3D.
Test the robot in activities besides drilling
  How does the human effort change within the test cases with tasks like pick and place
Test greater range for damping values that could cause instability
  The paper mentions that higher damping can result in non-passive unstable systems, but they did not thoroughly investigate this with their setup
Test Robust Stability
  Evaluate the effects of disturbances, noise, feedforward, etc.

## Slide 14: Reflection
The system identification method performed here results in a system order that is exceptionally high (around 15th order) that should be discussed
Their stability maps may be incorrect or lacking information. More detail on their construction is needed. Given their data, our team has been unable rebuild identical stability maps.
They do not go in depth enough on how they perform their stability analysis besides looking at the close loop poles and potentially the phase margin.
They do not thoroughly discuss why they chose their test m’s and b’s, and the repetitions and range of their tests are quite small.
The control scheme they use focuses on an input desired human velocity that results in the same transfer function in the case they focused on an input human force. An input human force seems more intuitive and directly related the output of their results and is more applicable to other robot control schemes as is found in other related litterature.
Critiques
Keemink AQ, van der Kooij H, Stienen AH. Admittance control for physical human–robot interaction. The International Journal of Robotics Research. 2018;37(11):1421-1444. doi:10.1177/0278364918768950

## Slide 15: Conclusion
The design of this admittance controller can be used to work on higher dimension robotics applications to increase transparency. This can be applied to our Galen robot system.
The stability maps and impedance cost maps can be used in conjunction to get a measurement of transparency quality. This will help us choose and m and b.
More robust stability analysis is needed to build more accurate impedance maps and guarantee the system identified is truly stable.

## Slide 16: References
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Buerger SP and Hogan N (2007) Complementary stability and loop shaping for improved human–robot interaction. IEEE Transactions
Keemink AQ, van der Kooij H, Stienen AH. Admittance control for physical human–robot interaction. The International Journal of Robotics Research. 2018;37(11):1421-1444. doi:10.1177/0278364918768950

## Slide 17: Supplemental Material 1: Robot Control Information
Robot Type -LBR iiwa 7 R800 robot (KUKA Inc.)
Controlled through the Fast Robot Interface (FRI) and through C/C++
Joint position controller
The force data from 2 sensors acquired at 10 kHz
Control loop was updated at 500 Hz

## Slide 18: Supplemental Material 2: System Identification
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Move the arm on select frequencies between 0.01Hz to 20Hz
Identify the transfer functions for each joint.
Sum the different joint transfer functions to get G(s)
Check stability of G(s)