## Slide 1: Check Point
Students: Brevin Banks
Mentors: Ugur Tumerdem, Manish Sahu, Adnan Munawar, Mohammad Salehizadeh, Russell Taylor
Transparency Optimization of the Galen Surgical System with a Frequency Domain Admittance Controller Design

## Slide 2: Project Review & Significance
The hand over hand guidance cobot in the mock OR, the Galen Robot, is used to assist surgeons in ENT microsurgery. It assists by restricting motion through virtual fixtures and allows for steady, accurate surgeries to be performed.
In order for the surgeon to feasibly and comfortably use the device it must be what we call stable and transparent. And the current controller could be better optimized for these two variables.
Stability is achieved through observing the forces, velocities, etc. on the input and ensuring the output is bounded and behaves as predicted. (ie. No vibrations or dangerous motions)
Transparency is achieved through control schemes that measure the input human force and try to react by removing some of the impedance or resistance that would naturally be felt by the robot dynamics and actuators.
Democratizing Robotic Surgery and Microsurgery. Galen Robotics. (2022, November 15). Retrieved February 13, 2023, from https://www.galenrobotics.com/

## Slide 3: Previous Deliverables
Minimum:
A stable frequency domain admittance controller in MATLAB code for the Galen surgical robot in the AMBF simulation environment
A simulated control system package with optimized transparency containing code files that can be used in AMBF and MATLAB and is transferable to hardware
Expected:
An applied control system package to the low-level Galen controller that is stable and optimized for transparency including virtual fixtures
A validated objective improvement in transparency according to specified metrics
Maximum:
A completed user study to investigate subjective transparency preference with different controllers on the Galen robot

## Slide 4: Summary of the Efforts to Now
Verified Stable and Transparent Mass Spring Damper Simulations
Galen robot controller in AMBF through MATLAB
Simulated System Identification
Application of Admittance controller in AMBF simulation
*Starting Real Robot System Identification

## Slide 5: Mass Spring Damper Simulations
Mimic Mass Spring Damper Admittance control designs from the literature with the basic feedback controller design

## Slide 6: Mass Spring Damper Simulations: Unsuccessful Results
Ensure this optimization admittance approach was feasible for guaranteeing stability and improved transparency
Unable to replicate work of Aydin et al. Lacking in depth stability analysis and their system identification method was unclear
[2] Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Theirs
Ours

## Slide 7: Mass Spring Damper Simulations: Successful Results
Observed expected results from our own mass spring damper simulations and analysis of closed loop poles.
Result was unstable with expected unstable admittance values and stable with expected stable admittance values with simulated damping.
Stability with simulated human and environment impedance
Stability with only simulated human impedance

## Slide 8: Galen robot controller in AMBF through MATLAB
Creation of a MATLAB interface pipeline for controlling the AMBF environment with ROS Nodes
Instructions for the installation and use of the interface for the design of the admittance controller
Scaffolding for simulation’s mid-level controller. Discretization of control system at 200Hz using the Tustin transform
Admittance Discretization

## Slide 9: Galen robot controller in AMBF through MATLAB
Joint control at 200Hz with MATLAB to AMBF control interface.
Move the Galen robot like a mass by giving the 3 carriage joints identical reference velocity
Turn off gravity as a form of gravity compensation (real identified system will have it within the plant)

## Slide 10: Simulated System Identification
Identify P(s) – the robot dynamics. Assume linear even though it’s nonlinear. Okay for small steady movements. Should have transfer function similar to mass spring damper in form.
For cartesian velocity control we required the simulated Galen Jacobian. Derived forward kinematics and Jacobian for the simulated robot.
Apply input signal. Chirp input in our case. Measure output. MATLAB system Identification tools tf and ssest help find at least a 2nd order estimate for P(s)

## Slide 11: Simulated System Identification: Results
Verified Jacobian and Forward kinematics of the robot with cartesian control.
Resultant identified transfer functions
Velocity Component | Transfer Function | Quality of Match
Vx | 132.8/(s + 145.8) | 77.93%
Vy | 131.8/(s + 132.4) | 92.15%
Vz | 1.973e06/(s^2 + 1.558e04*s + 1.975e06) | 92.58%
Wx | 2.542e05/(s^2 + 153.1*s + 2.561e05) | 89.39%
Wy | 1.587e04/(s^2 + 230.7*s + 1.584e04) | 91.03%

## Slide 12: Application of Admittance Controller in AMBF
Test the stability of identified transfer functions. Find acceptable and unacceptable m_ad and b_ad values
Test in actual contact with object

## Slide 13: Application of Admittance Controller in AMBF
When in contact with the skull the stable m_ad and b_ad admittance control remains stable. The unstable m_ad and b_ad goes unstable as expected

## Slide 14: Setback discussion
Feasibility of controller design took longer than expected to validate with previous literature
System identification was not entirely conceived within the scope of this project and the deliverable for that has become more critical.
Mentors decided to move the user study for now to focus on the more pressing design of the controller and implementation virtual fixtures.

## Slide 15: Justification for Deliverables Adjustment
Implementation of velocity control in cartesian space
Simulated model differs largely from real hardware
System identification simplifies P(s)

## Slide 16: Updated Deliverables
Minimum: Due 4/18/2023
A stable frequency domain admittance controller in MATLAB code for the Galen surgical robot in the AMBF simulation environment Completed
A simulated control system package with optimized transparency containing code files that can be used in AMBF and MATLAB and is transferable to hardware Completed
Expected: Due 4/25/2023
An applied control system package to the low-level Galen controller that is stable and optimized for transparency including virtual fixtures In progress
A validated objective improvement in transparency according to specified metrics, with identified system dynamics In progress
Maximum: Due 5/5/2023
Implemented Virtual Fixtures that constrain the robot hardware within desired simulated bounds. Waiting
Extended Maximum: TBD
During the summer a completed user study to investigate subjective transparency preference with different controllers on the Galen robot Waiting

## Slide 17: Project Dependencies
Dependency | Need | Contingency Plan | Planned Deadline | Hard Deadline | Status
Access to Computer | Need a computer with a Linux platform | Use a lab computer | 8-Feb | 13-Feb | Completed
Access to Galen AMBF Model | File access and editing permissions | Create a basic 3D model and crude dynamics | 14-Feb | 20-Feb | Awaiting Files
Software Installation MATLAB SIMULINK | License | Use Lab Computer with preinstalled software | 8-Feb | 13-Feb | Completed
Software Blender and AMBF Addon | Installation Instructions | Use Lab Computer with preinstalled software | 8-Feb | 13-Feb | Completed
Galen Robot and Controller Access | Anton and Adnan complete controller pipeline for Galen task space and joint space control | Go without Galen hardware implementation. Implement on similar robot or move on without implementation | 15-Mar | 15-Apr | Completed
IRB for user study | IRB Approval | Go without the User Study | (Submission 20-Feb) 3-Apr | (Submission 24-Feb) 17-Apr | ON HOLD FOR SUMMER

## Slide 18: Previous Project Timeline
Task 1.1
Task 1.2
Task 2.1
Task 2.2
Task 2.3
Task 2.4
Task 2.5
Task 3.1
Task 3.2
Task 4.1
Task 4.2
Task 4.3
Task 4.4

## Slide 19: Previous Project Timeline
Task 1.1
Task 1.2
Task 2.1
Task 2.2
Task 2.3
Task 2.4
Task 2.5
Task 3.1
Task 3.3

## Slide 20: Updated Project Milestones (Updates in blue)

## Slide 21: Plan to Deal With Setbacks
  Working with Mohammad Wednesday 10Am to perform system identification
  Unlikely, but in the case that system identification proves problematic, we will stick to applying the controller as if it is a mass in one DOF (most likely Z)
  The controller development on the actual Galen system will be performed with the high/mid level python crtk servo cv commands
  Development of virtual fixture prototypes have already started. Use spring approximation instead of finite element method.

## Slide 22: Project Management
  Brevin – Controller Design, Implementation, Stability and Transparency Analysis.
  Weekly meetings with mentors Mondays at 1:30 PM
  See wiki for Document Control Scheme
  MATLAB functions on private GitHub as instructed by mentor. Transferring to Lab repo
  No Galen code is on that repo.
  All Galen code stays within the mock OR and the Bitbucket branch. No local versions

## Slide 23: References
Democratizing Robotic Surgery and Microsurgery. Galen Robotics. (2022, November 15). Retrieved February 13, 2023, from https://www.galenrobotics.com/
Aydin, Y., Sirintuna, D., & Basdogan, C. (2020). Towards collaborative drilling with a Cobot using admittance controller. Transactions of the Institute of Measurement and Control, 43(8), 1760–1773. https://doi.org/10.1177/0142331220934643
Keemink AQ, van der Kooij H, Stienen AH. Admittance control for physical human–robot interaction. The International Journal of Robotics Research. 2018;37(11):1421-1444. doi:10.1177/0278364918768950
Williams, R. L. (2016). The Delta Parallel Robot: Kinematics Solutions. Mechanical Engineering: Ohio University, 1–46.