## Slide 1: Recreating Pelvic Trauma Surgery in Virtual Reality Computer Integrated Surgery II, Spring, 2023 Han Zhang, Zixuan Liu, Liam Wang, Mentored by Benjamin Killeen and Dr. Mathias Unberath
Introduction
We developed a virtual reality (VR) training environment in Unity that simulates percutaneous pelvic fracture surgery under C-arm fluoroscopy. This environment would allow clinicians to practice the procedure without exposure to ionizing radiation and enable the accessible collection of detailed operation data for further analysis.
Outcomes and Results
All of our goals for the functionality of our surgical simulation were met and manually tested for correct functionality
Our software APIs are documented and we have instructions for installing and getting started with our software
Used "Walkthrough" testing method to review the system and verify the coherence of the workflow
The Problem
Percutaneous pelvic fracture is minimally invasive surgery which relies on limited X-ray guidance. Clinicians need a training environment where they can easily practice the surgery without exposure to ionizing radiation and without needing a phantom or cadaver.
Current State of Art Solution?
  Cadaveric dissection training - High Cost, Limited access
  Current VR simulation - Limitations in accuracy and user interaction
Who will benefit from our solution?
  Residents and surgeons
    VR Training without ionizing radiation and low cost
    Excellent accessibility
    Expert-generated 2D educational content
    Benefit from computer-integrated surgical support technologies as a result of simulation-collected data
  Patient
    More accurate procedures with a smaller x-ray dose
Engineering Research Center for Computer Integrated Surgical Systems and Technology
Overview of the Virtual Reality Surgical Room
The Solution
Our VR training environment for percutaneous pelvic fracture surgery has the following features:
Runtime patient and annotation loading from CT scan
Interactive C-arm and surgical tools
Network interface with DeepDRR for real-time synthetic X-ray image generation with tool interaction
Interactive Unity UI for settings and numerical feedback
K-wire insertion UI and error calculation
K-wire and tissue insertion interaction simulation
Multiplayer networking for collaborative training
Real time data logging system for user interactions and DRR images
Credits
Han - Unity Interaction, Design of surgical tool models(CAD), Tool & Tissue Interaction, and User Study
Zixuan - Annotation, Patient Loading, UI Interface, and Documentation
Liam - DeepDRR Network & Multiplayer Connection, and Data Logging.
Knowledge Gained
Collaborative Unity development
Importance of documenting interfaces between subsystems for easier collaboration
Project management and communication
Future Work
We plan to conduct a user study this summer to evaluate the effectiveness of our environment as a training tool and submit our results to IPCAI 2024
DeepDRR X-ray Image
Drill
K-Wire
C-Arm Imager
Virtual Patient
Networking Block Diagram Overview
Screw Set and Drill with K-wire
Reconstructed Patient Model and K-wire
Pelvic Annotation