## Slide 1: Making 2D/3D Registration Accessible Computer Integrated Surgery II Spring, 2023 Jiaming Zhang, Zhangcong She, under the auspices of Benjamin Killeen and Professor Mathias Unberath
Outcomes and Results
We successfully integrated SyntheX and xreg as a sole package called XREGI. The package can be installed and utilized with simple terminal commands:
XREGI provides a toolkit for processing data between every module, allowing for seamless integration and efficient data transfer.
We created documentation for both SyntheX and XREGI, providing users with the necessary resources to effectively leverage the package to accelerate their research.
Figure 4: The landmarks are detected by SyntheX and the projection matrix is solved by xreg
The Solution
The registration workflow is proposed and implemented.
Our proposed package, XREGI, is modularized into three classes, namely LandmarkDetector, RegistrationSolver and Registration2D3D.
The LandmarkDetector class and RegistrationSolver class integrate the features of SyntheX and xreg separately. The Registration2D3D computes the projection matrix by utilizing the functionalities of the other two classes.
and provides interfaces for future modularization substitution and development.
Introduction
Proposed a unified and modularized architecture in Python for solving 2D/3D registration problem.
Incorporated an AI-based 2D landmark detention model, SyntheX, with a registration solver, xreg, into an integrated pipeline.
Encapsulated the functionalities into XREGI–a Python package with highly reconfigurable architecture. With XREGI, users can streamline registration process and achieve results efficiently.
Our proposed approach simplified the tedious and time-consuming 2D/3D registration process so that it can be utilized in the intraoperative real-time applications without the need of expertize.
Problem Formulation
2D/3D registration problem is to find the projection matrix between the CT coordinate system and the X-ray frame.
The intraoperative applications of the existing 2D/3D registration solutions are limited by their incompatibility and lack of generalization.
Intraoperative registration requires the solver to automatically solve the problem in the real-time.
These issues lead to frustration and inefficiency in the registration workflow, highlighting the need for a more user-friendly and streamlined solution.
Acknowledgements
We thank Dr. Cong Gao and Dr. Robert Grupp for making the source code of SyntheX and xReg public
We thank Prof. Russel Taylor, Prof. Mathias Unberath and Benjamin Killeen for their invaluable help and guidance
Reference
[1] C. Gao, “Synthetic data accelerates the development of generalizable learning-based algorithms for X-ray image analysis”, Nature Machine Intelligence, vol. 5, no. 3, pp. 294–308, 2023.
[2] Grupp, R.B., Unberath, M., Gao, C., Hegeman, R.A., Murphy, R.J., Alexander, C.P., Otake, Y., McArthur, B.A., Armand, M. and Taylor, R.H., 2020. Automatic annotation of hip anatomy in fluoroscopy for robust and efficient 2D/3D registration. International Journal of Computer Assisted Radiology and Surgery, pp.1-11.
Future Work
Integration with novel projective paradigm to visualize the result on HoloLens
Submission to a peer-reviewed conference or journal
Lessons Learned
Having comprehensive documentation is crucial for facilitating understanding and collaboration on related projects
Credits
Jiaming: xreg integration programming
Zhangcong: SyntheX integration programming
Both team members equally contributes to maintaining the repository and writing up the documentations.
Figure 2: Basic Workflow for the Proposed 2D/3D Registration Pipeline.
Figure 1: Frame Relationship for the X-ray, CT and Patient.
Figure 3: Class diagram for XREGI. Its modularized design has made it possible for incorporating more advanced detector and solver in the future
$ pip install xregi
Notes: performance: manual, one image, batch image
synthex output
l2 norm