## Slide 1: Team 07: Real-time Integration of Fully Automatic 2D/3D Pelvic Registration with Robotic X-ray Acquisition
Students:
Jiaming Zhang
Zhangcong She
Mentors:
Benjamin Killeen
Prof. Mathias Unberath
EN 601.656 Computer Integrated Surgery II: Project Plan Presentation

## Slide 2: Background - Intraoperative Fluoroscopy
In minimally invasive surgery, clinicians use intraoperative fluoroscopy to overcome the occlusion and ascertain the poses of anatomy, surgical instruments or artificial implants[1,6].
The registration between 2D X-ray (fluoroscopy) image and 3D CT/MR images are necessary for precisely localizing the target intraoperatively.
Illustration of spine injection
Intraoperative X-ray
Illustration of spine injection
Mandell, J. C., Czuczman, G. J., Gaviola, G. C., Ghazikhanian, V., & Cho, C. H. (2017). The Lumbar Neural Foramen and Transforaminal Epidural Steroid Injections: An Anatomic Review With Key Safety Considerations in Planning the Percutaneous Approach. AJR. American journal of roentgenology, 209(1), W26–W35.
Notes: First I wanna introduce the basic knowledge of our project, which are Intrao ,Fluoro and 2d3d reg

## Slide 3: Background - 2D/3D Registration
2D/3D registration is the process that estimates the pose of the 3D objects, such as the CT, based on 2D images, such as the X-ray[3].
Image-based 2D/3D registration approach, where intraoperative X-ray images are used to solve the registration, does not require physical contact, like screws, with the anatomical ROI in the patient. In other words, it’s a fiducial-less approach.
Intensity-based registrations, which we are using in our project, rely solely on voxels and pixels of 3D and 2D images, respectively.
[3]. C. Gao, “Fluoroscopic navigation for robot-assisted orthopedic surgery,” dissertation, 2022.

## Slide 4: Clinical Motivation
Performing registration tasks relies on multiple subroutines. Yet different subroutines, i.e., packages or softwares are not well-cooperated and therefore not straightforward to use intraoperatively.
Different packages are developed under various environments and sometimes not compatible with each other[1]. Some packages are poorly documented and therefore hard to maintain and difficult to employ.
Over-complicated procedure can prolong the learning curve for users and also increase the probability of misoperation.
https://www.philips.com/a-w/about/news/home

## Slide 5: Project Goal
Our project aims to develop a pipeline that automatically perform the 2D/3D registration process between X-ray images and CT Scan intra-operatively.
  To be specific, we need to integrate the image acquisition process, data synthesizing process, landmark detection, and online registration into one sole software with a user-friendly GUI.
We also seek to visualize the data with novel projective paradiams on HoloLens.
https://www.brainlab.com/surgery-products/overview-platform-products/robotic-intraoperative-mobile-cbct/
Loop-X
HMD
Phantom

## Slide 6: Previous Work
01
SyntheX [1]
SyntheX is a novel neural network architecture developed by Dr. Cong Gao, to create realistic synthesis for X-ray image analysis. In this project, we mainly use it to generate synthetic X-ray image and to initialize automatic registration.
02
xReg[4]
A library developed by Dr. Robert Grupp, with online and intraoperative registration strategy. It leverages image intensities and CNN features to compute registration matrix between CT frame and X-ray frame.

## Slide 7: Technical Approach
Intraoperative
Preoperative
SyntheX
Manually Annotated
Total
Segmentator
xReg
Initially, we would implement a script to retrieve the X-ray image from Loop-X to local device in the real-time.
Then, the landmark detection of X-ray image would be done by applying SyntheX.
While, in preoperative period, we would apply Total segmentator to perform segmentation and manually annotate the CT scan.
Finally, processed X-ray image and CT scan would be used as input of xReg to get FX-ray,CT
Pipeline Architecture

## Slide 8: Deliverables

## Slide 9: Key Milestones
Complete documenting and organizing the SyntheX repository Mar 6 - Mar 11
Finish developing python scripts incorporates previous work Mar 23 - Mar 28
Accomplish designing and documenting automatic pipeline Mar 27 - Apr 1
Present a well-analyzed report about validating pipeline Apr 4 - Apr 10
Complete developing visualization software on HMD May 15 - May 20
Planned - expected

## Slide 10: Project Timeline

## Slide 11: Dependency
 | Need | Status | Followup | Contingency Plan | Planned | Hard DL
MOCK OR Lab Access | manipulate Loop-X | Get access | N/A | Ask Benjamin for access | Feb 06 | Feb 10
Loop-X | Generate X-ray and CT Scan | Ready to use | N/A | Ask Benjamin for access | Feb 06 | Feb 10
SyntheX | Generate Domain Generalized X-ray | Open source github repository | N/A | Request the source code from Dr. Cong Gao | Feb 01 | Feb 06
Model Checkpoint | hyper parameters of SyntheX | On private onedrive folder | Keep secured |  | Feb 08 | Feb 12
xReg | Compute registration parameter between CT scan and X-ray Image | Open source github repository | N/A | Request the source code from Dr. Grupp | Feb 08 | Feb 12
CT DataSet | As a input used in Xreg | Ready to use | Keep secured | N/A | Feb 06 | Feb 20
Total Segmentator | Do CT Scan segmentation | Open source software | Downloaded | N/A | Feb 18 | Feb 20
Computers | Our own computer with an environment for software development | Install python, C++, Unity | Ready to use | “PACKMAN” ARCADE Server | Jan 23 | N/A
HoloLens | Do mixed reality visualization | Plan to request at Mar 10 from mentor | N/A | N/A | Mar 15 | Mar 20
Unity Code for visualization | Connecting our pipeline to HMD |  | N/A | N/A | Mar 15 | Mar 20
Optional: Wifi Memory Stick | Synchronizing data | Plan to purchase | Send the request to the lab manager | Research agreement to get API of Loop-X | Mar 10 | Mar 23

## Slide 12: Responsibility Arrangement
Jiaming Zhang：
  Mainly responsible for managing SyntheX section, basically includes:
    Implement interfaces for each package for future development.
    Make a user-friendly documentation.
Zhangcong she：
  Mainly Responsible for managing Intensity-based registration section:
    Configure a proper environment for Compiling the existing functionalities of xReg.
Both of us are also responsible for pipeline design, mixed reality visualization part, including:
  Design a pipeline to automatically swap data between Loop-X, SyntheX and 2D/3D Registration.
  Implement a program to manage these packages and integrate them into a single executable application with a Graphics User Interface.
  Develop an executable application on Hololens for projective visualization

## Slide 13: Management
Meetings with Benjamin Killeen:
  3:00 pm every Monday, in-person
ARCADE Lab meetings:
  4:15 pm every Thursday, in-person
Discussions between group members:
  Twice a week, 9:30 am every Monday and Wednesday, in-person
Communication:
  Email/Discord
All files are uploaded to private repository in Github and the wiki page

## Slide 14: Reference
[1]. Gao, C., “SyntheX: Scaling Up Learning-based X-ray Image Analysis Through In Silico Experiments”, arXiv e-prints, 2022. doi:10.48550/arXiv.2206.06127.
[2]. Arcadelab, “Arcadelab/synthex,” GitHub. [Online]. Available: https://github.com/arcadelab/SyntheX. [Accessed: 21-Feb-2023].
[3]. C. Gao, “Fluoroscopic navigation for robot-assisted orthopedic surgery,” dissertation, 2022.
[4]. P. Markelj, D. Tomaževič, B. Likar, and F. Pernuš, “A review of 3D/2D registration methods for image-guided interventions,” Medical Image Analysis, vol. 16, no. 3, pp. 642–661, 2012.
[5]. R. B. Grupp, M. Unberath, C. Gao, R. A. Hegeman, R. J. Murphy, C. P. Alexander, Y. Otake, B. A. McArthur, M. Armand, and R. H. Taylor, “Automatic annotation of hip anatomy in fluoroscopy for robust and efficient 2D/3D registration,” International Journal of Computer Assisted Radiology and Surgery, vol. 15, no. 5, pp. 759–769, 2020.
[6]. Y. Otake, M. Armand, R. S. Armiger, M. D. Kutzer, E. Basafa, P. Kazanzides, and R. H. Taylor, “Intraoperative image-based multiview 2D/3D registration for image-guided orthopaedic surgery: Incorporation of fiducial-based C-arm tracking and GPU-acceleration,” IEEE Transactions on Medical Imaging, vol. 31, no. 4, pp. 948–962, 2012.