## Slide 1: Background Reading Presentation
Team: 14
Students: Anushruti Singh
Mentors: Hisashi Ishida, Adnan Munawar, Prof. Peter Kazanzides, Dr. Deepa Galaiya
Computer Integrated Surgery II

## Slide 2: About the Project
Project: Improve Content Validity of Virtual-Drilling Simulator
Project Goal: To improve the content validity of the virtual drilling simulator, specifically focusing on the sound of the drilling and force during the drilling.
Individual Goals:
1. Create a data set and utilize existing phantoms and collect sound, density and force data while drilling.
2. Model the data of sound to find patterns and extract features.
3. Implementation report of the functionality in the drilling simulator based on the modeled data.
FIVRS setup

## Slide 3: Paper Selected
Paper chosen: “Automatic Identification of Hard and Soft Bone Tissues by Analyzing Drilling Sounds” by Vahid Zakeri and Antony J. Hodgson
This paper aimed to assess whether bone drilling sounds could be used in classifying bone tissues.
It highlights how densities affect audio since the primary classifier for the bone is their density.
It also illustrates an alternate method to experiment setup.

## Slide 4: Summary
The paper, “Automatic Identification of Hard and Soft Bone Tissues by Analyzing Drilling Sounds” aimed to assess whether bone drilling sounds could be used in classifying bone tissues.
A Support Vector Machine (SVM) algorithm was trained using the acquired data and tested for two scenarios, which will be discussed in the results.

## Slide 5: Significance
1. Our project requires us to do audio signal processing to extract audio features for modelling. Extraction of audio samples and features from recordings was covered in this paper.
2. There is great potential for audio feedback in drilling procedures. Works by the same author show that these classification results were much better than the classification survey done with surgeons (which was only 51.4% for judged answers).
3. Object density can be related to pitch of drilling sound.

## Slide 6: Technical Approach
Data Collection:
Phantom Choice: Six bovine tibia pieces were drilled during the paper’s study duration.
Motion of drilling: Drilling was done perpendicular to the bone surface using a Conmed Linvatec Hall Mpower2, Pr06202M surgical handpiece. The bones were fixed in a vice.
Data Specification: The cortical (hard) and soft (cancellous) tissues of each bone were drilled three times. The cortical tissues and cancellous tissues were drilled 18 times for an average duration of 6 and 4 seconds, respectively. 36 recordings were recorded using a Briiel & Kjrer 4165 microphone.
Phantom Setup

## Slide 7: Signal Processing
Recording Specifications: The recordings were collected at 20 kHz and were analyzed in different frequency regions. The Shannon-Nyquist theorem was used to determine the maximum frequency in the spectrum.
Filtering: 5 different filtering applied -
(1) No filtering,
(2) Low-pass filtering with cutoff frequency at 4kHz,
(3) Band-pass filtering between 2 kHz to 6 kHz,
(4) Band-pass filtering between 4 kHz to 8 kHz, and
(4) High pass filtering with cutoff frequency at 6 kHz.
For 2-5, an order-3 Butterworth filter was used.

## Slide 8: Continued
Each record was windowed using a 50 ms Hamming window with a 50% overlap. The window length was relatively short as we want to distinguishing between bone tissues in a short period of time
Each data window was a sample whose class was either cortical or cancellous.
In this study, there wear a total of 7248 samples in which 4364 were cortical and 2884 were cancellous.

## Slide 9: Classification
For classification, a Support Vector Machine (SVM) algorithm with a Gaussian kernel was applied.
Two scenarios were tested out.
LOBO (leave one bone out). It considered the training set to be a recording of all bones except one, which was called the test bone (TB). The recordings of the excluded bone were considered the testing data set.
BSP (Bone Specific), considered all recordings, including TB recordings, to be part of the training set.

## Slide 10: Results
For 120 bins (640 features) extracted from the samples, BSP (Bone Specific performed better with an accuracy of 83% as compared to 70.9% accuracy in LOBO scenarios.
The variability of most statistical measures was also lower in the BSP scenario.
This study also showed that generalizability across bone specimens is reasonable, albeit not great.

## Slide 11
Sampling Frequency = 20kHz
Hard and Soft Bone Drilling
Preprocessing
Band-pass filter = 2-9kHz, Order 3 Butterworth
Windowing
Hamming window, 50 ms
Classification
Support Vector Machine
Analysis in two training/testing scenarios (LOBO, BSP)

## Slide 12: Key Takeaways
1. Audio data needs to be processed with more than just filters in order to be studied properly. Filter methods, classification algorithms and sampling should be done carefully.
2. Density plays an important role and can be used in the classification of bone types.
3. Generalizability across bone specimens is reasonable albeit not great.
4. Audio could be used as a feature for classifying bones into different types.

## Slide 13: Limitations
1. The drilling in the paper was done perpendicular to the surface of the bone. Surgeons very rarely drill at such an extreme angle, and it is possible that the recordings could be different than what a surgeon hears in an operation theatre.
2. There are various factors that affect the pitch of the recording such as RPM of the drill, drill-bit used, angle of drilling etc. The data collection procedure could have mentioned more about if these factors were kept constant when drilling.
Drilling Bone Setup

## Slide 14: References
1. Wikimedia Foundation. (2023, April 12). Nyquist–Shannon sampling theorem. Wikipedia. Retrieved April 18, 2023, from https://en.wikipedia.org/wiki/Nyquist%E2%80%93Shannon_sampling_theorem
2. Gandhi, R. (2018, July 5). Support Vector Machine - introduction to machine learning algorithms. Medium. Retrieved April 18, 2023, from https://towardsdatascience.com/support-vector-machine-introduction-to-machine-learning-algorithms-934a444fca47
3. Zakeri, V., & Hodgson, A. J. (2017). Classifying hard and soft bone tissues using drilling sounds. 2017 39th Annual International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC). doi:10.1109/embc.2017.8037452
4. Zakeri, V., & Hodgson, A. J. (2019). Automatic identification of hard and soft bone tissues by analyzing drilling sounds. IEEE/ACM Transactions on Audio, Speech, and Language Processing, 27(2), 404-414. doi:10.1109/taslp.2018.2880336
5. Mathey, J. (2012, January 25). Understanding windowing and Overlapping Analysis. Retrieved March 14, 2023, from https://blog.prosig.com/2011/08/30/understanding-windowing-and-overlapping-analysis/