## Slide 1: Improve Content Validity of Virtual Drilling Simulator
Group 14
Students: Anushruti Singh
Mentors: Hisashi Ishida, Adnan Munawar, Prof. Peter Kazanzides, Dr. Deepa Galaiya

## Slide 2: Summary
This project aimed to validate the existing sound feedback of the Fully Immersive Virtual Reality System (FIVRS).
This goal was broken down into four major components:
Data Collection
Modelling of collected data
Implementation of the function created.
Evaluation of the functionality in the simulator.

## Slide 3: Updates
During the duration of the project, it was observed that data collection involved a lot more parameters that those originally thought of.
It was decided that the deliverables would be modified to fit the duration of this course. The new milestones decided were:
Create and utilize existing phantoms and collect sound, density and force data while drilling.
Model the sound data collected.
Implementation report of the functionality in the drilling simulator based on the modeled data.

## Slide 4: Timeline (Old)

## Slide 5: Updated Timeline
Milestones:
Data Set collected
Sound Data modeled
Technical Part of the project completed.
Expected deliverables reached.
Note: The maximum deliverable cannot be achieved within the duration of this semester.
Currently

## Slide 6: Current Approach
Phantom design and trial were done according to the following parameters:
Density
RPM of drill
Length of drill bit
Angle of drill bit

## Slide 7: Current Approach
1. Density:
Density. Density " IT'IS Foundation. (n.d.). Retrieved March 29, 2023, from https://itis.swiss/virtual-population/tissue-properties/database/density
Phantom | Density (kg/)
Phantom 1 | 1084.065
Phantom 2 | 2100.3
Phantom 3 | 1630.6
Phantom | 
Phantom 1 | 1084.065
Phantom 2 | 2100.3
Phantom 3 | 1630.6

## Slide 8: Current Approach
2. RPM of the drill was kept constant at 80000.
3. The walls of the phantom were made 3cm to ensure that any drill bit could be used to take at least 10 readings on a single phantom.
4. To fix the angle of drilling, the Galen robot was used. A straight-line motion script was prepared and was used for all readings.
Initial Phantoms
Final Phantom

## Slide 9: Current Approach
Data Set 1 consists of:
1. 30 readings. 10 readings taken from each phantom.
2. Along with sound and density, the forces measured by the gamma sensor, forces by the force-sensing drill and pose of the robot tool were also collected.
3. All these readings were collected as a rosbag and an audio file.
All topics collected in the rosbag

## Slide 10: Project Status
Level | Deliverable | Expected Date of Completion | Status
Minimum | Phantom Designing and Trial. | 15 March 2023 | Completed
Minimum | Data Set Collection. | 3 April 2023 | Completed
Expected | Modeling Report for Sound Data | 15 April 2023 | In-progress
Maximum | Implementation report of functionality in drilling simulator. | 20 May 2023 | Not started

## Slide 11: Dependencies
All dependencies have been met. No delay due to unmet dependencies is expected during the duration of this project.

## Slide 12: Documentation and Next Steps
All information about phantom design can be found on the project’s wiki page.
The data set will be uploaded to Microsoft teams where it will be accessible to all members of this project as well as extended projects.
The next goal is to model the collected data. This is broken down into the following parts:
Filtering the collected data to get rid of background noise.
Extraction and plotting of useful features using signal processing. (Most likely STFTs)
Plotting of features to study relations.
Studying ML models that can be applied.

## Slide 13: Management Plan
Bi-weekly meetings with Hisashi Ishida.
On-demand meetings with Prof. Peter Kazanzides
All data collected will be uploaded onto a Microsoft Teams group that has already been created.
Communication Platforms: Microsoft Teams, Messages and Emails

## Slide 14: Thank you!