## Slide 1: IMPROVE THE CONTENT VALIDITY OF THE VIRTUAL-DRILLING SIMULATOR Computer Integrated Surgery II Spring, 2023 Anushruti Singh, under the auspices of Professor Peter Kazanzides, Adnan Munawar, Hisashi Ishida and Dr. Deepa Galaiya
Introduction
Auditory feedback has great potential in surgical simulators that aim at training surgeons associated to the correct interpretation of anatomy of sounds (Hoffmann, Pablo Faundez et al. (2009)).
This project involved collecting a data set with varying density phantoms and extract frequency and force information.
The goal of this project was to improve the auditory feedback provided in FIVRS (Fully Immersive Virtual Reality System).
Outcomes and Results
The Problem
Validating the existing audio feedback in FIVRS allows us to improve and test the accuracy of the current implementation.
Engineering Research Center for Computer Integrated Surgical Systems and Technology
The Solution
Three phantoms were used during data collection. Modeling of the collected data was performed to study the relations between density of the phantom, force applied during drilling and frequency of the drill audio.
Support by and Acknowledgements
Thank you to all my mentors for providing consistent and continuous support during the duration of this project.
Lessons Learned
Workflow of research-oriented projects
Audio processing using Librosa, SciPy and MATLAB
Force collection and extraction using ROS
Future Work
Mathematically relation and implementation of these relations into the FIVRS.
Figure 2: Data Collection Setup
Parameter | Details |  | 
RPM of Drill | 80000 revolutions per minute |  | 
Density (in kg/ | Phantom 1 (LL) 1084.065 | Phantom 2 (AVG) 1630.6 | Phantom 3 (UL) 2100.3
Orientation | Kept constant as the initial orientation. Angle of the drill with the phantom surface was kept below 90 degrees. |  | 
Motion | Single stroke motion for every reading using the Galen robot. |  | 
Parameter | Details |  | 
RPM of Drill | 80000 revolutions per minute |  | 
 | Phantom 1 (LL) 1084.065 | Phantom 2 (AVG) 1630.6 | Phantom 3 (UL) 2100.3
Orientation | Kept constant as the initial orientation. Angle of the drill with the phantom surface was kept below 90 degrees. |  | 
Motion | Single stroke motion for every reading using the Galen robot. |  | 
Figure 3: Single-sided amplitude spectrum plots and wrench-force plots
The files were synched using manual taps. Audio wave files were passed through a highpass filter with the cutoff frequency set at 8000 Hz.
The offset in the resultant of the wrench-force and torque were fixed by shifting the entire data by the minimum value of the clipped data.
Fig 1: FIVRS Setup
Issues Faced:
Synchronization of some files couldn’t be done accurately.
Filtering of the sound when the drill was on but not drilling couldn’t be done without loss of information.
Table 1: Details about the experimental procedure
Microphone
Drill mounted on Galen
Gamma
Sensor
Phantom
With increase in density, mean wrench-force value increases from 0.062 N in LL to 0.1489 N for Avg and 1.698 N in UL. We also see the amplitude increase prominently in the 8000-16000 Hz range.
(in N)
(in N)
(in N)
Frequency Analysis
Force Analysis
LL
UL
Avg