## Slide 1: DaVinci-Assisted Continuum Robot Navigation and Manipulation
Group 15: Jaspor Jiang, Chenhan Zhang, Heyun Wang
Mentors: Dr. Mohammad Salehizadeh, Anton Deguet, and Dr. Russell Taylor
February 23, 2023

## Slide 2: Introduction
Objective: a continuum robot navigation and manipulation system that combines the accuracy and reachability of the DaVinci robot arm with the unique capabilities of a tendon-driven continuum robot end.
The intended approach involves designing DaVinci Research Kit (dVRK) with a flexible robot end, and then constructing corresponding remote actuation and navigation system through ROS and Python.
Furthermore, the application will be expanded to various kinds of catheter[2] and teleoperation in surgical application domains.
DaVinci Robot: robohub.org/intuitive-surgical-da-vinci-surgical-system-gets-big-endorsement/
Acunav catheter: jnjmedtech.com/en-US/product/acunav-ultrasound-catheter​
Notes: First, let me give a brief introduction on our projects. Our goal is to built a continuum robot navigation and manipulation system, which takes advantage of both the accuracy of DaVinci research kit (also known as dvrk), and the unique capabilities and flexibility of a tenden-driven continuum robot end.
To achieve this goal, we will first generate a new design of dvrk with flexible endoscope. The most challenging part it the computer integrated functionality: where we will rebuild a corresponding system of navigation and remote actuation for the continuum robot. We will especially focus on integrating various catheters with our dvrk design, and try to apply teleoperation for surgical applications in the end.

## Slide 3: Background
Ion Inc.'s Endoluminal System[3] combines continuum robotics with Intuitive's expertise in surgical robotics to provide a high-accuracy, minimally invasive solution for lung biopsies.
The dVRK Consortium, based at JHU, has been organized by members of the dVRK community to provide technical support.
Previous work of dynamic modeling of the continuum robot end has been established.
There are currently limited applications of flexible catheters integrated with the dVRK system, highlighting the potential for further development in our project.
Ion by Intuitive: https://youtu.be/0ZaobUiJhCQ
Notes: Let me talk more on the background of our project. Our inspiration comes from the ION surgical robot, which focused on minimal invasive solutions for lung biopsy through it's flexible and accurate robotic catheter end.
Also, our project takes advantage of the DaVinci platform and dVRK resources based right at JHU, and we will receive technical training by Anton Deguet in LCSR, to build our navigation and manipulation algorithm for the dVRK. Good news is that there had been very good dynamic model of the catheter for us to identify, but the limited practical application of flexible catheters on dVRK system gives us reason and potential to fully develop our project.

## Slide 4: Significance
The proposed DaVinci-assisted continuum robot navigation and manipulation system offers better reachability and dexterity in delicate surgical robotics and improves patient outcomes.
Notes: Finally let me quickly summarize our project's highlight: As a comprehensive project with a novel design, our development of a continuum robot end and corresponding navigation system has the potential to enhance the dVRK platform.
The proposed DaVinci-assisted continuum robot navigation and manipulation system offers better reachability and dexterity in delicate surgical robotics and improves patient outcomes.

## Slide 5: Workflow
Hardware Design &
Basic Actuation
Endoscope
Acunav Catheter
dVRK baseplate
Phantom Testing (optional)
Ultrasound catheter tracking and imaging
(optional)
Minimum
Maximum
Expected
Feb.11-(4 weeks)->Mar.10
Mar.11-(4 weeks)->Apr.07
Apr.08-(4 weeks)->May.07
dVRK Navigation and Manipulation
Collect experimental data for catheter parameter identification
Friction experiment
Weight release experiment
Parameter Identification
Code development and Forward Kinematics
Inverse Kinematics and teleoperation
(optional)
Code testing
Forward Kinematics
PSM
Find a fit surgical application

## Slide 6: Proposed Technical Approach
Hardware
Comparison of two end effectors:
Endoscope catheter and Acunav catheter
 | (a) Endoscope | (b) Acunav Catheter
Driven method | Tendon | Tendon
Flexibility | Rigid rod + Flexible tip | Flexible catheter
Motion control principle | Bending in pitch, yaw, and rolling via rotary joints on the baseplate | Bending in Pitch and Yaw, rolling by DVR-K arm
Endoscope (a)
Rigid robot end
Acunav catheter (b)

## Slide 7: Forward Kinematics: Experiment to Identify Catheter Parameter
Weight Release Experiment to Identify general Catheter’s Characteristic Parameters

## Slide 8: Collecting Experimental data for Identification of Catheter Friction Model
Tendon-Driven Actuation Experiment to Identify Friction Model Parameters

## Slide 9: Computer Integrated Functionality
GUI of dVRK[4]
Robot Catheter
Forward Kinematics
dVRK actuation
Dynamic modeling
DH parameter
ROS
Match joints &
configuration space
Notes: Ask Anton on Wednesday to get picture of software gui
My availability on Wednesday before 12pm.

## Slide 10: Deliverables
Minimum (4 weeks):
Mechanical design enhancement and design innovation.
Verify the basic actuation function of dVRK with continuum end-effector through ROS and GUI.
Expected (4 weeks)：
Obtain experimental results needed for identifying catheter parameters using DaVinci platform actuation.
Code development and forward kinematics actuation based on catheter parameters
Maximum (4 weeks):
Find a fit surgical application to our DaVinci-assisted continuum robot navigation and manipulation technology and (Optional) apply it in a phantom experiment.
(Optional) Teleoperation of the catheter using DaVinci dVRK
(Optional) Control tip of ultrasound catheter to do ultrasound imaging of a phantom

## Slide 11
 |  | Timeline |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Project Mentor: Dr. Mohammad Salehizadeh, Anton Deguet, Dr. Russel Taylor | Project Leader: Whitney Russ |  |  |  |  |  | February 11 - May 5, 2023 |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | W1 11/2 17/2 | W2 18/2 24/2 | W3 25/2 03/3 | W4 04/3 10/3 | W5 11/3 17/3 | W6 18/3 24/3 | W7 25/3 31/3 | W8 01/4 07/4 | W9 08/4 14/4 | W10 15/4 21/4 | W11 22/4 28/4 | W12 29/4 05/5 | 
Minimum | Preliminary Research | Literature Review | Literature Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Complete Project Proposal | Complete Project Proposal |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Mechanical design enhancement and designs innovation | Connection mechanism design | Connection mechanism design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Prototyping & testing | Prototyping & testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Verify the basic actuation function of dVRK with continuum end through ROS and GUI. | Training and get access of DaVinci operation | Training and getting access to DaVinci operation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Learning to control DaVinci Arm through GUI | Learning dVRK navigation through GUI and ROS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Design the mechanism and workflow of catheter motion control | Actuating the dVRK with continuum end-effector |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Expected | Obtain experimental results needed for identifying catheter parameters | ROS and dvr-k learning for DaVinci control | Setup experiments of the Acunav catheter |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Test and integrate the algorithm on DaVinci robot | Applying the experiment data to pre-defined model to get catheter parameters |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Code development and forward kinematics actuation based on catheter parameters | Design and setup experiments of the ultrasound catheter | Constructing the initial state of forward kinematics |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Integrate algorithms enable precise actuation of continuum effector |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Maximum | Find a fit surgical application |  | Find a fit surgical application to our DaVinci-assisted continuum robot navigation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Apply the experiment data to pre-defined model to get catheter parameters | Teleoperation of the catheter using DaVinci dVRK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Control tip of Acunav catheter to do ultrasound imaging of a phantom |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Timeline

## Slide 12: Key dates
 | Milestones | Output (submit in the team’s chat) | Deadline | Status
Minimum | Complete project proposal | 5-8 pages summary | Feb.23 | Done on Feb.22
Flexiblity | Prototyping & testing | An Acunav Catheter that can be controlled mechanically by DaVinci | Mar.10 | In progress
Motion | Actuating the dVRK with continuum end | Video about actuating the continuum end by dVRK | Mar.10 | In progress
Expected | Obtain experimental results for parameter identification | PDF document and data visualizations | Mar.24 | Waiting
 | Integrate algorithms enable precise actuation of continuum ends | PDF document and code with comments | Apr.07 | Waiting
Maximum | Find a fit surgical application | PDF document | May.07 | Waiting

## Slide 13: Dependencies
Dependency | Need | Contingency plan | Planned | Hard | Status
End-effectors for testing | DaVinci dVRK, endoscope and Acunav catheter | dVRK in Robotrium | Feb.27 | Feb.29 | Acquiring
Access to hardware Models | CAD Model of Acunav catheter and DaVinci baseplate | Manually measurement and modeling | Feb.27 | Feb.29 | Acquiring files
Software installation: ROS, Python, CISST library | License | Use Lab Computer with pre-installed software | Feb.24 | Feb.27 | Acquired
Access to dVRK | Access and training from Anton Deguet | N/A | Feb.25 | Mar.02 | Acquired
Identification experiments | Two EM tracker sensors Optical marker Test weights | from LCSR repository | Apr.07 | Apr.17 | Acquired
Phantom | Testing | Go without phantom testing | Apr.22 | Apr.27 | Waiting

## Slide 14: Management
Weekly meetings
  Student team meeting: brainstorming, third times a week
  Lab meeting: dVRK training
  Mentor meeting: progress report, 3:30 PM-5:30 PM each Friday
Platforms:
  Zoom, Email: communication
  Github: codes
  Microsoft Teams: communication, documentation

## Slide 15: Acknowledgement
We would like to thank Professor Emad Boctor for generously providing us with the Acunav ultrasound catheter.

## Slide 16: Reading list
Jessica Burgner-Kahrs, D. Caleb Rucker, and Howie Choset. 2015. Continuum Robots for Medical Applications: A Survey. Trans. Rob. 31, 6 (Dec. 2015), 1261–1280. https://doi.org/10.1109/TRO.2015.2489500
T. Kato, I. Okumura, S. -E. Song, A. J. Golby and N. Hata, "Tendon-Driven Continuum Robot for Endoscopic Surgery: Preclinical Development and Validation of a Tension Propagation Model," in IEEE/ASME Transactions on Mechatronics, vol. 20, no. 5, pp. 2252-2263, Oct. 2015, doi: 10.1109/TMECH.2014.2372635.
P. Kazanzides, Z. Chen, A. Deguet, G. S. Fischer, R. H. Taylor and S. P. DiMaio, "An open-source research kit for the da Vinci® Surgical System," 2014 IEEE International Conference on Robotics and Automation (ICRA), Hong Kong, China, 2014, pp. 6434-6439, doi: 10.1109/ICRA.2014.6907809.
Kesner SB, Howe RD. Position Control of Motion Compensation Cardiac Catheters. IEEE Trans Robot. 2011 Jul 21;PP(99):1-11. doi: 10.1109/TRO.2011.2160467. PMID: 21874124; PMCID: PMC3160644.
An Open-Source Research Kit for the da Vinci Surgical System, Kazanzides P, Chen Z, Deguet A, Fischer GS, Taylor RH, DiMaio SP, ICRA 2014, May 2014.
Cha H-J, Yi B-J, Won JY. An assembly-type master–slave catheter and guidewire driving system for vascular intervention. Proceedings of the Institution of Mechanical Engineers, Part H: Journal of Engineering in Medicine. 2017;231(1):69-79. doi:10.1177/0954411916679328

## Slide 17: Reference
[1] Tobe, Frank. “Intuitive Surgical Da Vinci Surgical System Gets Big Endorsement and New Competition.” Robohub, https://robohub.org/intuitive-surgical-da-vinci-surgical-system-gets-big-endorsement/.
[2] “Acuson AcuNav™ Ultrasound Catheter.” Biosense Webster, https://www.jnjmedtech.com/en-US/product/acunav-ultrasound-catheter.
[3] “Ion by Intuitive | Robotic Bronchoscopy Platform for Nodule Biopsy.” YouTube, YouTube, 4 May 2019, https://www.youtube.com/watch?v=0ZaobUiJhCQ&feature=youtu.be.
[4] JHU-dVRK. DaVinci Research Kit. GitHub, https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki.

## Slide 18: Thank You!

## Slide 19: Appendix I: Motion Control Principle for Semi-Flexible Endoscope
[P3]Rolling（1 DOF）
Pulleys:
P1 P2
P3 P4
[P1]Pitch upwards (0.5 DOF)
[P1]Pitch downwards (0.5 DOF)
[P2]Yaw upwards (0.5 DOF)
[P2]Yaw upwards (0.5 DOF)
Total：3 DOF

## Slide 20: Appendix II: Motion Control Principle for Flexible Acunav Catheter
Pulleys:
P1 P2
P3 P4
[P1]Pitch upwards (0.5 DOF)
[P3]Pitch downwards (0.5 DOF)
[P2]Yaw upwards (0.5 DOF)
[P4]Yaw upwards (0.5 DOF)
Total：3 DOF
[DVRK]Rolling（1 DOF）