## Slide 1: Automatic Calibration of an FBG-based Force-Sensing Instrument for Intraocular Surgery
Nili Abtahi
Mentors: Prof. Iulian Iordachita, Mojtaba Esfandiari
April 2023

## Slide 2: Background
Overview
Importance
Limitations

## Slide 3: Paper 1:
A Sub-Millimetric 3-DOF Force Sensing Instrument with Integrated Fiber Bragg Grating for Retinal Microsurgery

## Slide 4: Paper 1 Overview:
Objective
Approach & Methods
Results & Conclusions
Critical Assessment

## Slide 5: Paper 1: Approach & Methodology
01
Design & Calibration
Linearity
Sensitivity
Repeatability

## Slide 6: Paper 1: Approach & Methodology
02
Performance
Temperature
Strain
Bending
Simulating retinal microsurgery conditions

## Slide 7: Paper 1: Results & Conclusions
The results showed that the FBG-based force-sensing needle had good linearity, sensitivity, and repeatability.
However, the calibration process was manual, time-consuming, and affected by the operator's skill and experience. The study also found that temperature, strain, and bending significantly influenced the sensor's performance, necessitating their consideration during the calibration process.

## Slide 8: Paper 1: Critical Assessments
Strengths
The paper demonstrates the feasibility of using FBG-based force-sensing needles in retinal microsurgery.
detailed description of the calibration process and the factors affecting the sensor's performance.
The experimental evaluation of the force-sensing needle under simulated retinal microsurgery conditions strengthens the study's findings.
The manual calibration process is time-consuming and relies on the operator's skill and experience, which can affect the accuracy and reliability of the measurements.
The study uses a single FBG sensor, which may limit the potential to capture the full range of forces and effects during surgery.
Critique

## Slide 9: Paper 2:
A Multi-Function Force Sensing Instrument for Variable Admittance Robot Control in Retinal Microsurgery 2

## Slide 10: Paper 2 Overview:
Objective
Approach & Methods
Results & Conclusions
Critical Assessment

## Slide 11: Paper 2: Approach & Methodology
01
Calibration
Tip-Force Calibration
The force sensing instrument is mounted on a calibration stand, and a known force is applied to the instrument's tip in each direction.
The sensor readings are recorded and compared to the known forces to find the relationship between the sensor output and the actual force applied.
on the next step calibration matrix is generated, which relates the sensor readings to the actual forces in each direction. This matrix will be used to convert the sensor readings to force values

## Slide 12: Paper 2: Approach & Methodology
01
Calibration
Sclera-Force Calibration
The force sensing instrument is equipped with additional sensors to measure the forces applied to the sclera during the surgical procedure.
A controlled experiment is conducted, where known forces are applied to the sclera, and the corresponding sensor readings are recorded.
Similar to the tip force calibration, a calibration matrix is generated for the sclera forces, enabling the conversion of sensor readings to actual force values during the surgery.

## Slide 13: Paper 2: Approach & Methodology
02
Validation
Conducting a series of experiments on artificial retina models where the force sensing instrument was used to measure the forces exerted during simulated surgical procedures.
The results of these experiments showed that the force sensing instrument accurately measured tip force and sclera force and provided real-time feedback to the robotic control system

## Slide 14: Paper 2: Results & Conclusions
Sensitivity: 150 mN
Linearity: 99.4 %
Repeatability
Tip Force: 5 mN
Sclera Force: 10 mN
proposed calibration process provides a reliable and accurate method for ensuring the accuracy and reliability of force measurements!

## Slide 15: Paper 2: Critical Assessments
Strengths
Well-structured and comprehensive approach to developing a force sensing instruments
thorough description of the design, implementation, and validation of the proposed instrument
The method is limited to a specific needle design, which may not be suitable for all surgical instruments. This highlights the need for a more versatile calibration method that can be easily applied to different instrument designs.
The requirement of a large training dataset for calibration may not be practical in some clinical settings, as it can be time-consuming and resource-intensive to collect the necessary data. This suggests the need for a more efficient calibration method that can achieve high accuracy with a smaller dataset.
Critique

## Slide 16: Overall Evaluation
Two research papers have contributed to the development of needles that can measure force during eye surgery using Fiber Bragg Grating (FBG) sensors.
The calibration process in these studies was either time-consuming and required skilled operators
limited to a specific needle design with a large training dataset.
Also, they did not provide a detailed procedure for the calibration process, making it difficult for inexperienced individuals to do it properly.

## Slide 17: Next Steps
Development of clear and standardized procedure
Adaptation to different needle designs
Investigating different algorithms and temperature compensation technique
Experimental validation
Design of user-friendly GUI/App

## Slide 18: References
X. He, J. Handa, P. Gehlbach, R. Taylor, and I. Iordachita, “A Sub-Millimetric 3DOF Force Sensing Instrument with Integrated Fiber Bragg Grating for Retinal Microsurgery,” IEEE Transactions on Biomedical Engineering, vol. 61, no. 2, pp. 522 – 534, 2014.
X. He, M. Balicki, P. Gehlbach, J. Handa, R. Taylor, and I. Iordachita, “A MultiFunction Force Sensing Instrument with Variable Admittance Robot Control for Retinal Microsurgery,” IEEE International Conference on Robotics and Automation (ICRA), Hongkong, China, May 31-June 7, 2014.
I. I. Iordachita, M. D. De Smet, G. Naus, M. Mitsuishi and C. N. Riviere, "Robotic Assistance for Intraocular Microsurgery: Challenges and Perspectives," in Proceedings of the IEEE, vol. 110, no. 7, pp. 893-908, July 2022, doi: 10.1109/JPROC.2022.3169466.
Zhenglong Sun, M. Balicki, Jin Kang, J. Handa, R. Taylor and I. Iordachita, "Development and preliminary data of novel integrated optical micro-force sensing tools for retinal microsurgery," 2009 IEEE International Conference on Robotics and Automation, Kobe, Japan, 2009, pp. 1897-1902, doi: 10.1109/ROBOT.2009.5152836.

## Slide 19: Copyright The Johns Hopkins University 2022. All rights reserved.