## Slide 1
Automatic Calibration of an FBG-based Force-Sensing Instrument for Intraocular Surgery
Johns Hopkins University
Laboratory for Computational Sensing and Robotics
Nili Abtahi
Mentors: Prof. I. Iordachita, Mojtaba Esfandiari
Feb 2023
Notes: 1

## Slide 2
Motivation
Challenges in eye surgery:
The eye is a highly delicate and complex organ
Any deviation in needle trajectory can cause significant consequences
High risk of retinal tears (vision loss)
Limited access to different areas of the eye
Manual Dexterity

## Slide 3
Motivation
Why Needle Calibration?
* Precision:
Calibration of the needle helps to ensure that it is accurately positioned and moved with precision, which can help to minimize the risk of complications and improve surgical outcomes.
* Accuracy:
Calibration helps to ensure that the needle is accurately positioned, which can help to minimize damage to surrounding tissue and improve the success of the procedure.
* Real-time visualization:
Calibration of robotic surgical systems in retinal surgery often involves the use of advanced imaging technologies, such as OCT. These technologies provide real-time visualization of the retina and guide the placement of the needle, allowing the surgeon to make precise and accurate movements.
* Efficiency:
Calibration of needles in retinal surgery can help to improve the efficiency of the procedure by reducing the need for manual adjustments and reducing the time required for surgery. This can lead to shorter operating times and reduced risk of complications.

## Slide 4
Prior work
Accuracy and Precision
Calibration
To increase tissue safety and excessive force prevention
Force-sensing Tools
Iordachita et al. (2014)
Tang et al. (2017)
Choi et al. (2018)
He et al. 2014 (JHU)
Gibels et al. 2015, (Leuven University)
Ginenc et al. 2017 (JHU)

## Slide 5
Eye Robot (SHER 2.1)​,Scale, Force-sensing needle​,FBG Interrogator ​
​
System Setup

## Slide 6
Background
Enlarged needle and FBG fiber
Expansion/contraction of FBG causes shift in wavelength. The theory for finding calibration process which relates these wavelengths to interaction forces was developed by He et al, 2014
2-DOF Pick Tool
FBG sensors

## Slide 7
The first step of the technical plan is to design and fabricate the experimental setup for calibrating the force-sensing instrument.
Technical Overview

## Slide 8
Overview
Calibration of the force-sensing instrument: The second step is to calibrate the force-sensing instrument using the experimental setup and automatic data analysis framework.
The final step is to validate the calibration results using a separate validation dataset. This involves applying known loads to the instrument and comparing the resulting sensor output to the expected values.

## Slide 9
Overview
courtesy of Changyan He

## Slide 10
Deliverables
Minimum:
Experimental setup and documented calibration procedure
Automatic data analysis framework
Calibration of the force-sensing instrument
Validation of the results
Expected:
Software Requirements Specification (SRS)
GUI Design Documents
GUI Prototype
Source Code

## Slide 11
Deliverables
Maximum:
Develop a mobile application for tele-calibration

## Slide 12
Eliminate the effect of temperature changes on the FBG sensors by using methods such as neural network or other forms of analysis.
Until now, we have obtained an algebraic and first-order relationship between the FBG sensors and the force values ft, fs, which is a comprehensive and complete model because non-linear functions are not possible for FBGs.
Factorial experiments can be used to reduce the amount of time required for calibration in this project by identifying the most important factors that affect the accuracy of the force-sensing instrument, and optimizing these factors using a minimum number of experiments.
Future Work

## Slide 13
Dependencies

## Slide 14
Timeline

## Slide 15
Reading material
X. He, J. Handa, P. Gehlbach, R. Taylor, and I. Iordachita, “A Sub-Millimetric 3-DOF Force Sensing Instrument with Integrated Fiber Bragg Grating for Retinal Microsurgery,” IEEE Transactions on Biomedical Engineering, vol. 61, no. 2, pp. 522 – 534, 2014.
.2018.8600861.
H. Zhang et al., "An FBG-Based 3-DOF Force Sensor With Simplified Structure for Retinal Microsurgery," in IEEE Sensors Journal, vol. 22, no. 15, pp. 14911-14920, 1 Aug.1, 2022, doi: 10.1109/JSEN.2022.3187771.
K. Song, D. A. Lezcano, G. Sun, J. Seob Kim and I. I. Iordachita, "Towards Automatic Robotic Calibration System for Flexible Needles with FBG Sensors," 2021 International Symposium on Medical Robotics (ISMR), Atlanta, GA, USA, 2021, pp. 1-7, doi: 10.1109/ISMR48346.2021.9661542.

## Slide 16
References
X. He, M. Balicki, P. Gehlbach, J. Handa, R. Taylor, and I. Iordachita, “A Multi-Function Force Sensing Instrument with Variable Admittance Robot Control for Retinal Microsurgery,” IEEE International Conference on Robotics and Automation (ICRA), Hongkong, China, May 31-June 7, 2014.
I. I. Iordachita, M. D. De Smet, G. Naus, M. Mitsuishi and C. N. Riviere, "Robotic Assistance for Intraocular Microsurgery: Challenges and Perspectives," in Proceedings of the IEEE, vol. 110, no. 7, pp. 893-908, July 2022, doi: 10.1109/JPROC.2022.3169466.
Zhenglong Sun, M. Balicki, Jin Kang, J. Handa, R. Taylor and I. Iordachita, "Development and preliminary data of novel integrated optical micro-force sensing tools for retinal microsurgery," 2009 IEEE International Conference on Robotics and Automation, Kobe, Japan, 2009, pp. 1897-1902, doi: 10.1109/ROBOT.2009.5152836.