## Slide 1
Tele-operation Control of a High Dexterity Robot for Vitreoretinal Surgery
Team 21: Xiao Wei
Mentors: Mojtaba Esfandiari, Adnan Munawar, Dr. Iulian Iordachita

## Slide 2: Project Summary
Goal: To implement a simulation of a combined teleoperation system using the Asynchronous Multi-Body Framework (AMBF)
Build a model of the snake robot in Blender based on the CAD drawing and connect it in the simulation
Develop an AMBF plugin to manipulate the snake robot attached to SHER and interact with the OCT scan of the eye
Develop a control algorithms to control the snake robot using the feedback of haptic device
Fig. Envisioned high dexterity intraocular manipulator (Shi, K., 2022)

## Slide 3: Paper detail
Title: Fully Immersive Virtual Reality for Skull-base Surgery: Surgical Training and Beyond
Authors: Munawar A, Li Z, Nagururu N, et al
Journal: arXiv preprint arXiv:2302.13878 (2023)
Relevance:
  Apply the volumetric drilling simulation for certain kind of surgery
  Control the virtual drill using the haptic device
Fig. Hardware setup (Munawar, A., 2023)
Notes: The paper is named “: Fully Immersive Virtual Reality for Skull-base Surgery“ and is published on 阿开v this year.
This paper is closely relevant to our research interests. First, We are using the same volumetric drilling plugin, the author apply the plugin for skull-base surgery, our project is used for retinal surgery.
Also, the propose is the same. We all need to control the virtual drill using the haptic device.

## Slide 4: Technical Approach
FIVRS comprises of several software and hardware components aimed at providing
  a realistic user interface
  visual fidelity
  extensive data generation and recording
Fig. System architecture
Notes: The “simulation system” consists of several different hardware and software components which are presented in this Fig.
It provides realistic and immersive surgical simulation environment that allows users to practice surgical procedures with haptic feedback and real-time tissue deformation.
And it aims at providing a realistic user interface, visual fidelity and extensive data generation and recording.

## Slide 5: User Interaction and Interface
Head Mounted Display
  Use a VR headset to resemble a high-resolution stereo microscope used in traditional skull-base surgeries
Modelling drill types
  4 drill types (1, 2, 4, 6 mm)
  Adjust different bone removal rate (BRR) from surgeon feedback
GUI
  Deploy a user-friendly interface instead of typing in the Linux command line
Fig. Graphical User Interface (GUI)
Notes: The system did a good job at user interaction and interface.
For example, the author use a VR headset to resemble the microscope used in traditional skull-base surgeries.
And they also modelled 4 drill types and adjust different BRR from surgeon feedback.
What’s more, they design a user-friendly interface to ease the manipulation instead of typing in the Linux command line

## Slide 6: Visual Fidelity
Smoothing
  A volumetric ray casting approach implemented on the GPU and summarized in Algorithm 1
Shadow
  Implemented shadow mapping to the rendered volume to improve depth perception
Fig. Comparison of smoothing(up)/shadows(down) off and on
Improvement due to surgeons’ feedback:
unnatural artifacts and edges on the anatomical structures
challenges in accurately perceiving depth
mediocre illumination and shading
Notes: They also did improvement in visual fidelity due to surgeons’ feedback, such as unnatural artifacts and edges, hard to perceive depth and not enough illumination and shading.
To solve the above problem, they improve from two aspects.
And we can see from the two figures of comparison
To make the model look smoother, they use a volumetric ray casting approach shown as the algorithm here
To increase the shading, they implemented shadow mapping

## Slide 7: Data Generation and Management
Importing Anatomical Scans
  Develop a program that converts the data in “seg.nrrd” format to an array of images to ease the incorporation into FIVRS
Ground Truth Data Storage
  includes a pair of videos (from stereo cameras), real-time depth point cloud, segmentation mask, and kinematic and dynamics data of scene objects
Fig. Asynchronous data from FIVRS
Notes: The format is obtained in 3D Slicer, where each segment is either one hot encoded into a separate grid layer or labeled incrementally.
To make it easier to incorporate it to the simulation system, the author developed a program that converts the data to an array of images.
Another notable features of FIVRS is its ability to generate multi-modal ground truth data which can be used for future test and improvement.

## Slide 8: Experiment
Goal: Perform an initial validation of the system and the recorded data
Participants: 7 participants including 3 attending surgeons 3 residents and 1 medical student
Methods：Operate on multiple anatomies
Results:
  Temporal, kinematic and dynamics data for each participant
  Visualization of volume removed
Notes: In this paper they designed an experiment to perform an initial validation of the system and the recorded data
There are 7 participants included to operate on multiple anatomies.
The upper figure shows the recorded data while the below one is the visualization of volume removed. Colors other than bone represent unintended removal of structures.

## Slide 9: Critical Review
Pros:
  The author does a good job at integrating hardware and software of the system
  FIVRS provides a realistic “simulation system” for skull-surgery
  And it offers an extensive data generation and recording interface using an industry standard format
Cons:
  Small sample size and limited diversity
Key takeaway:
  Improvements on visual fidelity
  User-friendly interfaces and interaction
  Clear data management

## Slide 10: Conclusion
The framework established by the paper is applicable to our project
The simulation of virtual drilling can be an effective tool for surgical training and planning

## Slide 11: Reference
[1] Munawar, A., Li, Z., Nagururu, N., Trakimas, D., Kazanzides, P., Taylor, R. H., & Creighton, F. X. (2023). Fully Immersive Virtual Reality for Skull-base Surgery: Surgical Training and Beyond. arXiv preprint arXiv:2302.13878.
[2] Munawar, A., Li, Z., Kunjam, P., Nagururu, N., Ding, A. S., Kazanzides, P., ... & Unberath, M. (2022). Virtual reality for synergistic surgical training and data generation. Computer Methods in Biomechanics and Biomedical Engineering: Imaging & Visualization, 10(4), 366-374.

## Slide 12
THANKS