## Slide 1
Tele-operation Control of a High Dexterity Robot for Vitreoretinal Surgery
Team 21: Xiao Wei
Mentors: Mojtaba Esfandiari, Adnan Munawar, Dr. Iulian Iordachita

## Slide 2: Clinical motivation
Vitreoretinal surgery is highly delicate and difficult
exceptional precision on micron scale targets
in a constrained and fragile workspace
Challenges
physiological hand tremor
forces that are imperceptible by human result in retinal tears
(Hani S., 2022)

## Slide 3: Project Summary
Goal: To implement a simulation of a combined teleoperation system using the Asynchronous Multi-Body Framework (AMBF)
Develop a simulation model for the Eye Robot and the Eye Snake systems in AMBF
Use AMBF plugin to manipulate the snake robot attached to SHER and interact with the OCT scan of the eye
Develop a control algorithms to control the snake robot using the feedback of haptic device
Fig. Envisioned high dexterity intraocular manipulator (Shi, K., 2022)

## Slide 4: Deliverables
Minimum (90%)
Develop a simulation model for the Eye Robot and the Eye Snake systems in AMBF
- Learn AMBF + ADF + Blender addon
- Learn about how to use different plugins
- Get familiar with volume and 3D scans
Expected (60%)
Develop and implement a control algorithm on the AMBF model using a haptic device
Maximum
Implement the controller on the real robots

## Slide 5: Minimum - Simulation models
· Three translational DoFs (‘X’,‘Y’,‘Z’)
· Two rotational DoFs (‘Roll’, ‘Pitch’)
Notes: The SHER has five actuated degrees of freedom. It is comprised of three translational DoFs (‘X’,‘Y’,‘Z’) and two rotational DoFs (‘Roll’, ‘Pitch’)

## Slide 6: Minimum - Simulation models
Clinicians can insert surgical tools into it without large translational movement by the SHER
Notes: RCM stands for Remote Center of Motion. By using it, … .
Here we can see in the simulation, when we drag the slider or the rod connected to the slider, the end effector will move. In this way, it only has one DoF.

## Slide 7: Minimum - Simulation models
Enlarged version for better view

## Slide 8: Expected - Controller
Forward kinematics
Transformation between the global reference frame and the tool tip
1. SHER
3 linear transformations and 2 rotational transformations representing the joint motion between the positions of each joint. (see robot joint file)
2. I2RIS
q6: bending about the I2RIS Y-axis
q7: bending about the I2RIS X-axis
As a result, ±45° bending range
3. Frames of reference
Fig 1. Virtual joint representation(Shi, K., 2022)
Fig 2. Frames
Notes: F is the transformation between the global reference frame and the tool tip.
We can calculate this by multiplying the forward kinematics functions of the SHER and I2RIS robots respectively.
For ease of computation, multiple frames of reference were used to make it easy to perform relative additions and subtractions.
The two frames (’Eye’ and ’Robot’) use the following variables to describe the configuration.

## Slide 9: Further work
1. (Minimum) Make the snake robot interact with the eyeball model
2. (Expected) Implement the controller through haptic device and SHER system
More details about the plugin: https://github.com/htp2/continuum-manip-volumetric-drilling-plugin
Convert the eyeball model to AMBF volumes
Use AMBF plugin to manipulate the snake robot attached to SHER and interact with the OCT scan of the eye
Coordinates registration of Fphantom and FSHER
Real-time control test

## Slide 10: Milestones
Milestone | Start Date | End date | Buffer date | New date
Learn AMBF + Blender | 02/20 | 02/27 | N/A | DONE
Learn about different AMBF plugins | 02/27 | 03/13 | N/A | DONE
Incorporate eye robot and snake robot in AMBF | 03/13 | 03/27 | 04/03 | DONE
Develop a controller using haptic device | 04/3 | 04/17 | 04/27 | 04/30
Implement controller on real robot | 04/11 | 04/23 | 04/28 | 05/07

## Slide 11: Timeline
* The shaded regions of the timeline represent the buffer period.
Tasks | 2/20 | 2/27 | 3/6 | 3/13 | 3/20 | 3/27 | 4/3 | 4/10 | 4/17 | 4/23 | 4/30 | 5/7
Learn AMBF + ADF + Blender addon |  |  |  |  |  |  |  |  |  |  |  | 
Learn about how to use the plugin (volumetric_drilling) |  |  |  |  |  |  |  |  |  |  |  | 
Get familiar with volume and 3D scans |  |  |  |  |  |  |  |  |  |  |  | 
Learn other plugins related to snake robot and UR5 |  |  |  |  |  |  |  |  |  |  |  | 
Implement and incorporate eye robot and snake robot in AMBF |  |  |  |  |  |  |  |  |  |  |  | 
Develop a controller for the combined teleoperation of the eye robot and snake robot (using haptic device) |  |  |  |  |  |  |  |  |  |  |  | 
Implement the controller on the real robots |  |  |  |  |  |  |  |  |  |  |  | 
Develop comprehensive report and documentation |  |  |  |  |  |  |  |  |  |  |  | 
Previous
Modified

## Slide 12: Dependencies
Dependency | Status | Point of Contact | Fallback/Contingency measure | Need by date | Result in case of failure
Eye Robot accessibility | Readily available | Mojtaba Esfandiari / Dr. Iordachita | No contingency | N/A | N/A
Snake Robot accessibility | Readily available | Mojtaba Esfandiari / Dr. Iordachita | No contingency | N/A | N/A
Phantom Omni | Available | Mojtaba Esfandiari / Dr. Iordachita | No contingency | N/A | N/A
Snake robot CAD models | Obtained | Mojtaba Esfandiari / Dr. Iordachita | No contingency | 03/13/2023 | Delay in the implementation of the simulation
Access to robotorium | Obtained | Mojtaba Esfandiari | No contingency | 03/06/2023 | N/A
Access to snake robot plugin | Obtained | Adnan Munawar | No contingency | ongoing | N/A
CT data / the loop X machine | Not yet obtained ( Have stl model of eyeball instead ) | Mojtaba Esfandiari / Dr. Iordachita | If no CT data, use the loop X machine to collect the eyeball 3D scan | 03/20/2023 | 

## Slide 13: Documentation
All scripts and model files are uploaded on GitHub. ( link see wiki page)

## Slide 14: Management plan
Meeting
Weekly meetings with Mojtaba Esfandiari and Adnan Munawar on Wednesday afternoon 3-4 pm
Bi-weekly meetings with Prof. Iulian Iordachita on Friday afternoon (Time may change due to schedule).
Communication
Maintain communication on Microsoft Teams
Files are stored and shared through OneDrive and GitHub

## Slide 15: References
Shi, K., Zhou, Y., Ebrahimi, A., Li, G., & Iordachita, I. (2022, April). Optimization-based Concurrent Control of a High Dexterity Robot for Vitreoretinal Surgery. In 2022 International Symposium on Medical Robotics (ISMR) (pp. 1-7). IEEE.
Munawar, A., Wang, Y., Gondokaryono, R., & Fischer, G. S. (2019, November). A real-time dynamic simulator and an associated front-end representation format for simulating complex robots and environments. In 2019 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS) (pp. 1875-1882). IEEE.

## Slide 16
THANKS