## Slide 1
Tele-operation Control of a High Dexterity Robot for Vitreoretinal Surgery
Team 21: Xiao Wei
Mentors: Mojtaba Esfandiari, Adnan Munawar, Dr. Iulian Iordachita

## Slide 2: Clinical motivation
Vitreoretinal surgery is highly delicate and difficult
exceptional precision on micron scale targets
in a constrained and fragile workspace
Challenges
physiological hand tremor, causing blindness
forces > 7.5 mN that are imperceptible by human result in retinal tears
(Hani S., 2022)

## Slide 3: Background
Steady Hand Eye Robot (SHER)
Filter physiological tremor affects
2 DoF Integrated Robotic Intraocular Snake (IRIS)
A more flexible end-effector for increased intraocular reach
6 DoF Phantom Omni device
Control the position and orientation of the tool tip
Fig. Envisioned high dexterity intraocular manipulator (Shi, K., 2022)

## Slide 4: Goals
To implement the simulation of the combined teleoperation system in Asynchronous multi-body framework (AMBF) *
* More detailed information about AMBF is on the website https://github.com/WPI-AIM/ambf/wiki

## Slide 5: Technical Approach
Blender addon
To ease the creation of multi-body config files
Plugins
To modify volumes with a virtual drill in the simulation
Control Algorithms
To develop forward kinematics and calibrate the motion
(Munawar, A., 2022)
(Shi, K., 2022)

## Slide 6: Deliverables
Minimum
Developing a simulation model for the Eye Robot and the Eye Snake systems in AMBF
- Learn AMBF + ADF + Blender addon
- Learn about how to use various plugin
- Get familiar with volume and 3D scans
Expected
Develop and implement a control algorithm on the AMBF model using a haptic device
Maximum
Implement the controller on the real robots

## Slide 7: Dependencies
Dependency | Status | Point of Contact | Fallback/Contingency measure | Need by date | Result in case of failure
Eye Robot accessibility | Readily available | Mojtaba Esfandiari / Dr. Iordachita | No contingency | N/A | N/A
Snake Robot accessibility | Readily available | Mojtaba Esfandiari / Dr. Iordachita | No contingency | N/A | N/A
Phantom Omni | Available | Mojtaba Esfandiari / Dr. Iordachita | No contingency | N/A | N/A
Eye robot and snake robot CAD models | Not yet obtained | Mojtaba Esfandiari / Dr. Iordachita | No contingency | 03/13/2023 | Delay in the implementation of the simulation
Access to robotorium | Obtained | Mojtaba Esfandiari | No contingency | 03/06/2023 | N/A
Access to snake robot plugin | Obtained | Adnan Munawar | No contingency | ongoing | N/A
CT data / the loop X machine | Not yet obtained | Mojtaba Esfandiari / Dr. Iordachita | If no CT data, use the loop X machine to collect the eyeball 3D scan | 03/20/2023 | 

## Slide 8: Timelines
* The shaded regions of the timeline represent the buffer period.

## Slide 9: Milestones
Milestone | Start Date | End date | Buffer date
Learn AMBF + Blender | 02/20 | 02/27 | N/A
Learn about different AMBF plugins | 02/27 | 03/13 | N/A
Incorporate eye robot and snake robot in AMBF | 03/13 | 03/27 | 04/3
Develop a controller using haptic device | 04/3 | 04/17 | 04/27
Implement controller on real robot | 04/11 | 04/23 | 04/28

## Slide 10: Management plan
Meeting
Weekly meetings with Mojtaba Esfandiari and Adnan Munawar on Tuesday afternoon 3-4 pm
Bi-weekly meetings with Prof. Iulian Iordachita on Friday afternoon (Time may change due to schedule).
Communication
Maintain communication on Microsoft Teams
Files are stored and shared through OneDrive and GitHub

## Slide 11: References
Roizenblatt, M., Edwards, T. L., & Gehlbach, P. L. (2018). Robot-assisted vitreoretinal surgery: current perspectives. Robotic Surgery: Research and Reviews, 1-11.
Fleming, I., Balicki, M., Koo, J., Iordachita, I., Mitchell, B., Handa, J., ... & Taylor, R. (2008). Cooperative robot assistant for retinal microsurgery. In Medical Image Computing and Computer-Assisted Intervention–MICCAI 2008: 11th International Conference, New York, NY, USA, September 6-10, 2008, Proceedings, Part II 11 (pp. 543-550). Springer Berlin Heidelberg.
“The peripheral aspects of vitreoretinal surgery,” Centre for Sight, 07-Mar-2020. [Online]. Available: https://www.centreforsight.net/blog/the-peripheral-aspects-of-vitreoretinal-surgery/. [Accessed: 01-Mar-2022].
“Eye anatomy,” Glaucoma Research Foundation. [Online]. Available: https://www.glaucoma.org/glaucoma/anatomy-of-the-eye.php. [Accessed: 01-Mar-2022].
Shi, K., Zhou, Y., Ebrahimi, A., Li, G., & Iordachita, I. (2022, April). Optimization-based Concurrent Control of a High Dexterity Robot for Vitreoretinal Surgery. In 2022 International Symposium on Medical Robotics (ISMR) (pp. 1-7). IEEE.
Munawar, A., Wang, Y., Gondokaryono, R., & Fischer, G. S. (2019, November). A real-time dynamic simulator and an associated front-end representation format for simulating complex robots and environments. In 2019 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS) (pp. 1875-1882). IEEE.
Munawar, A., Li, Z., Kunjam, P., Nagururu, N., Ding, A. S., Kazanzides, P., ... & Unberath, M. (2022). Virtual reality for synergistic surgical training and data generation. Computer Methods in Biomechanics and Biomedical Engineering: Imaging & Visualization, 10(4), 366-374.
(unpubl. MS)Mojtaba, E., Yanlin, Z..(2023). A Data-Driven Model with Hysteresis Compensation for I2RIS Robot. In 2023 International Conference on Robotics and Automation(ICRA). IEEE.
[References should be alphabetized and in APA style. Additional reference examples]