## Slide 1: Design of a Robotic System for Ultrasound-Guided Central Line Placement
Students: Kesi Liang, Pranathi Golla, Xuanning Liu
Mentors: Dr. Axel Krieger, Lidia Al-Zogbi, Dr. Vinciya Pandian, Dr. Mathias Unberath, Wenhao Gu

## Slide 2: Clinical Background
Centrally Inserted Central line Catheters (CICCs) are inserted into a central vein to administer medication, nutrition etc. into bloodstream.
The most commonly used CICC is the non-tunnelled catheter.
The procedure has 4 standard access points: jugular, subclavian, femoral and arm veins.
Y. Haddadin, P. Annamaraju, and H. Regunath, “Central line associated blood stream infections,” in StatPearls, StatPearls Publishing, 2017.

## Slide 3: Motivation for automating
Central lines can introduce microorganisms that can cause infections:
  result in increased healthcare costs, and even death.
  Therefore, a robotic system can minimise the risk of infection and reduce healthcare costs.
The procedure of central line placement can be physically and mentally demanding for clinicians:
  requires a steady hand, precise movements and focus.
  Hence, a robotic system can assist clinicians with these tasks.
Rupp, Mark E., and Rajendra Karnatak. "Intravascular catheter–related bloodstream infections." Infectious Disease Clinics 32, no. 4 (2018): 765-787.

## Slide 4: Workflow
The procedure of the central line placement after the determination of the insertion site using ultrasound may be summarised as follows:
Needle insertion: the needle is inserted at the site
Guidewire insertion: the guidewire is inserted through the needle
Needle retraction: the needle is retracted at the site
Dilator insertion: a dilator is inserted to make space for the catheter
Catheter insertion: the catheter is threaded over the guidewire
Guidewire retraction: the guidewire is finally removed and the catheter is secured
J. R. Roberts and J. R. Hedges, Roberts and Hedges’ clinical procedures in emergency medicine E-book. Elsevier Health Sciences, 2013.
Seldinger Technique for Central Intravenous (IV) Line Placement (ebmconsult.com)
Notes: Preparation: Sterilize the patient, workspace, and the robot
• Ultrasound preparation: Apply ultrasound gel and place the probe on the area of interest
• Robot setup: The clinician set the target point and insertion angle. The robot arm is positioned to perform the needle insertion.
• Needle insertion: The robot performs the needle insertion under the guidance of the ultrasound image. The clinician monitors the robot and ensures the needle is properly positioned.
• Guidewire insertion: The robot inserts the guidewire through the needle, and maintains a grip on the wire. Then the clinician removes the needle.
• Catheter insertion: The robot threads the catheter over the guidewire and advances it into the vein. The clinician stops the insertion when the catheter is in the proper position. Then the clinician removes the guidewire.
• Secure placement: The catheter is secured in place with sutures or adhesive, and a dressing is applied over the insertion site.
Details such as Anesthesia and dilation are not mentioned but will be perform by clinician

## Slide 5: Prior Work
Zevallos et al. developed a robotic system for teleoperated needle insertion.
  It consists of a UR3e robotic arm to hold the needle insertion mechanism and the ultrasound probe.
  Limitations: the robotic setup is bulky and challenging to use, and the setup can be used only for femoral access.
Reuben et. al proposed the HaemoBot robotic system
  It incorporates AI and ML to improve the accuracy and success rate of intravenous (IV) catheterization.
  Limitations: The device can be used only for the hand.
N. Zevallos, E. Harber, K. Patel, Y. Gu, K. Sladick, F. Guyette, L. Weiss, M. R. Pinsky, H. Gomez, J. Galeotti, et al., “Toward robotically automated femoral vascular access,” in 2021 International Symposium on Medical Robotics (ISMR), pp. 1–7, IEEE, 2021
R. D. Brewer, “Improving peripheral IV catheterization through robotics: From simple assistive devices to a fully-autonomous system,” 2015.

## Slide 6: Objectives
Overall, the objective of the project is to enhance the accuracy and safety of central line placement and improve patient safety and outcomes.
Develop a prototype of a light-weight and bed- or table-mountable robotic system for non-tunnelled central line catheter placement through the jugular vein for:
  Needle insertion
  Guidewire insertion
  Catheter insertion
Test the accuracy and safety of the system
Workflow documentation for easy integration into clinical practice
Notes: comparing the outcomes of central line placement using the proposed system to the outcomes of traditional central line placement methods.

## Slide 7: Technical Approach
Determine device design specifications:
  Weight and Size
  Mounting design
  Form of actuation
Start design for jugular insertion, adaptable to other insertion locations
Design high-level and low-level specifications
Synthesise design using computer-aided design (CAD) software
Design controller for robot
User-friendly software showing real-time ultrasound images
Registration between image and actuator coordinates
Actuator precisely controls needle movement to desired location under ultrasound imaging
Clinician can stop the insertion if needed
Clinicians input
Robot actuation
Image capturing
User interface
Ultrasound Leadership Academy: Central Line Placement — EM Curious
Notes:   High-level design: overall architecture of the system
  Low-level design: detailed components and subsystems of the device
internal jugular vein (IJV)
carotid artery (CA)

## Slide 8: Testing Plan
Design validation:
  Validate the design using computer simulations
  Ensure that the robot’s kinematic designs are correct
Functional testing:
  Conduct functional testing of prototype
  Ensure robot can accurately and reliably perform the necessary movements and actions
Performance testing:
  Test the robot in a laboratory or simulated clinical environment
  Ensure that it can perform central line placement accurately and consistently
  Involve measuring the robot performance metrics, such as accuracy, precision, and speed
Issue identification and resolution:
Identify and address any issues or problems that arise during testing
Blue Phantom™ Internal Jugular Central Line Ultrasound Manikin | AED Superstore - BPIJ500
Notes: Design validation:
  Validate the design using computer simulations or models to ensure that the robot can effectively perform the central line placement operation.
Functional testing:
  Conduct functional testing to ensure that the robot can accurately and reliably perform the necessary movements and actions.
Performance testing:
  Test the robot in a laboratory or simulated clinical environment to ensure that it can perform central line placement accurately and consistently. This would involve measuring the robot's performance against established performance metrics, such as accuracy, precision, and speed.
Issue identification and resolution:
  Identify and address any issues or problems that arise during testing.
Throughout the testing process, the robot's performance would be monitored and evaluated to ensure that it meets the required standards for central line placement. The testing process would be iterative, with any issues or problems addressed and resolved before moving on to the next phase of testing. Ultimately, the goal of testing is to ensure that the robot can perform central line placement accurately, reliably, and safely in a clinical setting.

## Slide 9: Deliverables

## Slide 10: Dependencies

## Slide 11: Timeline

## Slide 12: Roles & Responsibilities
Team Member
• Kesi Liang (kliang19@jhu.edu)
MSE BME Student, first-year Responsible for the registration of the robotic system w.r.t. ultrasound image, calibration of the ultrasound probe, software development, and system integration.
• Pranathi Golla (pgolla1@jhu.edu)
MSE ME Student, first-year
Responsible for the Kinematic design of the mechanism, 3D printing of the parts of the mechanism and motor control using Arduino.
• Xuanning Liu (xliu226@jhu.edu)
MSE ME Student, first-year
Responsible for the CAD model design of the robotic system, and the workflow development.
The team will also have some shared responsibilities, which are the design specifications, the prototype assemble, and testing.

## Slide 13: Management Plan
• Meeting plan
(1) Mentor meeting
Time: Tuesday 10:00 - 11:00
Location: Zoom or Hackerman 116
Weekly meeting scheduled with Lidia Al-Zogbi and Wenhao Gu, Dr. Axel Krieger will attend the meeting biweekly
(2) Group meeting
Time: Thursday 10:00 - 11:00
Location: Zoom or Hackerman 136
Weekly meeting scheduled for three group members
• Communication platform
Slack, Zoom, Overleaf, Dropbox, Email

## Slide 14: References
[1] A. Tse and M. A. Schick, “Central line placement,” in StatPearls, StatPearls Publishing, 2022.
[2] Y. Haddadin, P. Annamaraju, and H. Regunath, “Central line associated blood stream infections,” in StatPearls, StatPearls Publishing, 2017.
[3] V. Chopra and I. Davidson, “Central venous access: Device and site selection in adults,” in UpToDate, UpToDate Publishing, 2022.
[4] E. Cheung, M. O. Baerlocher, M. Asch, and A. Myers, “Venous access: a practical review for 2009,” Canadian Family Physician, vol. 55, no. 5, pp. 494–496, 2009.
[5] J. R. Roberts and J. R. Hedges, Roberts and Hedges’ clinical procedures in emergency medicine E-book. Elsevier Health Sciences, 2013.
[6] N. Zevallos, E. Harber, K. Patel, Y. Gu, K. Sladick, F. Guyette, L. Weiss, M. R. Pinsky, H. Gomez, J. Galeotti, et al., “Toward robotically automated femoral vascular access,” in 2021 International Symposium on Medical Robotics (ISMR), pp. 1–7, IEEE, 2021.
[7] R. D. Brewer and J. K. Salisbury, “Visual vein-finding for robotic iv insertion,” in 2010 IEEE International Conference on Robotics and Automation, pp. 4597–4602, 2010.
[8] A. I. Chen, M. L. Balter, T. J. Maguire, and M. L. Yarmush, “Deep learning robotic guidance for autonomous vascular access,” Nature Machine Intelligence, vol. 2, no. 2, pp. 104–115, 2020.
[9] Brattain LJ, Pierce TT, Gjesteby LA, Johnson MR, DeLosa ND, Werblin JS, Gupta JF, Ozturk A, Wang X, Li Q, Telfer BA, Samir AE, “AI-Enabled, Ultrasound-Guided Handheld Robotic Device for Femoral Vascular Access,” Biosensors, vol. 11, no. 12, 2021.
[10] R. D. Brewer, “Improving peripheral iv catheterization through robotics: From simple assistive devices to a fully-autonomous system,” 2015.

## Slide 15
There are different kinds of CICCs: Non-tunnelled CICC, Tunnelled CICC, Peripherally Inserted Central line Catheter (PICC), Implanted port.
The choice of CICC depends on the individual patient’s needs and medical condition.
Y. Haddadin, P. Annamaraju, and H. Regunath, “Central line associated blood stream infections,” in StatPearls, StatPearls Publishing, 2017.

## Slide 16: Design Specifications
Precision and accuracy: robot should avoid puncturing the carotid artery
Patient diversity: designing the robot for patients of all gender, and age
Infection risk reduction:
  Reducing the risk of infections by avoiding contact between the clinicians and the tools
  Sterilizing the robot system properly
Minimum mechanisms:
  Designing a robot with minimum mechanisms
  Switch between different insertion objects (needle, guidewire, and catheter)
Notes: Precision and accuracy: Ensuring precise and accurate needle insertion, guidewire advancement, and catheter insertion procedures.
Vascular anatomy: Navigating through the complex vascular anatomy of the jugular vein while avoiding possible complications, such as puncturing the carotid artery or the lung.
Patient diversity: Designing the robot for patients of all anatomy, gender, age, and sex.
Infection risk reduction: Reducing the risk of complications like infections by avoiding contact between the clinicians and the parts of the Catheterisation kit.
Minimum mechanisms: Designing a robot with minimum mechanisms for the different procedures of needle insertion, guidewire advancement, and catheter insertion.
Guidewire retention: Holding the guidewire in place while the catheter is being inserted to prevent the patient from inhaling it.
The proposed robotic system must overcome these challenges to be successful in clinical practice.