## Slide 1: Simulation-Based Uncertainty Propagation in Geometric Networks for Surgical Robotics
X.M. Christine Zhu
Mentor: Dr. Russell H. Taylor
Reference:
Barfoot, T. D., and Furgale, P. T., “Associating uncertainty with three-dimensional poses for use in estimation problems,” IEEE Transactions on Robotics, vol. 30, no. 3, pp. 679–693, Jun. 2014, doi: 10.1109/TRO.2014.2298059.
Notes: Tip: If you want to update this template with your division or center logo, navigate to View > Slide Master and edit the template from there.

## Slide 2: MOTIVATION & GOAL
Surgical robotic systems rely on multiple geometric components:
  Robots, tracking systems, anatomy, sensors, etc.
Each component introduces uncertainty:
  Calibration error
  Measurement noise
  Kinematic modeling error
These uncertainties interact through geometric composition
Core problem:
There is no unified, general framework to model and query uncertainty propagation across an arbitrary geometric network.
Project Goal:
Develop a general simulation framework that models and propagates uncertainty through a network of geometric relationships, enabling uncertainty queries between any two nodes.
Note from 2025 CIS I course
Notes: Kinematic modeling error

## Slide 3: Background & Relevance
In surgical robotics, a robot arm is a chain of coordinate frames — each joint, sensor, and rigid link introduces measurement noise.
The classical approach attaches a covariance matrix to a pose written as a position vector and Euler angles, then propagates it through linearized Jacobians. This breaks down because the rotation group SO(3) is a nonlinear manifold — a Gaussian distribution defined on Euler-angle coordinates is geometrically incorrect and degrades with large rotations.
This paper directly solves that problem, and its solution is the exact mathematical foundation of our project
T. D. Barfoot and P. T. Furgale, "Associating Uncertainty With Three-Dimensional Poses for Use in Estimation Problems," IEEE Transactions on Robotics, vol. 30, no. 3, pp. 679–693, June 2014. DOI: 10.1109/TRO.2014.2298059

## Slide 4: Paper’s Goals & Contributions
Central goal:
Given a 4×4 homogeneous transformation matrix T in SE(3), derive a rigorous and practical way to attach a covariance matrix and propagate it through rigid-body compositions.
Key contribution:
The paper establishes a principled framework for associating Gaussian uncertainty with 3D poses on , and shows how to propagate and fuse that uncertainty accurately in estimation problems.

## Slide 5: Experimental Validation in paper
This paper does not present a physical robot or clinical experiment.
Instead, it validates the proposed uncertainty framework through three simulation-based estimation studies, always comparing analytic approximations against Monte Carlo ground truth.
Main Takeaway
The experiments show that uncertainty in 3D poses should be handled using the geometry of , and that higher-order or sampling-based methods can give much better accuracy than simple first-order approximations.

## Slide 6: Compound Pose Experiment
Two uncertain poses are composed, and covariance is propagated through the pose chain.
Methods compared: second-order, fourth-order, and sigma-point approximations versus 1,000,000-sample Monte Carlo.
Result: all methods work well for small uncertainty, but as uncertainty increases, the fourth-order approximation is most accurate.
Barfoot, T. D., and Furgale, P. T., “Associating uncertainty with three-dimensional poses for use in estimation problems,” IEEE Transactions on Robotics, vol. 30, no. 3, pp. 679–693, Jun. 2014, doi: 10.1109/TRO.2014.2298059.

## Slide 7: Pose Fusion Experiment
Several noisy pose estimates of the same true pose are fused using an iterative Gauss–Newton method on .
Performance is evaluated using final cost and RMS pose error over many random trials.
Result: more iterations and a better Jacobian inverse approximation improve performance, with benefits largely saturating after a few terms.
Barfoot, T. D., and Furgale, P. T., “Associating uncertainty with three-dimensional poses for use in estimation problems,” IEEE Transactions on Robotics, vol. 30, no. 3, pp. 679–693, Jun. 2014, doi: 10.1109/TRO.2014.2298059.

## Slide 8: Stereo Camera Experiment
Pose and landmark uncertainty are propagated through a nonlinear stereo camera model.
Methods are again compared with a large Monte Carlo reference.
Result: the sigma-point method best matches Monte Carlo for both projected mean and covariance under strong nonlinearity.
Barfoot, T. D., and Furgale, P. T., “Associating uncertainty with three-dimensional poses for use in estimation problems,” IEEE Transactions on Robotics, vol. 30, no. 3, pp. 679–693, Jun. 2014, doi: 10.1109/TRO.2014.2298059.

## Slide 9: Results
Method | Small uncertainty | Medium | Large
First-order | ~1% error | ~3% | ~15%
Second-order | ~0.3% | ~1% | ~3%
Sigma-point | ~0.4% | ~1% | ~4%
Key findings:
For small perturbations (sub-mm, sub-degree), first-order and sigma-point methods both match Monte Carlo to within ~1% — sufficient for surgical robotics
Second-order correction improves accuracy significantly at large uncertainties
Sigma-point and second-order methods are proved to be algebraically equivalent for pose compounding — not just empirically similar

## Slide 10: How I Use These Results
Paper result | How it is used in my project
T=exp(δξ∧)Tnominal​,δξ∼N(0,Σ) | UncertainTransform(Fnom, C) — left-perturbation convention throughout
Σc = Σa + Ad(Ta)·Σb·Ad(Ta)T | Chain propagation in query() / query_frame(), validated in validate_open_chain_mc.py
Information-form fusion Σfused = inverse(ΣΣk⁻¹) | Extended to S-matrix for paths sharing physical edges — prevents double-counting of shared uncertainty, the main gap left open by the paper
Cpost = (C0⁻¹ + HT Cnoise⁻¹ H)⁻¹ | Loop closure conditioning in condition_on_loop(), validated in validate_closed_loop_mc.py
The S-matrix extension is the primary novel contribution of my project beyond Barfoot & Furgale: when two paths share a physical edge, their uncertainties are correlated and the simple information-form sum overcounts the shared uncertainty. The S-matrix captures these off-diagonal cross-covariances and gives the correct fused result.

## Slide 11: Strengths & Weaknesses
Strengths
Mathematically rigorous — no gimbal lock, no coordinate singularities, valid for any rotation magnitude
Closed-form formulas that are directly implementable — now the standard reference in robotics state estimation
Naturally extends to kinematic chains of any length via the adjoint composition rule
Consistent with Kalman filter theory — unifies pose uncertainty with decades of prior estimation work
Forms the backbone of Barfoot's textbook State Estimation for Robotics

## Slide 12: Strengths & Weaknesses
Weaknesses
Gaussian approximation still breaks down for very large uncertainties (near-90° rotation variance)
Does not handle joint distributions of correlated poses — Mangelson et al. (TRO 2020) identified this gap, which is exactly what the S-matrix in this project addresses
Assumes Gaussian noise throughout — cannot represent multimodal or heavy-tailed errors from backlash, friction, or calibration drift common in real surgical instruments
Left vs. right perturbation convention ambiguity causes inconsistencies across the literature

## Slide 13: Key Takeaways
Pose uncertainty must live in the Lie algebra se(3) to be geometrically correct — this is the foundational insight of the paper
The adjoint map is the SE(3) predict step — it is the correct and complete tool for propagating covariance through rigid-body chains
Information-form fusion is the SE(3) update step — optimal when paths are independent; this project extends it to the correlated case
First-order linearization is sufficient for surgical robotics applications (sub-mm, sub-degree regime)
The paper leaves the shared-edge correlation problem open — the S-matrix in this project is the direct fix
The experiments show that uncertainty in 3D poses should be handled using the geometry of , and that higher-order or sampling-based methods can give much better accuracy than simple first-order approximations.

## Slide 14: Reference
T. D. Barfoot and P. T. Furgale, "Associating Uncertainty With Three-Dimensional Poses for Use in Estimation Problems," IEEE Transactions on Robotics, vol. 30, no. 3, pp. 679–693, June 2014. DOI: 10.1109/TRO.2014.2298059

## Slide 15: Thank You!
X.M. Christine Zhu
xzhu83@jhu.edu
Notes: Tip: There’s no need to include WWW or HTTPS in front of your URL.