## Slide 1: Visual Annotation of Clinically Important Anatomical Landmarks for VitreoRetinal Surgery
Project Update
Vincent Ng

## Slide 2: Retina Project Overview
Registration
  Preoperative images to intraoperative images
  Overlay of landmarks on live microscopic feed
Requirements
  Image Matching/Tracking
Images courtesy of Rogerio Richa

## Slide 3: Relevance
3
Solution:
Annotations overlay on video
Surgeon annotates preoperative image
Problem:
Mentally track notes & locations during surgery, adding significant load to the already challenging surgical task.
Slide taken from Rogerio Richa’s presentation
Notes: Surgeon annotates preoperative image
Problem:
Mentally track notes & locations during surgery, adding significant load to the already challenging surgical task.

## Slide 4: Process
RANSAC/Homography – 25 – 200ms
SURF Feature Extraction – 50ms
Match Features using NCC – 50-500ms
Overlay Result

## Slide 5: Milestones & Progress
Working SURF detection/matching program, preop/intraop processing | 
Validation using test/non-surgical data | 
Integrating program onto platform | 
Validation using real intra-operative data | Week of April 25th
Real-time tracking through speedup | Week of April 25th
Week of March 28th
Week of March 14th

## Slide 6: Dependencies
Access to platform (machine, microscope) | 
Fundus image for phantom | 
Intraoperative data from surgeons | 

## Slide 7: Results/Video

## Slide 8: Next steps / Plan Updates
Speedup
  Image size reduction
Phantom/Real data testing
Algorithm Updates
  NCC
    Takes too long
  Homography (planar projection)
    Too many degrees of freedom
  Determine optimal settings
    SURF Hessian threshold
    NCC threshold
    Number of SURF feature points per landmark

## Slide 9: Updated Timeline Below
Task | 21-Feb | 28-Feb | 7-Mar | 14-Mar | 21-Mar | 28-Mar | 4-Apr | 11-Apr | 18-Apr | 25-Apr | 2-May
Presentation and Proposal |  |  |  |  |  |  |  |  |  |  | 
Feature detection and Matching |  |  |  |  |  |  |  |  |  |  | 
Validation |  |  |  |  |  |  |  |  |  |  | 
Intra-Intra image processing |  |  |  |  |  |  |  |  |  |  | 
Preop Image Processing |  |  |  |  |  |  |  |  |  |  | 
Annotation registration |  |  |  |  |  |  |  |  |  |  | 
GUI |  |  |  |  |  |  |  |  |  |  | 
Hardware Acceleration |  |  |  |  |  |  |  |  |  |  | 
Final Poster |  |  |  |  |  |  |  |  |  |  | 
Documentation |  |  |  |  |  |  |  |  |  |  | 
Task | 21-Feb | 28-Feb | 7-Mar | 14-Mar | 21-Mar | 28-Mar | 4-Apr | 11-Apr | 18-Apr | 25-Apr | 2-May
Presentation and Proposal |  |  |  |  |  |  |  |  |  |  | 
Feature detection and Matching |  |  |  |  |  |  |  |  |  |  | 
Validation |  |  |  |  |  |  |  |  |  |  | 
Intra-Intra image processing |  |  |  |  |  |  |  |  |  |  | 
Preop Image Processing |  |  |  |  |  |  |  |  |  |  | 
Annotation registration / GUI |  |  |  |  |  |  |  |  |  |  | 
Updates to Algorithm |  |  |  |  |  |  |  |  |  |  | 
Hardware Acceleration |  |  |  |  |  |  |  |  |  |  | 
Final Poster |  |  |  |  |  |  |  |  |  |  | 
Documentation |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Difficulties so far/future
Validation
  How?
  Sensitivity of tracking to change?
Speed
  200ms – slow ?
Real data

## Slide 11: What’s Next
Working SURF detection/matching program, preop/intraop processing | 
Validation using test/non-surgical data | 
Integrating program onto platform | 
Validation using real intra-operative data | Week of April 25th
Real-time tracking through speedup | Week of April 25th
Week of March 28th
Week of March 14th

## Slide 12: What’s Next: Deliverables
Minimum
  Utilize, understand and implement SURF
  Test/Validate program using manually picked annotations as ground truth
  Data: Surgical and non-surgical
Expected
  Simple GUI that marks annotation for surgeon
  Initial Image processing for real surgery data
Maximum
  Deploy solution into OR.
  Integrate fundus/OCT data to surgeon’s screen

## Slide 13: Documentation
Updates to the wiki
Documented Code
  Comments
  Well structured, portable (CISST Filters)
Image taken from CISST website
https://trac.lcsr.jhu.edu/cisst/wiki/cisstStereoVisionTutorial

## Slide 14: Questions?
Thank You