## Slide 1
Existing breast screening methods use low-dose radiation resulting in increased cancer risk.
Many third world countries lack the medical facility and expertise.
Aim
Develop a simple, low-cost and low-risk vest for automated detection of breast lumps
Methods
  High density Fabric pressure sensor is used to measure the surface features.
  1:6 multiplex Analog to Digital conversion circuit is used to read output voltage into Matlab.
  Lump is detected and localized by interpolation, thresholding and connected component search.
  Lump type is determined using stiffness estimations by first principles and trained classifier outputs.
  Lumps are visualized in Matlab GUI after background subtraction.
Results
  Sensitivity: depth (d) < 6 mm: 78 %
6 mm < d > 10 mm: 37%
Design and Fabrication of Tactile Method for Breast Lump Detection
Member(s): Amrita Krishnaraj
Mentor(s): Dr. Jeremy Brown, Dr. Nitish Thakor
Group ID: 16