## Slide 1: DL-based extraction of respiratory motion for interventional cone-beam CT
Clinical Motivation
Motion artifacts can confound 3D image quality in interventional cone-beam CT (CBCT) and inhibit precise image guidance.
Complex, deformable anatomical motion is especially challenging, but may be addressed using a recently developed “3D auto-focus” method.
I.J. Lee, et al. Cardiovasc. Intervent. Radiol. 38(5) (2015)
Siemens Healthineers

## Slide 2: DL-based extraction of respiratory motion for interventional cone-beam CT
Description
“3D auto-focus” deformable motion compensation for CBCT requires benefits from an accurate initialization of gross anatomical motion.
This project will use deep learning (DL) techniques to automatically extract the respiratory signal directly from CBCT projection data.
ROI-wise Motion Trajectories
3 DoF Translation (mm)
3 DoF Rotation (deg)
0
Nk
Projection View (k)
knot N
Cost Function
Multi-ROI Autofocus Metric
Temporal Regularization
Spatial Regularization
+
CMAES - Optimization iteration (, )
Uncompensated Volume
ROI 1
ROI M
Motion Compensated Volume
Converged?
Yes
No
4D Motion Vector Field
k
Warped Back Projector
X-ray source
Detector
Back projected ray
Uncompensated
Motion Compensated

## Slide 3: DL-based extraction of respiratory motion for interventional cone-beam CT
What Students Will Do:
Develop a simulation framework to generate realistic cone-beam CT projection data from CT volumes
  The simulator will be based on Monte Carlo and analytical methods, using existing tools.
Generate a collection of synthetic CBCT datasets with physiologically realistic motion patterns including: respiratory, cardiac, peristaltic…
Design a CNN to extract the respiratory signal characteristics from the projection data
Train and validate the network on simulated data
Perform a validation experiment on phantom or clinical data with controlled, realistic motion
Input
Uncompensated
Output
Amplitude Map
8x8 ROIs
7x7 conv, ch 1, /2
+
1x1 conv, ch
Batch Normalization
ReLU
1x1 conv, ch
Batch Normalization
ReLU
3x3 conv, ch
Batch Normalization
ReLU
1x1 conv, ch
ResBlock
Avg pool, /2
ResBlock, ch 64
Avg pool, /2
ResBlock, ch 32
Avg pool, /2
1x1 conv, ch 1

## Slide 4: DL-based extraction of respiratory motion for interventional cone-beam CT
Deliverables
Minimum: Develop the simulation pipeline, synthetic motion database, and CNN design.
Expected: Validate in simulation data and basic phantom experiment.
Maximum: Apply the algorithm to interventional CBCT data.
Group size: 2 - 3
Skills
Programming skills, Python and Matlab.
Knowledge of signal processing.
Basic knowledge of machine learning (and CNNs in particular).
Mentors
Dr. Alejandro Sisniega, Dr. Jeffrey H. Siewerdsen
Contact
Dr. Alejandro Sisniega (asisniega@jhu.edu)