## Slide 1: Vision Guided Mosquito Dissection for the Production of Malaria Vaccine
Nick Greene
Project Group 5
Checkpoint Presentation
Mentors: Balazs Vagvolgyi, Alan Lai, Parth Vora

## Slide 2: Backgound
Sanaria has developed practical and effective malaria vaccines which could be critical in the global fight against malaria [1] [5]
Currently, production of malaria vaccine is heavily bottlenecked by manual extraction of mosquito salivary glands
Ongoing development of an automated robot system for the mosquito salivary gland extraction
[1] Jongo et al. 2018
[5] Sanaria
Source: JHU
Source: JHU
Source: JHU

## Slide 3: Goals
Implement vision algorithms with both machine learning and conventional image processing:
Tasks are:
    Check if turntable cleaning was successful at the cleaning station
    Check if gripper has mosquito parts stuck to it
    Estimate the volume of the mosquito extrudate
Integrate these algorithms with the current system

## Slide 4: Significance
The computer vision methods are essential for reliable and efficient operation of the system.
  Also useful for analysis and monitoring of the system
The system could eventually lead to significantly higher production of malaria vaccine to fight malaria globally
Cartoon Sources:
https://evil.fandom.com/wiki/Guillotines
https://www.shutterstock.com/image-vector/cartoon-mosquito-character-vector-illustration-285430751
https://www.cnet.com

## Slide 5: Machine Setup / Demonstration
All Images from JHU
except where noted
Cutting Station
Squeezing Station
Cleaning Station

## Slide 6: System Integration
The vision algorithms will be integrated with the existing system through the use of ROS Services.
  ROS Service will be implemented in C++
  for OpenCV and Python for PyTorch
Camera
Robot System
Computer
Vision Computer
PyTorch
OpenCV
Compare and Validate
Actuators
Ros Service Request
image
Ros Service Response
Network
final result
commands
image
image
output
output
All Images from JHU
except where noted

## Slide 7: Turntable Cleaning - Image Processing
Image Processing method is 98% accurate on the dataset.
Mosquitos Segmented by filtering/thresholding
  Threshold of final segmented area determines if the slot is clean
All Images from JHU
except where noted

## Slide 8: Turntable Cleaning – Image Processing
Mosquito Segmentation
  Convert Image to HSV color space
  Set value channel to 100%
  Convert back to RGB,
  Threshold by color
Image Source: http://www.ece.northwestern.edu/
All Images from JHU
except where noted

## Slide 9: Segmentation – Image Processing
Specular Reflection Segmentation
  Perform a brightness threshold and subtract from previous result
    Remove specular reflections which interfere with the segmentation
  Only consider predefined region of interest
  Gaussian and Median filtering used to clean up the results more
All Images from JHU
except where noted

## Slide 10: More Work – Image Processing
Detect pipe features with a Hough Transforms to register a mask for a more precise region of interest
Not used in the end
All Images from JHU
except where noted

## Slide 11: Volume Estimation – Image Processing
Two subtasks: classification and segmentation
Both subtasks completed with color thresholding and median blur filtering
Squeezing Station Exudate Segmentation
Squeezing Station Exudate Classification
All Images from JHU
except where noted

## Slide 12: Turntable Cleaning - Deep Learning
Transfer learning with VGG16 pretrained on ImageNet
Dataset Size was about 300
100% accuracy on the Test set
98.6% accuracy on the entire dataset
  False positive rate was 0.6%
  False negative rate was 0.6% over the whole dataset.
Network Failures
Deep Learning Training Images
All Images from JHU
except where noted

## Slide 13: Gripper Cleaning – Deep Learning
Again a VGG16 transfer learning model was used
Dataset size was about 600
95.4% accuracy on the test set
98.3% accuracy over the entire dataset
  0.6% false positive rate
  1.05% false negative rate
All Images from JHU
except where noted

## Slide 14: Deliverables
 | Activity | Deliverable | Original Expected Deadline | Status
Min | Collect images of cleaning station and annotate | Annotated cleaning station dataset | 3/1 | Completed
 | Implement image processing method for cleaning station | Functioning image processing based code and high quality documentation in a wiki | 3/15 | Completed
 | Develop and train a neural network on the cleaning station dataset | Trained parameters of a neural network classifier, along with code and high quality documentation in a wiki | 3/18 | Completed
 | Integrate both with the rest of the system using ROS | Working ROS services which can be successfully interfaced with from the robot control computer, and thorough documentation for how to use them in a wiki page | 3/22 | Completed
Expected | Repeat for gripper cleaning | Same deliverables as for turntable cleaning station. | 4/7 | Completed (Deep Learning) Not Completed (Classical Method)
Max | Discuss with hardware team about collecting exudate data | Plan for collecting exudate ground truth data | 4/1 | Completed
 | Repeat for exudate volume estimation | Same deliverables as for previous two tasks. | 5/1 | Completed (Classical Method) Not Completed (Deep Learning)

## Slide 15: Dependencies
Dependency | Need | Contingency Plan | Planned Deadline | Hard Deadline | Status
Continued access to GPU | GPU for training neural network | I have a very capable personal GPU | Ongoing | Ongoing | Currently have access to the Diva computer and personal GPU
Cameras for collection of images of each task need to be mounted and integrated | To collect images for annotation | Use existing but less desirable views from the other existing cameras. | 3/14 | 3/22 (for remaining camera) | Completed
Hardware team | 300+ images of turntable cleaning station in progress with mosquitos. | Begin working on the image processing methods for the other tasks while waiting for additional training data collection. | 3/1 | 3/7 | Completed (slightly delayed)
Hardware team | 300+ images of gripper cleaning in progress with mosquitos. | Small Delay: Begin working “out of order” on the image annotation and image processing for the exudate estimation task Long Delay or Expected Failure: Change from the gripper cleaning task to one of the are many remaining vision tasks | 3/14 | 3/22 | Completed
Hardware team | Method for ground truth collection of mosquito exudate volume for training images | Abandon neural network approach and only do image processing for this task | 3/15 | 4/1 | Discussion completed however the neural network approach was abandoned due to time

## Slide 16: Management
Weekly meetings with the entire mosquito project team including hardware, control,
Additional meetings as needed with the vision team (approximately every other week)

## Slide 17: Future Work
There are many more vision tasks to be completed in the system
The tasks I implemented with classical methods have clear ways to be improved regarding ROIs
Deep learning methods could be trained on more information than just “clean” or “not clean”
All Images from JHU
except where noted

## Slide 18: Lessons Learned
Everything takes a very a longer than expected on a real system
Use the simplest methods possible at the outset

## Slide 19: References
[5] Sanaria, Sanaria.com.